## Slide 1: Signal for preemption request
Date: 2024-3-11
Authors:

## Slide 2: Background
To achieve low latency, preemption is a good approach.
Many contributions provide preemption solutions.
  In this contribution, we give considerations and proposals on the preemption request signal.

## Slide 3: Considerations on preemption request
STA(s) that are going to send preemption request after the ongoing transmitting PPDU, have got time and frequency synchronization with the PPDU.
  So the preemption request does not need to be a complete PPDU
  It is simpler to use a signal that is easy to be detected.
  It is recommended to use orthogonal sequences as the preemption request.
Take Zadoff Chu sequences for instance.
  1 symbol on 52 subcarriers can have 46[*] root ZC sequences which are orthogonal to each other.
  Each root ZC sequence can generate M ZC sequences by cyclic shift. The generated sequences are easy to be detected by autocorrelation with the root ZC sequence. M is 46 if the coverage radius is less than 100 meters.
  Different ZC sequences transmitted in same duration on the channel can be addressed simultaneously.
  A ZC sequence can be assigned to a STA that has potential LL traffic in association procedure.
The TX power for the PR can be determined.
  Path loss + target power to receive.
Notes: [*] The prime integer which is less than and closest to 52 is 47. So the number of the root ZC sequences is 46.

## Slide 4: UL Preemption in DL TXOP

## Slide 5: UL Preemption in UL TXOP of another STA

## Slide 6: Conclusion
In this contribution, we give considerations and proposals on the preemption request signal.
  ZC sequences are proposed for preemption request.

## Slide 7: Appendix
ZC sequence has been used as msg1 in LTE/NR for random access procedure
  The Base Station can simultaneously detect ZC sequence(s) transmitted in one timeslot on the channel and address the User Equipment(s) that sent the msg1(s), i.e. ZC sequence(s).
  It has been verified in real deployment.
The advantages of ZC sequence
  Good autocorrelation between a root ZC sequence and any ZC sequence it generates by cyclic shift (outstanding detection performance)
  Low cross correlation between one root ZC sequence and another root ZC sequence
  Constant envelop (low PAPR)
  Output of a ZC sequence through FFT is still a ZC sequence. (simple signal processing)
ZC sequence
  q is from 1 to NZC -1 for NZC -1 root sequences
  Each root sequence can generate NZC -1 sequences by cyclic shift.

## Slide 8: References
[1] 11-24-0103-01-00bn-txop-level-preemption-for-low-latency-application-in-802-11bn Juan Fang
[2] 11-23-1229-01-0uhr-preemption-for-low-latency-application-follow-up Juan Fang
[3] 11-23-1886-03-00bn-preemption-techniques-to-meet-low-latency-ll-targets Giovanni Chisci
[4] 11-24-0247-00-00bn-considerations-on-ll-preemption Woojin Ahn
[5] 11-24-0390-00-00bn-a-uniform-procedure-for-preemption Yunbo Li