## Slide 1: DRU Tone Plan for 11bn
Date: 2024-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Introduction
Motion has been passed in January IEEE meeting to support Distributed tone RU (DRU) for a UHR TB PPDU transmission
We have shared our thoughts on DRU tone plan design criteria, methodology and principle in [1]. Our studies show that 26-tone RU based DRU tone plan design can:
  Meet all the design target and achieve optimal power boost gain
  Preserve hierarchical structure as RRU
  Have better tone distribution pattern with either uniformly or near-uniformly distributed
  Make easier for channel smoothing and simpler for scheduling/signaling
In this contribution, we will share the detailed DRU tone plan design:
  DRU subcarrier indices table for BW20/40/80
  DRU power boost gains
  DRU tone distribution range
  DRU tone distribution pattern
  PAPR performance

## Slide 3: Recap: Design principles & methodologies of DRU Tone Plan [1]
Shengquan Hu, Mediatek Inc.
Slide 3
Minimize the number of tones per 1MHz to achieve the optimal power boost gain.
Preserve DRU hierarchical structure as regular RU (RRU) to allow simple signaling of DRUs
  The key for simplified signaling of DRU is to have a one-to-one mapping between the RRU and the DRU
  Can reuse the existing RU Allocation table
Allow scheduling and distributing different size DRUs without overlapped tones.
Do not introduce new RU sizes to avoid extra different data rates and extra parsing, interleaving and encoding.
Achieve uniform or near-uniform tone distribution pattern for simpler smoothing algorithms, easier phase tracking, ICI cancellation and improved diversity
Reserve enough edge tones (e.g. left-12 & right-11 tone for DRU on BW40/80, left-6 & right-5 for BW20)
Reserve enough DC tones (e.g. >= 5 DC tone for DRU on BW40/80, >=3 for BW20)
Tones distributed over non-OFDMA tone plan range
DRU subcarrier indices generation with PAPR reduction

## Slide 4: Recap: 26-tone RU Based DRU Design Method [1]
Shengquan Hu, Mediatek Inc.
Slide 4
RRU has the hierarchical structure, i.e. each larger size RU consists of corresponding smaller size RU tones
For an example, one RRU52 consists of tones from two RRU26s, one RRU106 consists of tones from two RRU52 or four RRU26 with two extra tones
This hierarchical structure makes RU assignment & scheduling much simpler
It would be desired for DRU to maintain the similar hierarchical structure to make DRU implementation more friendly, scheduling easier and signaling simpler
DRU will maintain the similar hierarchical structure as RRU
RRU Index in BW40

## Slide 5: DRU Tone Pattern and Power Boost Gains for BW20
Shengquan Hu, Mediatek Inc.
Slide 5
 | BW20 | 
 | #Tone/MHz | Power Boost (dB)
DRU26 | 2 | 8.13
DRU52 | 3 | 6.37
DRU106 | 6 | 3.56
The key for design 26-tone RU based DRU design method is to generate 26-tone DRU
To achieve the optimal gains and better distribution patterns, the tone separation distance/or repetition period Np=9 is used for DRU26 on distribution BW =20MHz
Using DRU26 as a basic building block, all other sized DRUs are built on DRU26 tone plan
  DRU52 is built from two DRU26
  DRU106 is built from four DRU26 or two DRU52 with 2 extra padding tones
  The extra padding tones are chosen to make tone distribution pattern in repeatable fashion and without causing tone-overlap issue
Np=9
Np=9
Np=9
Np=9
Np=9
Np=9
DRU106
DRU26
DRU52
(1 tone in one repetition period)
(2 tones in one repetition period)
(4 tones in one repetition period)

## Slide 6: DRU Distribution Range on 20MHz
Shengquan Hu, Mediatek Inc.
Slide 6
RRUs Span over 245 tones in range of [-122:-3,3:122] on BW20
-120
120
DRUs Span over 241 tones in range of [-120:-2,2:120]
all DRUs keep >= 3 DC tones
DRU within 242-tone region for each 20MHz subblock on BW80/160/320
This allows DRU distribution on 20MHz subblock for puncture mode or 20MHz only operating devices

## Slide 7: DRU Tone Plan for Distribution Bandwidth 20MHz
Shengquan Hu, Mediatek Inc.
Slide 7
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 
Keep the same number of DRUs as RRUs on BW20:
  9 DRU26; 4 DRU52D; 2 DRU106
Same format of indexing/ordering and tone plan table as RRU
Reuse existing RU Allocation table for trigger frame signaling

## Slide 8: Example Illustration of DRU Distribution Pattern: DRU on BW20
Shengquan Hu, Mediatek Inc.
Slide 8
26-tone DRUs are uniformly distributed over 20MHz
52-tone DRUs are near-uniformly distributed over 20MHz

## Slide 9: Example Illustration of DRU Distribution Pattern: DRU on BW20
Shengquan Hu, Mediatek Inc.
Slide 9
106-tone DRUs are near-uniformly distributed over 20MHz

## Slide 10: Example Illustration of DRU on BW20
Shengquan Hu, Mediatek Inc.
Slide 10
Different sized DRUs can be scheduled without tone-overlapping
The following illustrates 1st DRU26 (blue) and 2nd DRU52 (red) are assigned to two users

## Slide 11: PAPR Performance of DRU on BW20
Shengquan Hu, Mediatek Inc.
Slide 11
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
For PAPR reduction, tone spacing of all DRU26 are with an integer multiple of Np = 9
DRU26 achieves similar PAPR as RRU26 on BW20

## Slide 12: PAPR Performance of DRU on BW20
Shengquan Hu, Mediatek Inc.
Slide 12
For DRU52/106 on BW20, PAPR is about 0.5~0.7dB higher than RRU @90%- percentile

## Slide 13: DRU Tone Pattern and Power Boost Gains for BW40
Shengquan Hu, Mediatek Inc.
Slide 13
 | BW40 | 
 | #Tone/MHz | Power Boost (dB)
DRU26 | 1 | 11.14
DRU52 | 2 | 8.13
DRU106 | 3 | 6.37
DRU242 | 7 | 2.69
Tone separation distance/or repetition period Np=18 is used for DRU26 on distribution BW =40MHz
Using DRU26 as a basic building block, all other sized DRUs are built on DRU26 tone plan
  DRU52 is built from two DRU26
  DRU106 is built from four DRU26 or two DRU52 with 2 extra padding tones
  DRU242 is built from two DRU106 and one DRU26 with 4 extra padding tones
  The extra padding tones are chosen to make tone distribution pattern in repeatable fashion and without causing tone-overlap issue
Np=18
DRU106
DRU26
DRU52
(1 tone in one repetition period)
(2 tones in one repetition period)
(4 tones in one repetition period)
Np=18
Np=18
Np=18
DRU242
(9 tones in one repetition period)

## Slide 14: DRU Tone Plan for Distribution Bandwidth 40MHz
Shengquan Hu, Mediatek Inc.
Slide 14
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 40 MHz UHR TB PPDU |  |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  |  | 
26-tone DRU i=1:18 | DRU1 [-242:18:-26, 10:18:226] | DRU2 [-233:18:-17, 19:18:235] | DRU3 [-238:18:-22, 14:18:230] | DRU4 [-229:18:-13, 23:18:239] | DRU5 [-225:18:-9, 27:18:243] | DRU6 [-240:18:-24, 12:18:228]
 | DRU7 [-231:18:-15, 21:18:237] | DRU8 [-236:18:-20, 16:18:232] | DRU9 [-227:18:-11, 25:18:241] | DRU10 [-241:18:-25, 11:18:227] | DRU11 [-232:18:-16, 20:18:236] | DRU12 [-237:18:-21, 15:18:231]
 | DRU13 [-228:18:-12, 24:18:240] | DRU14 [-234:18:-18, 18:18:234] | DRU15 [-239:18:-23, 13:18:229] | DRU16 [-230:18:-14, 22:18:238] | DRU17 [-235:18:-19, 17:18:233] | DRU18 [-226:18:-10, 26:18:242]
52-tone DRU i=1:8 | DRU1 [-242:9:-17, 10:9:235] |  | DRU2 [-238:9:-13, 14:9:239] |  | DRU3 [-240:9:-15, 12:9:237] | 
 | DRU4 [-236:9:-11, 16:9:241] |  | DRU5 [-241:9:-16, 11:9:236] |  | DRU6 [-237:9:-12, 15:9:240] | 
 | DRU7 [-239:9:-14, 13:9:238] |  | DRU8 [-235:9:-10, 17:9:242] |  |  | 
106-tone DRU i=1:4 | DRU1 26-tone [DRU1~4], [-8,5] |  | DRU2 26-tone [DRU6~9], [-6,7] |  | DRU3 26-tone [DRU10~13], [-7,6] | 
 | DRU4 26-tone [DRU15~18], [-5,8] |  |  |  |  | 
242-tone DRU i=1:2 | DRU1 106-tone [DRU1~2],26-tone DRU5, [-244,-4,3,9] |  | DRU2 106-tone [DRU3~4],26-tone DRU14, [-243,-3,4,244] |  |  | 

## Slide 15: Example Illustration of DRU Distribution Pattern: DRU on BW40
Shengquan Hu, Mediatek Inc.
Slide 15
26-tone DRUs are perfect uniformly distributed over 40MHz
52-tone DRUs are perfect uniformly distributed over 40MHz

## Slide 16: Example Illustration of DRU Distribution Pattern: DRU on BW40
Shengquan Hu, Mediatek Inc.
Slide 16
106-tone DRUs are near-uniformly distributed on 40MHz

## Slide 17: PAPR Performance of DRU on BW40
Shengquan Hu, Mediatek Inc.
Slide 17
Apply same design methodology as DRU on BW20, for PAPR reduction, tone spacing of all DRU26 are with an integer multiple of Np = 18; tone spacing of all DRU52 are with an integer multiple of Np = 9;
DRU26 achieves similar PAPR as RRU26 on BW40; DRU52 achieves similar PAPR as RRU52 on BW40;

## Slide 18: PAPR Performance of DRU on BW40
Shengquan Hu, Mediatek Inc.
Slide 18
For DRU106/242 on BW20, PAPR is about 0.5~0.7dB higher than RRU @90% percentile

## Slide 19: DRU Tone Pattern and Power Boost Gains for BW80
Shengquan Hu, Mediatek Inc.
Slide 19
 | BW80 | 
 | #Tone/MHz | Power Boost (dB)
DRU52 | 1 | 11.14
DRU106 | 2 | 8.13
DRU242 | 4 | 5.12
DRU484 | 7 | 2.69
Tone separation distance/or repetition period Np=36 is used for DRU26 on distribution BW =80MHz
Using DRU26 as a basic building block, all other sized DRUs are built on DRU26 tone plan
  DRU52 is built from two DRU26
  DRU106 is built from four DRU26 or two DRU52 with 2 extra padding tones
  DRU242 is built from two DRU106 and one DRU26 with 4 extra padding tones
  DRU484 is built from two DRU242
  The extra padding tones are chosen to make tone distribution pattern in repeatable fashion and without causing tone-overlap issue
Make larger DRU242/484 perfect uniformly distributed instead of small DRU52/106, larger DRU will be benefit more better smoothing & lower PAPR from uniformly tone distribution
DRU106
DRU52
(2 tones in one repetition period)
(4 tones in one repetition period)
DRU242
(9 tones in one repetition period)
DRU484
(18 tones in one repetition period)
Np=36
Np=36
Np=36
Np=36

## Slide 20: DRU Tone Plan for Distribution Bandwidth 80MHz
Shengquan Hu, Mediatek Inc.
Slide 20
52-tone DRU i=1:16 | DRU1 [-483:36:-51, 17:36:449],[-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457],[-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453],[-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461],[-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455],[-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463],[-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451],[-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459],[-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450],[-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458],[-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454],[-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462],[-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456],[-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464],[-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452],[-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460],[-456:36:-24, 44:36:476]
106-tone DRU i=1:8 | DRU1 52-tone [DRU1~2], [-495, 485] | DRU2 52-tone [DRU3~4],[-491, 489] | DRU3 52-tone [DRU5~6],[-489, 491] | DRU4 52-tone [DRU7~8],[-493, 487]
 | DRU5 52-tone [DRU9~10],[-494, 486] | DRU6 52-tone [DRU11~12],[-490,490] | DRU7 52-tone [DRU13~14],[-488,492] | DRU8 52-tone [DRU15~16],[-492,488]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 21: Example Illustration of DRU Distribution Pattern: DRU on BW80
Shengquan Hu, Mediatek Inc.
Slide 21
52/106-tone DRUs are near-uniformly distributed on 80MHz

## Slide 22: PAPR Performance of DRU on BW80
Shengquan Hu, Mediatek Inc.
Slide 22
242-tone DRUs are perfect uniformly distributed on 80MHz

## Slide 23: PAPR Performance of DRU on BW80
Shengquan Hu, Mediatek Inc.
Slide 23
Apply same design methodology as DRU on BW20/40, for PAPR reduction, tone spacing of larger DRU242 are with an integer multiple of 4; tone spacing of all DRU484 are with an integer multiple of 2;
DRU242 achieves similar PAPR as RRU242 on BW80; DRU484 achieves similar PAPR as RRU484 on BW80;

## Slide 24: PAPR Performance of DRU on BW80
Shengquan Hu, Mediatek Inc.
Slide 24
For DRU52/106 on BW80, PAPR is about 0.5~0.7dB higher than RRU @90% percentile

## Slide 25: Summary
In this contribution, we have shared our detailed DRU tone plan design for distribution BW20/40/80 by using 26-tone RU based method, and conclude that our final detailed DRU tone plan:
  Meets all the design target and achieve optimal power boost gain
  Preserve hierarchical structure for simpler scheduling & signaling
  Better tone distribution pattern in repetitive fashion with either uniformly or near-uniformly distributed which makes channel smoothing easier and achieve better smoothing gains
  Tone indices generation with PAPR reduction

## Slide 26: Reference
Shengquan Hu, Mediatek Inc.
Slide 26
  [1]. 11-23-2021-01-00bn-principle-and-methodology-for-dru-tone-plan-design

## Slide 27: Straw Poll #1
Shengquan Hu, Mediatek Inc.
Slide 27
Do you agree to include the following text to the 11bn SFD?
  DRUs tone plan design for 11bn is 26-tone RU based DRU method (using 26-tone DRUs as basic building blocks)

## Slide 28: Straw Poll #2
Shengquan Hu, Mediatek Inc.
Slide 28
Do you agree to include the following text to the 11bn SFD?
  Data and pilot subcarrier indices for DRUs in a 20 MHz UHR PPDU are defined in following table:
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 

## Slide 29: Straw Poll #3
Shengquan Hu, Mediatek Inc.
Slide 29
Do you agree to include the following text to the 11bn SFD?
  Data and pilot subcarrier indices for DRUs in a 40 MHz UHR PPDU are defined in following table:
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 40 MHz UHR TB PPDU |  |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  |  | 
26-tone DRU i=1:18 | DRU1 [-242:18:-26, 10:18:226] | DRU2 [-233:18:-17, 19:18:235] | DRU3 [-238:18:-22, 14:18:230] | DRU4 [-229:18:-13, 23:18:239] | DRU5 [-225:18:-9, 27:18:243] | DRU6 [-240:18:-24, 12:18:228]
 | DRU7 [-231:18:-15, 21:18:237] | DRU8 [-236:18:-20, 16:18:232] | DRU9 [-227:18:-11, 25:18:241] | DRU10 [-241:18:-25, 11:18:227] | DRU11 [-232:18:-16, 20:18:236] | DRU12 [-237:18:-21, 15:18:231]
 | DRU13 [-228:18:-12, 24:18:240] | DRU14 [-234:18:-18, 18:18:234] | DRU15 [-239:18:-23, 13:18:229] | DRU16 [-230:18:-14, 22:18:238] | DRU17 [-235:18:-19, 17:18:233] | DRU18 [-226:18:-10, 26:18:242]
52-tone DRU i=1:8 | DRU1 [-242:9:-17, 10:9:235] |  | DRU2 [-238:9:-13, 14:9:239] |  | DRU3 [-240:9:-15, 12:9:237] | 
 | DRU4 [-236:9:-11, 16:9:241] |  | DRU5 [-241:9:-16, 11:9:236] |  | DRU6 [-237:9:-12, 15:9:240] | 
 | DRU7 [-239:9:-14, 13:9:238] |  | DRU8 [-235:9:-10, 17:9:242] |  |  | 
106-tone DRU i=1:4 | DRU1 26-tone [DRU1~4], [-8,5] |  | DRU2 26-tone [DRU6~9], [-6,7] |  | DRU3 26-tone [DRU10~13], [-7,6] | 
 | DRU4 26-tone [DRU15~18], [-5,8] |  |  |  |  | 
242-tone DRU i=1:2 | DRU1 106-tone [DRU1~2],26-tone DRU5, [-244,-4,3,9] |  | DRU2 106-tone [DRU3~4],26-tone DRU14, [-243,-3,4,244] |  |  | 

## Slide 30: Straw Poll #4
Shengquan Hu, Mediatek Inc.
Slide 30
Do you agree to include the following text to the 11bn SFD?
  Data and pilot subcarrier indices for DRUs in an 80 MHz UHR PPDU are defined in following table:
52-tone DRU i=1:16 | DRU1 [-483:36:-51, 17:36:449],[-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457],[-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453],[-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461],[-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455],[-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463],[-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451],[-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459],[-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450],[-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458],[-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454],[-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462],[-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456],[-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464],[-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452],[-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460],[-456:36:-24, 44:36:476]
106-tone DRU i=1:8 | DRU1 52-tone [DRU1~2], [-495, 485] | DRU2 52-tone [DRU3~4],[-491, 489] | DRU3 52-tone [DRU5~6],[-489, 491] | DRU4 52-tone [DRU7~8],[-493, 487]
 | DRU5 52-tone [DRU9~10],[-494, 486] | DRU6 52-tone [DRU11~12],[-490,490] | DRU7 52-tone [DRU13~14],[-488,492] | DRU8 52-tone [DRU15~16],[-492,488]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range