## Slide 1: Unequal Modulation Patterns and new MCS
Date: 2024-03-08
Authors:

## Slide 2: Introduction
Unequal modulation has been proposed as a promising technology for UHR to enhance MIMO RvR [1~3].
In this contribution, we will further
  evaluate the useful unequal modulation combinations, and
  investigate the benefits of adding several new MCSs.

## Slide 3: UEQM QAM levels
UQAM examples:
  E.g. 2ss, [256-QAM, 64-QAM]
  E.g. 4ss, [1K-QAM, 1K-QAM, 256-QAM, 64-QAM]
Existing MCS has 7 QAM level
  Limit the maximum Nss for UEQM to 4ss
  Potentially has 100+ options for 4ss
Need to reduce the combinations to balance gain and complexity

## Slide 4: 2x2: UEQM QAM Level
1 QAM level diff: achieves most gains, but show losses across entire SNR range
2 QAM level diff: achieves all gains with minor difference

## Slide 5: 4x4: UEQM QAM Level
Both 3ss and 4ss EQM/UEQM are considered at each SNR points
Limit to 2 QAM level difference achieves most of the gains, with limited impact in middle SNR region

## Slide 6: UEQM QAM Selection
Balancing between gain and complexity, 2-level QAM difference is sweet spot.
For up to 4ss, still up to 9 combinations for each MCS.
Further mode reduction to choose the most useful QAM combinations:
  Per-channel PER simulation and per-channel per-SNR point optimal rate selection, i.e. manual rate adaptation
  Rate selection criteria
    UEQM is selected if >=4% higher goodput than existing MCS
      Smallest rate difference between adjacent MCSs is 8% (MCS11 to MCS12)
      Avoid the biased count at high-SNR points
    Rank each UEQM QAM pattern by the occurrence count
      across all configurations, channels, SNR points

## Slide 7: 4x4 UEQM Rank
4ss
3ss
M1 | M2 | M2 | M4 | %
0 | 0 | -1 | -2 | 21.05
0 | 0 | 0 | -2 | 15.79
0 | -1 | -2 | -2 | 15.79
0 | 0 | -1 | -1 | 10.53
0 | 0 | -2 | -2 | 10.53
0 | 0 | 0 | -1 | 10.53
0 | 0 | 0 | 0 | 10.53
0 | -1 | -1 | -2 | 5.26
M1 | M2 | M2 | %
0 | 0 | -2 | 25.93
0 | -1 | -2 | 22.22
0 | 0 | -1 | 18.52
0 | -1 | -1 | 11.11
0 | -2 | -2 | 11.11
0 | 0 | 0 | 11.11
DNLos
M1 | M2 | M2 | M4 | %
0 | 0 | -1 | -2 | 20
0 | 0 | 0 | -2 | 14.29
0 | 0 | -1 | -1 | 14.29
0 | -1 | -2 | -2 | 14.29
0 | 0 | -2 | -2 | 11.43
0 | 0 | 0 | -1 | 11.43
0 | -1 | -1 | -2 | 11.43
0 | -1 | -1 | -1 | 2.86
M1 | M2 | M2 | %
0 | -1 | -2 | 25.93
0 | -1 | -1 | 25.93
0 | 0 | -1 | 18.52
0 | 0 | -2 | 14.81
0 | -2 | -2 | 14.81
Blos

## Slide 8: 4x4 UEQM Choices
3ss:
4ss
M1 | M2 | M3
0 | 0 | -1
0 | 0 | -2
0 | -1 | -2
 | M1 | M2 | M3 | M4
 | 0 | 0 | -1 | -2
 | 0 | 0 | 0 | -2
Option 1 | 0 | -1 | -1 | -2
Option 2 | 0 | -1 | -2 | -2
Option 3 | 0 | 0 | -1 | -1
Option 4 | 0 | 0 | 0 | -1

## Slide 9: DNLos 4x4 Goodput Gain
[0 0 0 -1] shows good benefits for the region that SNR saturates for certain QAM
Considering Tx power difference between MCSs, the pattern can help in more practical use cases.

## Slide 10: BLos 4x4 Goodput Gain
[0 0 0 -1] shows good benefits for the region that SNR saturates for certain QAM
Considering Tx power difference between MCSs, the pattern can help in more practical use cases.

## Slide 11: UEQM QAM Combinations
Propose UHR UEQM to define the following patterns
  Note:
    M is the modulation order index
    M-1 refers to the modulation that is one order lower than M
    M-2 refers to the modulation that is two orders lower than M
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2

## Slide 12: Thoughts on New MCS
Finer MCSs was discussed during 11be generation [4]
Revisit for UHR for RvR enhancement, especially for Nss=1 transmissions
New MCS definition can also help UEQM support
  E.g. there is only one QAM (64 QAM) with rate 2/3

## Slide 13: New MCS Selection
Per-channel PER simulation and per-channel per-SNR point optimal rate selection, i.e. manual rate adaptation
New rate selection criteria
  New rate is selected if >=4% higher goodput than existing MCS
    Smallest rate difference between adjacent MCSs is 8% (MCS11 to MCS12)
    Avoid the biased count at high-SNR points
  Rank each new rate by the occurrence count
    across all configurations, channels, SNR points

## Slide 14: 1x1-1ss AWGN
M | CR | Percentage %
16 QAM | 5/6 | 29.46
256 QAM | 2/3 | 14.5
16 QAM | 2/3 | 11.79
BPSK | 5/6 | 11.79
QPSK | 2/3 | 11.67
QPSK | 5/6 | 9.07
4K QAM | ½ | 5.89
BPSK | 2/3 | 5.83

## Slide 15: 2x1-1ss
M | CR | Percentage %
16 QAM | 5/6 | 26.3
256 QAM | 2/3 | 22.18
16 QAM | 2/3 | 18.22
QPSK | 2/3 | 17.3
BPSK | 2/3 | 9.45
QPSK | 5/6 | 6.55
M | CR | Percentage %
16 QAM | 5/6 | 27.36
256 QAM | 2/3 | 20.9
16 QAM | 2/3 | 19.07
QPSK | 2/3 | 15.65
BPSK | 2/3 | 9.88
QPSK | 5/6 | 5.32
4K QAM | 1/2 | 1.82

## Slide 16: 2x2-1ss
M | CR | Percentage %
16 QAM | 5/6 | 28.38
256 QAM | 2/3 | 20.98
16 QAM | 2/3 | 16.17
QPSK | 2/3 | 15.1
QPSK | 5/6 | 11.52
BPSK | 2/3 | 7.63
4K QAM | 1/2 | 0.23
M | CR | Percentage %
16 QAM | 5/6 | 28.64
256 QAM | 2/3 | 20.08
16 QAM | 2/3 | 18.18
QPSK | 2/3 | 14.17
BPSK | 2/3 | 9.09
QPSK | 5/6 | 8.79
4K QAM | 1/2 | 1..06

## Slide 17: New Rate Selection
Top four new MCSs benefits Nss=1 RvR the most.
Suggest to add.
Modulation | CR | %
16 QAM | 5/6 | 29.57
256 QAM | 2/3 | 21.76
16 QAM | 2/3 | 17.41
QPSK | 2/3 | 15.49
BPSK | 2/3 | 5.15
QPSK | 5/6 | 5.37
BPSK | 5/6 | 3.05
4K QAM | ½ | 2.15
64 QAM | 1/2 | 0.03

## Slide 18: Summary
Suggest to limit UEQM QAM combination
Suggest to add four new MCS
  QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2

## Slide 19: Reference
[1] 11-24/16, uhr-mimo-rvr-enhancement-with-unequal-modulation
[2] 11-24/0113, unequal-modulation-in-mimo-txbf-in-11bn
[3] 11-24/0117, improved-tx-beamforming-with-ueqm
[4] 11-20/0083, impacts-of-mcs-set-expansion-on-11be-link-adaptation

## Slide 20: SP
Do you support to include in the 11bn SFD:
  Define unequal modulation over different spatial streams?

## Slide 21: SP
Do you agree to add the following text into 11bn SFD?
11bn defines unequal modulation with the same coding rate for beamformed multi-stream transmission to single STA in full bandwidth or on a RU/MRU in OFDMA.

## Slide 22: SP
Do you agree that the maximum QAM level difference for UEQM is 2?

## Slide 23: SP
Do you agree to UEQM QAM combination for Nss=2 is limited to two as below?
[M M-1]
[M, M-2]
Note:
  M is the modulation order index
  M-1 refers to the modulation that is one order lower than M
  M-2 refers to the modulation that is two orders lower than M

## Slide 24: SP
Do you agree to UEQM QAM combination for Nss=3 is limited to three as below?
[M, M, M-1]
[M, M, M-2]
[M, M-1, M-2]
Note:
  M is the modulation order index
  M-1 refers to the modulation that is one order lower than M
  M-2 refers to the modulation that is two orders lower than M

## Slide 25: SP
Do you agree to UEQM QAM combination for Nss=4 is limited to three as below?
[M, M, M, M-1],
[M, M, M, M-2],
[M, M, M-1, M-2]
Note:
  M is the modulation order index
  M-1 refers to the modulation that is one order lower than M
  M-2 refers to the modulation that is two orders lower than M

## Slide 26: SP
Do you agree to define UEQM QAM combination as below?
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2

## Slide 27: Appendix

## Slide 28: Simulations
80MHz, DNLos/BLos channels
4x EHT-LTF, LDPC code
Tx: SVD Tx BF
Rx: Linear receiver
Modulations: BPSK to 4K-QAM
  Unequal modulation: Up to 3 QAM gap between two streams
  Coding [1/2, 2/3, 3/4, 5/6]
  Equal modulation with new rates: all QAM + all CR (28 rates)
Comparison:
  Equal modulation (EQM)
  Equal modulation with new rates (EQM-new)
  Unequal modulation (UEQM)

## Slide 29: 4x2 UEQM QAM level
1-level QAM: achieves most gains, but show losses in several SNR segments
2-level QAM: achieves all gains with minor difference

## Slide 30: BLos 4x4 QAM Option RvR

## Slide 31: DNLos 4x4 QAM Option RvR

## Slide 32: Consideration on Tx Power Difference
Tx power backoff is needed for high QAMs to meet EVM
  Some regions experience SNR saturation for lower QAM
  More use cases to choose [M M M M-1] pattern
4K QAM
1K QAM

## Slide 33: DNLos 4x4 without 4K-QAM

## Slide 34: BLos 4x4 without 4K-QAM