## Slide 1: Low power listening mode for clients
Date: 2024-03-01
Authors:

## Slide 2: Background
Low power listen mode was proposed by [1], and this concept have gradually received much support.
  Listening mode contributes more than half of the power consumption in testing
  Introducing a 20MHz LPL chain can brings the power consumption down to certain level, such as 10%-20% relative to the regular power consumptions in RF
MU-RTS
CTS
PPDU
BA
Low power listening mode
1 ss, 20 MHz, low MCS
Regular TX/RX mode
Up to 8 ss, 320 MHz, 4K QAM
Low power listening mode
1 ss, 20 MHz, low MCS

## Slide 3: Background
Reference [2] and [3] continue to develop this low power listen mode and provide more details
  Extra FCS with padding for transition delay between the low power listen mode and the regular TX/RX mode
  The low power listen mode is at link level
  Mandate inclusion of initial control frame (ICF) at the beginning of the TXOP
In this contribution, we will provide our thought about this feature from the following aspects
  TXOP Sequence in regular TX/RX mode
  Extra FCS design

## Slide 4: TXOP Sequence in regular TX/RX mode
According to reference [4], more than 60% DL packets and almost 90% UL packets are less 100 bytes in enterprise scenarios. Similar tendency can also be seen in other scenarios
For packets of small size, it doesn’t require more spatial streams, large bandwidth and high MCS.
We propose 20 MHz Data transmission in low power listening mode
  20 MHz Data transmission is in non-HT PPDU format with 1 spatial stream and low MCS
  Mandate inclusion of initial control frame (ICF) at the beginning of the TXOP for transmission with more than 20 MHz bandwidth
  Many overheads, especially for large transition delay, are saved
MU-RTS
CTS
PPDU
BA
Low power listening mode
1 ss, 20 MHz, low MCS
Regular TX/RX mode
Up to 8 ss, 320 MHz, 4K QAM
Low power listening mode
1 ss, 20 MHz, low MCS
20 MHz non-HT PPDU
Ack

## Slide 5: TXOP Sequence in regular TX/RX mode
MU-RTS frame should be transmitted in non-HT duplicated format and its bandwidth may be larger than 20 MHz.
At the client side, it only receives 20 MHz MU-RTS since it is in low power listening mode. However, the response frame may also be larger than 20MHz, depending on the implementation and CCA results
  Padding added in MU-RTS provides enough transition delay for client
For the TXOP Sequence, the following rule should be obeyed
  The PPDU bandwidth should be narrower or equal to its preceding PPDU bandwidth in the same TXOP
Rules are defined in EMLSR/EMLMR for switching back to the listening operation can also be reused for this TXOP Sequence termination in regular TX/RX mode
  We are also open to other methods for termination

## Slide 6: Extra FCS design
Extra FCS design involve the following aspects
  The size of extra FCS
  The container of extra FCS
  The location identification of extra FCS
  For the size of FCS, we prefer to keep the same size as current FCS, which is 4 bytes
  Keep the same size to avoid the asymmetry issue on false alarm and missing rate with respect to legacy devices
  On the other hand, there are other two candidates from the aspect of reusing current 802.11 CRC engines
  16-bit CRC (e.g., SIG field protection of DSS PHY (15.3.3.7 (PHY CRC field), which is used to validate 32 bits PHY signaling
  8-bit CRC (e.g., A-MPDU delimiter protection (9.7.2 (MPDU delimiter CRC field), which obviously, which is used to validate 16 bits in MPDU delimiter.

## Slide 7: Extra FCS design
To keep the same structure of the trigger frame, we also prefer to have User Info field to include extra FCS as in [3], but the number of User Info field is only one
The Use Info field that includes extra FCS doesn’t starts a special AID, but extra FCS. The remaining bits in this User Info field are reserved.
Compared to special AID for identifying the location of extra FCS, we propose an earlier indication for it
  Simplify parsing action at the client side and also help quickly identify the location of extra FCS
Frame Control
Duration
RA
TA
Common Info
Special User Info
User Info 1
User Info 2
Extra FCS
Padding User Info…
FCS
Example for initial control frame

## Slide 8: Extra FCS design
An earlier indication for identifying the location of extra FCS
  For example, reuse UL Length field which is reserved in MU-RTS
  Regarding padding between extra FCS and FCS, it should also start with AID of 4095.

## Slide 9: Summary
In this contribution, we propose the following aspects for low power listening mode at the clients side.
  20 MHz non-HT PPDU should be transmitted in low lower listening mode, not regular TX/RX mode
  An earlier indication in Common User info field for location identification of extra FCS of 4 bytes
  The Use Info field that includes extra FCS doesn’t starts with a special AID, but extra FCS. The remaining bits in this User Info field are reserved.

## Slide 10: References
[1] 11-22-1414-01-0uhr-low-power-listening-mode
[2] 11-23-1875-01-00bn-power-save-proposal-for-non-ap-mobile-ap
[3] 11-23-2003-01-00bn-client-power-save
[4] 11-14-0874-00-00ax-unified-traffic-model-on-enterprise-scenario