## Slide 1: Discussion on Control Frame and MAC Header Protection
Date: 2024-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Many presentations in the UHR SG and 11bn discuss secure control frame and MAC header protection; [1-9]
The target of designs is to solve the issues below:
  Data stream disruption
  Denial of service
  Power drainage
  Resource wastage
Before we dive into the design, we need to think about the questions below
  Are these real issues to be solved?
  How to deal with other control frames besides TF, BAR and BA?
  Can we achieve the target when secure control frame and MAC header protection are used?
  Can an attack spread?
  What do we finally get?

## Slide 3: Are These Real Issues?
I don’t think all of these are real issues that the group needs to address;
Lack of motivation for an attacker to initiate an attack;
  Because the victim’s data is encrypted, the attacker can not get the date;
  The attacker needs to spend a lot of effort to initiate the attack, and also waste the attacker’s time and power;
No data to show whether and how often these issues happen in the real world;
Practice is the best proof
  The unprotected control frames are used since the beginning of the Wi-Fi eco-system, which has already been used for 20 + years;
  The Trigger frame that was introduced in 11ax, will be used for 10+ years when Wi-Fi 8 be published;
  The Wi-Fi eco-system is widely used everyday in every country/area in the world.

## Slide 4: Issues for Other Control Frames?
The presentations mainly discuss issues for the control frames below
  Trigger frame
  BAR frame
  BA frame
Issue for other control frames are mentioned in [4];
  RTS frame
  PS-Poll frame
  Ack frame
More issues for other control frames may exist
  Ack: All individual management frames (except Action No Ack) will solicit an Ack frame, the attacker may respond with a fake Ack frame to cheat an AP
  CF-End: the attacker may abuse a CF-End frame to terminate a TXOP holder’s TXOP
  CTS-to-self: the attacker can send a CTS-to-self without backoff, to occupy the medium through a virtual CCA mechanism

## Slide 5: Can We Achieve The Target?
I don’t think so;
Please remember that the purpose of the attacker is one or more of:
  Data stream disruption
  Denial of service
  Power drainage
  Resource wastage
The attacker can achieve the purpose easily, even totally following all the rules;
  Always transmit broadcast frames, so that all the STAs need to receive the packets all of the time, and will drain all STA’s power quickly;
  Always contend the medium by using the minimum CW, and occupy the channel through CTS-to-self. The result is, denial of service for all STAs.

## Slide 6: Can The Attacks spread?
No, the attacks are very difficult to spread;
The key requirements for such attacks are
  Physical approaches to the victims, typically within 10 meters
  Constant power supply to maintain the attack
I can not imagine how the attacker can install such equipment in the victim's home or office;
Even if the attacker can make it, the attack equipment can be easily located since it is in a very limited physical area and needs to transmit wireless signals frequently.

## Slide 7: What Have We Finally Got?
A similar example is that: installation of traffic lights at the road crossing will help to reduce traffic accidents. So the suggestion is to install traffic lights at each country cross road;
Obviously it is not necessary. The traffic lights on the country roads will significantly add cost, and obstruct the traffic;
If we do control frame protection and MAC header protection, the customer will have same secure experience (or negligible improvement) as before, but will need to pay more for the higher cost of the Wi-Fi chips;
The low cost and high efficiency are the big benefits of the Wi-Fi eco-system, we are weakening these benefits if we go in this direction.

## Slide 8: Summary
The control frame protection and MAC header protection are not for real issues that need to be solved;
The target of avoiding data disruption and power drain cannot be achieved through secure control frame and MAC header protection;
Even such attacks happen in some rare circumstances, the attacks are difficult to spread;
We will add cost and burden for the Wi-Fi eco-system, but with negligible improvements in security, if we go in this direction.

## Slide 9: References
[1] 11-23-0286 Trigger Frame Protection
[2] 11-23-0312 Thoughts on Secure Control frames
[3] 11-23-0352 Enhanced Security Discussion
[4] 11-23-1102 security enhancement follow up
[5] 11-23-1914 Enhanced Security Consideration in UHR
[6] 11-23-1995 Trigger BA and BAR protection
[7] 11-23-0356 MAC Header Protection
[8] 11-23-1997 MAC Header Protection
[9] 11-23-1888 MAC Header protection- follow up