## Slide 1: In-device Coexistence Follow Up: Control Frame
Date: 2024-03-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Initial (Dynamic) Control Information for Various Purpose
In a TXOP, the TXOP holder can notify the BW, MCS, Nss that will be used by the low-capacity listening TXOP responder within the TXOP for the enhanced power save (low-capacity mode listening to high-capacity mode for frame exchange).
  The TXOP responder can switch to the high-capacity mode from the low-capacity listening mode and stay in high-capacity mode until the end of the TXOP.
In a TXOP, the TXOP responder can notify the available BW, available time, unavailable time because of the in-device non-WiFi radio activity (for in-device radio coexistence).
  The available time and unavailable time have different responding time requirements.
A STA/AP may announce its available BW, available time, unavailable time because of the in-device non-WiFi radio activity without soliciting.
A STA and AP may negotiate the Tx/Rx parameters for the TXOP or SP.
The TXOP responder may notify the reason why the frames in A-MPDU are not received correctly so that the TXOP holder will not drop the Tx MCS wrongly.

## Slide 3: Support of Different Features
A STA/AP can announce whether it supports the enhanced power save feature, in-device coexistence feature, and per TXOP Tx/Rx parameter negotiation separately.

## Slide 4: Initial (Dynamic) Control Information Organization
The various dynamic control information can be organized as tuples of Control ID, Length, Control Content.
  An initial soliciting control frame and initial responding control frame can include one or more of them.

## Slide 5: Various MAC Features under Dynamic Control Information Exchange
The EMLSR mode needs to be supported under enhanced power save, in-device radio coexistence.
The TXOP protection, dynamic BW negotiation needs to be supported under enhanced power save, in-device radio coexistence.
  The variable length responding frame needs to be considered.
  The NAV timer resetting by the neighbor STAs/APs when no PPDU following the first initial control frame exchange that needs the CCA checking needs to be supported.
The MU operation needs to be supported under enhanced power save, in-device radio coexistence.

## Slide 6: Per User Control Information and Control Information for All Addressed/Associated STAs
The broadcast Control frame needs to support the initial control information for single addressed STA, and/or for all addressed/associated STAs.
  Example of the initial control information for a specific addressed STA: Tx/Rx parameters for the user in the TXOP
  Example for of the initial control information for a specific addressed STA: the unavailable future time period.

## Slide 7: Initiator of Dynamic Control Frame Exchange
The initiator can be non-AP STA or AP.
The responding PPDU is TB PPDU if multiple STAs send the responding frames with the different content.
  The RUs of two responding STAs can’t be allocated in one 20MHz channel if available time is reported through Duration field unless the duration information in PHY header is set to UNSPECIFIED.
The responding PPDU can be SU PPDU if single responder transmit the responding frame.
  At least the AP as the responder needs to transmit SU PPDU.

## Slide 8: Initial Control Soliciting and Responding Frame
Frame exchange initiated by an AP
  Option 1: BSRP Trigger and Multi-STA BA.
  Option 2: BSRP Trigger and QoS Null
  Option 3: New Trigger variant and new control responding frame.
  The frame exchange sequence needs to be the initial frame exchange for EMLR, EMLMR.
  The frame exchange sequence needs to support the enabling of the responding STA’s CCA checking and TXOP protection.
  The initiating broadcast frame needs to provide the per STA dynamic control information and dynamic control information for all addressed/associated STAs.

## Slide 9: Initial Control Soliciting and Responding Frame
Frame exchange initiated by a non-AP STA
  Option 1: BAR and Multi-STA BA when soliciting device is a non-AP STA.
  Option 2: BSRP Trigger and Multi-STA BA.
  Option 3: New Trigger variant and new control responding frame
  The frame exchange sequence needs to support the enabling of responding STAs CCA checking and TXOP protection.
  The frame body and frame header if used can only carry the dynamic control information.

## Slide 10: Trigger Frame Special Consideration
In Trigger frame, the various types of information for all the addressed STA(s) of the Trigger frame, e.g. unavailable time (start time and the time period when the transmitter is not available), is carried in one or multiple User Info fields with the specific AID value (e.g. 2006 or 2009) in AID12 field of the User Info field.
  Such User Info has the same length as the Special User Info field where the Trigger Dependent User Info if exists is reserved.
  A combination of control ID + Length + control content is used to carry one of the various types of the information. One or multiple control ID + Length + control content can be carried in the User Info field(s) with the specific AID value in AID12 field.
In Trigger frame, the information for a user (e.g. Tx/Rx parameters for the user in the TXOP) is carried in an additional User field following the User Info field for the User.
  The additional User field is another User Info field whose AID12 field has a specific value (AID 2005 as an example) or the User’s AID value.
  A combination of control ID + Length + control content is used to carry one of the various types of the information.

## Slide 11: BAR and Multi-STA BA Special Consideration
Common for BAR and Multi-STA BA:
  The frame may not carry the information for soliciting BA bitmap, and BA bitmap and Ack respectively.
Specific for Multi-STA BA:
  A Multi-STA BA should not use multiple Per AID TID Info fields instead of one Per AID TID Info field if the two cases provide the same aggregated BA bitmap size.
  A Multi-STA BA should not use a Per AID TID Info field if another Per AID TID Info field with smaller BA bitmap size can carry all the required dynamic control information.

## Slide 12: QoS Null Consideration
The HE Control field in QoS Null can be variable length.

## Slide 13: Summary
The possible initial control soliciting frame and initial responding frame transmitted by AP and STA for coexistence, enhanced power save, and the other features are discussed.
  The format to carry various dynamic control information is discussed.
Whichever of the frames are used, the following need to supported besides carrying the various dynamic control information:
  MU support.
  EMLSR/EMLMR support (the new initial frame exchange trigger EMLSR STA’s radio switch).
  TXOP protection.
The special requirement if BAR, Multi-STA BA, or QoS Null is selected is also discussed.