## Slide 1: Unequal Modulation in MIMO TxBF in 11bn
Date: 2024-03-09
Authors:
Name | Affiliations | email
Alice Chen | Qualcomm | alicel@qti.qualcomm.com
Bin Tian |  | btian@qti.qualcomm.com
Sameer Vermani |  | svverman@qti.qualcomm.com
Akansh Jain |  | akanjain@qti.qualcomm.com

## Slide 2: Introduction
Two design flavors were considered to deal with the channel quality imbalance among the eigen modes in MIMO beamformed channel,
  Unequal MCS among spatial streams [1-2, 8]
  Unequal modulation with joint coding across streams [3-7, 9-10]
Unequal modulation is more promising than unequal MCS due to
  Better performance [4]
    It was shown in [4] that due to joint encoding among 2 spatial streams, unequal QAM outperformed unequal MCS after 1st stream SNR saturates
  Lower implementation complexity [5, 8]
In this presentation, we jointly discuss unequal QAM and new MCS
  Quantify the contribution of each to the RvR improvement
  Propose unequal QAM design and new MCS for 11bn

## Slide 3: Unequal QAM And New MCS
Gain of unequal modulation comes from the following two sources
    Providing intermediate data rates for the multi-stream case
    Matching modulation to SINRs of different spatial streams
  Need to understand how much of that gain comes from each of the two sources
Need to jointly consider unequal QAM and adding new MCS
  With existing MCS only, unequal QAM combinations for each code rate are limited and none for rate 2/3
  In [5], it was shown that with existing MCS only, unequal QAM harvest majority of gain. There is still room for RvR improvement if new MCS(s) may be added to the MCS set
Mod \ Coderate | 1/2 | 2/3 | 3/4 | 5/6
BPSK | MCS 0 |  |  | 
QPSK | MCS 1 |  | MCS 2 | 
16QAM | MCS 3 |  | MCS 4 | 
64QAM |  | MCS 5 | MCS 6 | MCS 7
256QAM |  |  | MCS 8 | MCS 9
1K QAM |  |  | MCS 10 | MCS 11
4K QAM |  |  | MCS 12 | MCS 13

## Slide 4: Simulation Setup
20MHz, 2x2x2ss
DNLoS & BLoS
TxBF (using SVD) with equal power allocation to all spatial streams
Linear receiver
Genie per channel rate adaptation
Candidate code rates: 1/2, 2/3, 3/4, 5/6
Candidate QAM: from BPSK to 1kQAM
Different schemes being compared
  Equal MCS with existing MCS
  Equal MCS with intermediate MCS (any code rate & QAM)
  Optimum Unequal QAM (any QAM combination for a code rate)
  Unequal QAM with existing MCS (both streams use existing MCS from MCS0-11 and share same code rate)

## Slide 5: Unequal QAM Vs Intermediate MCS 2x2x2ss
Compared to equal MCS with intermediate MCS, optimum unequal QAM has an additional gain (up to 1.1dB)
  Gain comes from matching modulation to SINRs of different spatial streams
Unequal QAM brings significant gain (up to 2.2dB) over wide range of SNR
  With existing MCS only, unequal QAM harvest majority of gain

## Slide 6: New MCS Study
New MCS may be useful in the following to improve RvR
  1ss transmission
  Unequal QAM in MIMO
Spectral efficiency |  |  |  | 
Mod \ Coderate | 1/2 | 2/3 | 3/4 | 5/6
BPSK | 0.5000 | 0.6667 | 0.7500 | 0.8333
QPSK | 1.0000 | 1.3333 | 1.5000 | 1.6667
16QAM | 2.0000 | 2.6667 | 3.0000 | 3.3333
64QAM | 3.0000 | 4.0000 | 4.5000 | 5.0000
256QAM | 4.0000 | 5.3333 | 6.0000 | 6.6667
1K QAM | 5.0000 | 6.6667 | 7.5000 | 8.3333
4K QAM | 6.0000 | 8.0000 | 9.0000 | 10.0000
All MCS (Index in SE non-decreasing order) |  |  |  | 
Mod \ Coderate | 1/2 | 2/3 | 3/4 | 5/6
BPSK | MCS 0 | MCS0.1 | MCS0.2 | MCS0.3
QPSK | MCS 1 | MCS1.1 | MCS 2 | MCS2.1
16QAM | MCS 3 | MCS3.1 | MCS 4 | MCS4.2
64QAM | MCS4.1 | MCS 5 | MCS 6 | MCS 7
256QAM | MCS5.1 | MCS7.2 | MCS 8 | MCS 9
1K QAM | MCS7.1 | MCS9.1 | MCS 10 | MCS 11
4K QAM | MCS8.1 | MCS10.1 | MCS 12 | MCS 13
We use the following guidelines for introducing new MCS
  MCS that improve RvR in 1ss or unequal QAM
  MCS with SNR at 10% PER not very close to those of existing MCS to avoid rate adaptation difficulty
  MCS must have a different spectral efficiency compared to existing ones
Define the MCS indices according to spectral efficiency non-decreasing order

## Slide 7: New MCS Simulation
1ss Simulation setup
  20MHz, DNLoS
  MIMO config
    2x2x1ss TxBF
    2x2x1ss OL
    4x2x1ss TxBF
  Equal MCS and equal power allocation to all spatial streams
  Perfect CSI feedback in TxBF
  Ideal CHEST
  Candidate code rates: 1/2, 2/3, 3/4, 5/6
  Candidate QAM: from BPSK to 1kQAM
  SNR points are simulated with 1dB granularity
See later slides for the unequal QAM simulation with recommended new MCS

## Slide 8: New MCS Recommendation
Goodput plots are in Appendix
Here we summarize the MCS that provide goodput gain in the tables
We recommend to adopt MCS1.1, MCS3.1, MCS4.2 and MCS7.
  They are useful in 1ss scenarios
  In subsequent slides, we show that these MCS are useful for unequal QAM as well
20MHz, 2x2x1ss, DNLoS, TxBF |  |  |  |  | 15.5
Nss | MCS | SNR_Start (dB) | SNR_End (dB) | Gain_Min (%) | Gain_Max (%)
1ss | 1.1 | -0.5 | 0.5 | 2.4 | 10.9
 | 3.1 | 5.5 | 6.5 | 6.8 | 14.3
 | 4.2 | 9.5 | 10.5 | 1.2 | 4.8
 | 7.2 | 16.5 | 17.5 | 3.1 | 4.1
20MHz, 2x2x1ss, DNLoS, OL |  |  |  |  | 4.5
Nss | MCS | SNR_Start (dB) | SNR_End (dB) | Gain_Min (%) | Gain_Max (%)
1ss | 1.1 | 3.5 | 4.5 | 3.1 | 17.8
 | 3.1 | 8.5 | 10.5 | 3.8 | 22.7
 | 4.1 | 11.5 | 12.5 | 0.0 | 1.8
 | 4.2 | 13.5 | 13.5 | 0.7 | 0.7
 | 7.2 | 19.5 | 20.5 | 3.2 | 6.0
20MHz, 4x2x1ss, DNLoS, TxBF |  |  |  |  | 5.5
Nss | MCS | SNR_Start (dB) | SNR_End (dB) | Gain_Min (%) | Gain_Max (%)
1ss | 1.1 | -3.5 | -2.5 | 8.1 | 10.7
 | 2.1 | -0.5 | -0.5 | 0.1 | 0.1
 | 3.1 | 2.5 | 3.5 | 11.3 | 12.6
 | 4.2 | 6.5 | 6.5 | 8.3 | 8.3
 | 7.2 | 13.5 | 13.5 | 4.9 | 4.9
All MCS (Index in SE non-decreasing order) |  |  |  | 
Mod \ Coderate | 1/2 | 2/3 | 3/4 | 5/6
BPSK | MCS 0 | MCS0.1 | MCS0.2 | MCS0.3
QPSK | MCS 1 | MCS1.1 | MCS 2 | MCS2.1
16QAM | MCS 3 | MCS3.1 | MCS 4 | MCS4.2
64QAM | MCS4.1 | MCS 5 | MCS 6 | MCS 7
256QAM | MCS5.1 | MCS7.2 | MCS 8 | MCS 9
1K QAM | MCS7.1 | MCS9.1 | MCS 10 | MCS 11
4K QAM | MCS8.1 | MCS10.1 | MCS 12 | MCS 13
Existing MCS
Recommended New MCS

## Slide 9: Unequal QAM Design Philosophy
While this feature is attractive, still want to minimize:
  Modes in the spec
  Testing burden
  Signaling overhead
  Implementation complexity
  Link adaptation complexity
To achieve these goals, we adopt the following design approach
  Simplify the unequal modulation set by limiting the QAM gaps across spatial streams
    Only use up to 2 QAM levels difference between strongest and weakest streams
  Reduce the QAM variation patterns allowed for every Nss
    E.g., Patterns like (QAM/QAM-1/QAM-1/QAM-1) for the 4ss case are completely unnecessary
    Consider up to 3 patterns for each Nss
Without loss of generality, each QAM variation pattern (i.e., QAM variation across spatial streams) is assumed to have QAM in non-increasing order
  Eigen mode SINRs assumed to be in non-increasing order

## Slide 10: Adjacent Eigen Channel SNR Gap in NxN
For NxN channels, the SNR gap between two weakest eigen channels follows similar distribution, and the SNR gap between the second and third weakest eigen channels also follows similar distribution

## Slide 11: Unequal QAM Design for Up to 2 QAM Difference and 3 Patterns Per Nss
For 2ss, use 2 patterns, (QAM/QAM-1) and (QAM/QAM-2)
For 3ss
  The last 2ss use 2ss QAM variation patterns
  The 1st stream use same QAM as the 2nd stream or 1 QAM higher
For 4ss
  The last 3ss use 3ss QAM variation patterns
  The 1st stream use same QAM as the 2nd stream
Summary of design in the table
  There are 7 QAM levels from BPSK to 4kQAM
  “QAM” is the QAM level of the 1st stream
  “QAM-x” denotes x level down from “QAM”
Scenario | Unequal QAM Variation Patterns |  |  | 
 | 1st Stream | 2nd Stream | 3rd Stream | 4th Stream
2ss | QAM | QAM-1 |  | 
 | QAM | QAM-2 |  | 
3ss | QAM | QAM | QAM-1 | 
 | QAM | QAM | QAM-2 | 
 | QAM | QAM-1 | QAM-2 | 
4ss | QAM | QAM | QAM | QAM-1
 | QAM | QAM | QAM | QAM-2
 | QAM | QAM | QAM-1 | QAM-2

## Slide 12: Unequal QAM Simulation
Simulation setup
  20MHz, DNLoS & BLoS
  Tx BF for 2x2 with 1ss or 2ss, 3x3 with 2ss or 3ss, 4x4 with 3ss or 4ss
    Eigen mode SINRs assumed to be in non-increasing order
    Equal power allocation to all spatial streams
  Genie per channel rate adaptation in choice of MCS and Nss
  Candidate code rates: 1/2, 2/3, 3/4, 5/6
  Candidate QAM: from BPSK to 1kQAM
  Different schemes being compared
    Equal MCS with existing MCS
    2ss-optimum unequal QAM (any QAM combination for a code rate)
    Nss-pUEQM (Proposed unequal QAM with the selected patterns for Nss in slide 11, where Nss=2, 3, 4)
  All spatial streams use MCS in a particular set according to legend and share same code rate
      Any MCS
      Existing MCS (existing MCS from MCS0-11)
      Existing+new MCS (MCS0-11 and the recommended 4 new MCS in slide 8)
    In 2ss-optimum unequal QAM, MCS is omitted in legend

## Slide 13: 2x2 with 1ss & 2ss Perfect Link Adaptation
With the 4 proposed new MCS, 2ss unequal QAM with 2 patterns performs just slightly worse than 2ss optimum unequal QAM
  Improves over existing MCS only in large range of SNR

## Slide 14: 3x3 with 2ss & 3ss Perfect Link Adaptation
Additional 4 new MCS slightly improve over unequal QAM with existing MCS in operating SNR region for 3ss

## Slide 15: 4x4 with 3ss & 4ss Perfect Link Adaptation
Additional 4 new MCS improve over unequal QAM with existing MCS mainly in operating SNR region for 3ss but not in operating SNR region for 4ss

## Slide 16: Gains of Proposed Unequal QAM Design
Our proposed unequal QAM design performs good with existing MCS and better in some SNR regions with the additional 4 new MCSs
Scenario | Unequal QAM Design Options | MCS Set | Max Gain | 
 |  |  | DNLoS | BLoS
2ss | 2 patterns (QAM/QAM-1) & (QAM/QAM-2) | Existing MCS only | 1.8dB | 2dB
 |  | Existing MCS+MCS1.1, MCS3.1, MCS4.2, MCS7.2 | 2.2dB | 2.2dB
3ss | 3 patterns (QAM/QAM/QAM-1), (QAM/QAM/QAM-2) & (QAM/QAM-1/QAM-2) | Existing MCS only | 2.5dB | 2.6dB
 |  | Existing MCS+MCS1.1, MCS3.1, MCS4.2, MCS7.2 | 2.5dB | 2.6dB
4ss | 3 patterns (QAM/QAM/QAM/QAM-1), (QAM/QAM/QAM/QAM-2) & (QAM/QAM/QAM-1/QAM-2) | Existing MCS only | 2.3dB | 2.4dB
 |  | Existing MCS+MCS1.1, MCS3.1, MCS4.2, MCS7.2 | 2.3dB | 2.4dB

## Slide 17: Summary
Proposed unequal modulation design for 2-4ss with up to 2 QAM difference between strongest and weakest streams and up to 3 QAM variation patterns for each Nss
Analyzed unequal modulation RvR gain
  Majority of unequal modulation gain comes from matching modulation to SINRs of different spatial streams
  Adding new MCS could further improve goodput
Proposed new MCS that provide substantial gain in 1ss scenarios and unequal modulation

## Slide 18: SP1
Do you agree to add the following text to 11bn SFD?
  UEQM patterns for Nss=3 are limited to three:
    [M, M, M-1]
    [M, M, M-2]
    [M, M-1, M-2]
    Note:
      M is the constellation index
      M-1 refers to the constellation that is one order lower than M
      M-2 refers to the constellation that is two orders lower than M
Y/N/A

## Slide 19: SP2
Do you agree to add the following text to 11bn SFD?
  UHR defines unequal modulation which uses joint LDPC encoding across multiple spatial streams while at least one spatial stream uses a different modulation order compared to the first spatial stream, and is applicable only to non-MU-MIMO beamformed transmissions using 2 to 4 spatial streams in a UHR MU PPDU.
Supporting DCNs: 11-24/474, 11-24/498, 11-24/507
Y
N
A

## Slide 20: Reference
11-22/1930r0, Layered QoS and multi-layer transmission
11-22/0060r2, Layered QoS and multi-layer transmission follow-up
IEEE 802.11n-2009, IEEE Standard for Information technology-- Local and metropolitan area networks-- Specific requirements-- Part 11: Wireless LAN Medium Access Control (MAC)and Physical Layer (PHY) Specifications Amendment 5: Enhancements for Higher Throughput
11-24/0016r1, UHR MIMO RvR enhancement with unequal modulation
11-24/0113r1, Unequal Modulation in MIMO TxBF in 11bn
11-24/0117r1, Improved Tx Beamforming with UEQM
11-24/0176r1, Unequal Modulation over Spatial Streams
11-24/0433r0, Analysis on UEQM and UEQ MCS
11-24/0438r0, UEQM Benefit Analysis
11-24/0439r0, UEQM evaluation and simulation results

## Slide 21: Appendix

## Slide 22: 2x2x1ss, DNLoS, TxBF

## Slide 23: 2x2x1ss, DNLoS, OL

## Slide 24: 4x2x1ss, DNLoS, TxBF

## Slide 25: Per Stream SNR Gap in 2x2 Channel
Two eigen channels have median SNR gaps of 10.4dB in DNLoS and 11.5dB in BLoS
Equal MCS in TxBF is not optimal
Per stream SNR gap for other antenna configurations are shown in appendix

## Slide 26: Per Stream SNR Gaps in 3x3
In 3x3, eigen channels also have larger SNR gaps

## Slide 27: Per Stream SNR Gaps in 4x4
In 4x4, eigen channels also have larger SNR gaps

## Slide 28: SNR Gaps in 3x3 Vs 4x4, DNLoS
>1dB
worse
~7dB
worse

## Slide 29: Adjacent Eigen Channel SNR Gap in NxN
For NxN channels, the SNR gap between two weakest eigen channels follows similar distribution, and the SNR gap between the second and third weakest eigen channels also follows similar distribution
In i.i.d. channels, see pretty good alignment