## Slide 1: Considerations of Transmissions of Initial Control Response frames
Date: 2024-06-08
Authors:

## Slide 2
Recap
In [1], we reviewed NPCA, DSO, Power saving, in-device coexistence and dynamic preamble puncturing procedures, and considered them as changes between different modes.
Although they are different procedures to achieve different purposes, they share some commonalities.
A unified design of initial control frames for dynamic mode changes is proposed.

## Slide 3
Recap: General Design Considerations for ICF [1]
ICF | NPCA | DSO | Power Saving | Coexistence | Dynamic Puncturing | Highlighed Design Consideration
Transmitted before Mode Change | No | Yes | Yes | Yes | No | 
ICF/ICR in the same Mode | Yes | Maybe | Maybe | Yes | Yes | If with diff modes, padding is needed
Padding (e.g., FCS2) | No | Yes | Yes | No | No | 
Carried in non-HT Dup PPDU | Maybe | Maybe | Maybe | Maybe | Maybe | To support lagecy NAV setting, better to use non-HT Dup PPDU
Support multicast transmission (one-to-multiple) | Yes | Yes | Yes | Maybe | Yes | Could reuse TF. Need to design whether ICR is carried in TB PPDU
Initiated by an AP | Yes | Yes | Yes | Yes | Yes | 
Initiated by a non AP STA | Yes | No | Maybe | Yes | Yes | TF is DL only now. Either using TF with modification or a new type, or a new frame.
Contains Max BW | Maybe | Maybe | Yes | Yes | Maybe | With unified design, we could define different types/variants for different use cases/scenarios
Contains Max Tx/Rx Nss | Maybe | Maybe | Yes | Yes | Maybe | 
Contains Max MCS/Rx MCS | Maybe | Maybe | Yes | Yes | Maybe | 
Contains Dynamic puncturing | Maybe | Maybe | Maybe | Yes | Yes | 
Contains unavailable time | No | No | No | Yes | No | 
Contains QoS | Maybe | Maybe | Maybe | Maybe | Maybe | Good to have in all cases

## Slide 4
What Should Be Carried in ICR?
Option 1: ICR serves as an acknowledgement of ICF.
  The transmission of ICR is an implicit indication that the STA accepts the proposed dynamic mode change.
  In some scenarios, ICRs are concurrently transmitted in UL by multiple STAs. A natural question would be whether an ICR carries STA specific information, or it is designed to be identical from different STAs.
Option 2: ICR is used to accept or reject the proposed dynamic mode change by ICF.
  Status code may be included in the ICR so that it could explicitly indicate whether it accepts or rejects the proposed dynamic mode change and the reason to reject.
Option 3: ICR carries operational parameters proposed by the TXOP responder.
  The operational parameters carried in the ICR may be limited by the parameters proposed by the ICF.
  For example, a maximum bandwidth carried in the ICR may be upper bounded by the maximum bandwidth carried in the ICF.
Different options may be used for different types of ICFs that solicited the ICR frames.

## Slide 5
Transmission of ICF and ICR
Mode 1 could be considered as a permanent/static mode and Mode 2 could be considered as a transient/dynamic mode.
Option 1: An ICF is transmitted in Mode 1 and an ICR is transmitted in Mode 2. Padding is needed in ICF. Exemplary usage cases include power saving, DSO, etc.
Option 2: both ICF and ICR are transmitted in Mode 1. Padding may be needed in the ICR. Exemplary usage cases include coexistence, DSO, etc.
Option 3: both ICF and ICR are transmitted in Mode 2. Exemplary usage cases include NPCA, dynamic preamble puncturing, etc.
It may be more flexible if we allow different ICF/ICR transmission options for the same usage case with different STA capabilities.
  For example, we could use option 1 or option 2 for DSO STAs with different center frequency switching delay capabilities.

## Slide 6
Summary
We reviewed what kind of information should be carried in the ICR.
Three different options to transmit ICF/ICR are discussed.
For ICR design, we propose to consider the following:
  The information carried by ICR depends on the Dynamic mode change types, e.g., NPCA, DSO, Power saving, in-device coexistence, dynamic preamble puncturing, etc.
  Flexible transmission mechanisms of ICF/ICR, e.g., transmitted before the mode change or after the mode change.

## Slide 7
Reference
[1] 11-24-0504 Considerations of a unified initial control frame