## Slide 1: Thoughts on Co-Ex and P2P for 11bn
Date: 03-08-2024
Authors:

## Slide 2: Abstract
In this contribution, we provide some of the potential enhancements to 802.11 to better support in-device coexistence for WLAN devices.

## Slide 3: Introduction
Improving the in-device coexistence (co-ex) for WLAN STAs is important to enhance the performance and reliability of the overall network [1-4].
Co-ex event may occur due to interaction with—
  Other Wi-Fi devices: E.g., peer-to-peer (P2P) communication
  Non-Wi-Fi devices: E.g., Bluetooth, Ultra-wideband (UWB)
During the co-ex event, a STA may not be able to communicate with another STA (/AP) using the agreed-upon parameters. New co-ex constraints can be on--
  Period of operation: co-ex event overlapping with existing expected transmissions/reception time
  Frequency: co-ex event happening on a specific frequency
  Spatial streams: co-ex event reducing the receive NSS capability
Better addressing the in-device coexistence issues should be one of the critical goals for the TGbn group.

## Slide 4: Handling In-Device Co-existence Issues
In general, for predictable and non-urgent co-ex events, the STA (/AP) can notify the other AP(/STA) ahead of time about the upcoming unavailability for operation
  Existing technologies defined in 802.11, such as peer-to-peer TWT, can be used or enhanced to support these co-ex events
For urgent co-ex events, a TXOP-level intervention is needed
  The STA(/AP) can indicate within a TXOP the reduced capability of operation due to the co-ex events
  Control frames can be used to make such indications—
    Truncated TXOP
    Reduced BW
    Reduced RX NSS etc.

## Slide 5: Co-Ex for a Peer STA
Co-ex events for a STA (the “Co-ex STA”) often involve Wi-Fi or Non-Wi-Fi operation with another STA
  The other STA can be referred to as a “Co-ex Peer STA”
The constraints that are applicable for the Co-ex STA are often also applicable for the Co-ex Peer STA.
  Both STAs can be associated with the same AP
The Co-ex Peer STA also needs to handle the joint co-ex events
  As a co-ex event responder, in comparison with the co-ex event initiator, the Co-ex Peer STA may have even less opportunity to handle the co-ex events in time (e.g. with the AP)

## Slide 6: Proxy Co-Ex Indication (PCI)
The Co-ex STA, as a TXOP holder or TXOP responder, should be able to identify the Co-ex Peer STA when informing the AP about the co-ex events.
The AP can operate with both STAs with the knowledge that both STAs have the same co-ex events and, as a result, similar constraints.
  For example, due to non-responsiveness to transmissions during the co-ex event, the AP may not take any punitive action (e.g. reducing MCS) against either of the STAs

## Slide 7: Example: Proxy Co-Ex Indication (PCI)
In the figure, instead of RTS/CTS, other control/control response frames can also be used
In the figure, CTS/Response frame contains the time information beyond which both STA1 and STA2 will be unavailable due to co-ex events.

## Slide 8: Trust Mechanism for Proxy Co-Ex Indication (PCI)
A trust mechanism may need to be established between peer STAs before one STA can indicate to the associating AP the coex events and the corresponding constraints for the other STA.
The AP can verify whether a STA has the authority to indicate coex constraints for another STA.
  Based on the verification, the AP can confirm coex mode transition for one STA or both of the STAs.

## Slide 9: Summary
Better handling of the in-device coexistence is important for efficient and reliable UHR operation.
Predictable and non-urgent co-ex events can be handled by using or enhancing existing protocols in 802.11 (e.g. peer-to-peer TWT).
While informing the AP about a co-ex event, the STA, along with other reduced capability parameters, can also include information about the Co-ex Peer STA for fast co-ex signaling for the peer STA.

## Slide 10: Appendix

## Slide 11: Example 1: Trust Mechanism for PCI

## Slide 12: Example 2: Trust Mechanism for PCI

## Slide 13: References
[1] Liwen Chu, et.al., IEEE 802.11-23/1934r0, “In-device interference mitigation follow up”.
[2] Alfred Asterjadhi, et.al., IEEE 802.11-23/1964r0, “Coexistence Protocols for UHR”.
[3] Laurent Cariou, et.al., IEEE 802.11-23/2002r1, “In-device coexistence and interference follow – up”.
[4] Brian Hart, et.al., IEEE 802.11-23/2026r0, “Balanced In-Device Coexistence”.

## Slide 14: Straw Poll-1
Do you agree to define a mechanism to allow a STA to optionally indicate coexistence constraints information of another peer STA?