## Slide 1: Indication of 11bn Feature Set
Date: 2024-3-DD
Authors:
Name | Affiliations | Address | Phone | e-mail
Akira Kishida | NTT | 1-1, Hikarinooka Yokosuka-Shi, Kanagawa 239-0847, Japan | +81-46-859-2093 | akira.kishida@ntt.com
Yusuke Asai | NTT |  |  | 
Yasushi Takatori | NTT |  |  | 

## Slide 2: Introduction
In TGbn, various technologies, including coordination controls and supporting latency sensitive traffic technologies, are discussed to realize the scope of the project indicated in the PAR[1], and use cases in the CSD[2].
  e.g., Multi-AP coordination (coordinated R-TWT and coordinated TDMA, etc) [3]-[12], preemption for sporadic latency sensitive traffic support[13][14].
The effectiveness of those technologies depends on the operating use case because the reliability requirement is different according to each use case[15][16].
  Managed network architecture[17] will provide AP-centric scheduled operations suitable for private networks.
  Also, features supporting latency sensitive traffic will be essential, especially in specific use cases such as industrial automation[18].
Therefore, we discuss the features of indication of a set of 11bn features and parameters according to the use case.

## Slide 3: Application of 11bn technologies according to use cases and requirements
What 11bn technologies should be applied depends on the requirements of each use case.
  11bn technologies do not simply enhance throughput different from previous primal standards.
  It depends on the requirements of the use case whether supporting latency sensitive traffic (periodic or sporadic) or applying coordination controls is needed.
    For example, proactive coordination or latency improvement controls can be operated in private networks where the area owner exists (e.g., enterprise or industrial automation use cases) and refrain from using those controls in public networks.
Knowing what features will be operated would help to control appropriate 11bn technologies.

## Slide 4: Indication of capabilities and issues
Various information elements in management frames, such as Beacon, Probe Request, and Probe Response frames indicate the capabilities of supporting features.
  More features are defined in a new standard, and more information elements are created and included in management frames.
  This results in the bloating of management frames.
Capabilities do not signify what features are operated in the BSS.
  For example, though supporting Multi-AP coordination is indicated, any coordination control might not actually be operated if there is no necessity for the coordination.
If features and parameters to be operated are indicated as a feature set, efficient use of 11bn technologies could be achieved.
  For example, an AP can avoid the channel(s) or link(s) that other BSS operates latency sensitive traffic feature set.

## Slide 5: Indication of the operating 11bn features and parameters
Rather than individually indicating the operating information for each feature, it is preferable to indicate an index defining a set of features to be operated.
  Indicating each operating feature in addition to capabilities individually will increase information and result in the bloating of management frames.
  Defining features included in a feature set for each index is a future discussion item in TGbn.
The operating use case could be utilized as an index for the feature set.
  By indicating the operating use cases as an index, AP(s) and STA(s) can set features and parameters that should be operated.
  There is room for consideration of other methods to indicate the operating features in TGbn.
Step 1: Indicate the index (use case) that will be operated in the BSS.
e.g., No.x: Factory and Industrial
Indication
Step 2: Specify the operating feature set and its parameters designated by the index. e.g., C-RTWT, C-TDMA, Preemption, TXOP sharing…
Step 3: Notify the information of the index (use case).
Associated STAs can decide the operating feature set based on the information.
Others can know what features will be operated.
Notification
Configuration (TBD)

## Slide 6: Difference between capabilities and the operating features
The capability means the ability that the STA to support the features.
  Announced by management frames and so on.
The operating feature is the feature that the STA actually uses (or has a possibility to use) during its operation.
  Indicating a set of these operating features is the point of this contribution.
Management frames
IE a (Feature A)
IE b (Feature B)
IE c (Feature C)
IE x (Feature X)
Indication information (e.g., some kind of IE)
Capabilities
…
Feature A and operating parameters
Feature C and operating parameters
Feature F and operating parameters
Feature H and operating parameters
Operating features
These operating features should not be notified individually to reduce information bloating.
(These operating features correspond with the index)
Indication information might be some kind of IE (TBD) and it should contain minimum information such as Information index.
Feature B is supported but not in use actually.
Only features used in actual are listed.

## Slide 7: Summary
Unlike previous primary standards, IEEE 802.11bn aims to improve reliability, and the reliability requirement is different according to each use case.
11bn technologies should be operated appropriately according to the requirements of applications and use cases.
Therefore, indicating an index that denotes a feature set of the operating features and parameters is considered.
  The use case is a candidate of the index for the indication.
  The operating features denote features that will be operated actually and differ from the capabilities of features that the APs or STAs have.

## Slide 8: SP
Do you agree that indicating the operating features and parameters defined in 11bn is beneficial?
  -Yes
  -No
  -Abstain

## Slide 9: Reference
[1] Laurent Cariou, et al., “UHR proposed PAR,” IEEE 802.11-23/0480r3
[2] Laurent Cariou, et al., “IEEE 802.11 UHR Proposed CSD,” IEEE 802.11-23/0079r10
[3] Arik Klein, et al., “M-AP Coordinated Transmission framework,” IEEE 802.11-23/1871r2
[4] Yanchun Li, et al., “Discussion on UHR enhanced channel access,” IEEE 802.11-23/1973r0
[5] Laurent Cariou, et al., “R-TWT for Multi-AP,” IEEE 802.11-23/0297r0
[6] SunHee Baek, et al., “R-TWT Coordination in Multi-BSS,” IEEE 802.11-23/1916r1
[7] Liuming Lu, et al., “Coordinated R-TWT for Multi-AP scenarios - Follow up,” IEEE 802.11-23/1952r1
[8] Jeongki Kim, et al., “Discussion on Enhanced R-TWT for UHR,” IEEE 802.11-23/2084r0
[9] Xiangxin Gu, et al., “R-TWT protection in 11bn,” IEEE 802.11-23/2212r0
[10] Liuming Lu, et al., “Multi-AP Coordination for Low Latency Traffic Delivery,” IEEE 802.11-23/1556r1
[11] Abhishek Patil, et al., “Coordinated TDMA (C-TDMA) Follow-up,” IEEE 802.11-23/1895r2
[12] Geonhwan Kim, et al., “Coordinated TDMA Procedure,” IEEE 802.11-23/1912r0
[13] Giovanni Chisci, et al., “Preemption techniques to meet low-latency (LL) targets,” IEEE 802.11-23/1886r1
[14] Kiseon Ryu, et al., “TXOP Preemption Follow Up,” IEEE 802.11-23/1174r0
[15] Inaki Val, et al., “High Criticality Use Cases and Requirements,” IEEE 802.11-23/1834r0
[16] Brian Hart, et al., “Overview of Enterprise Policy and Goals,” IEEE 802.11-23/2026r0
[17] Inaki Val, et al., “Managed Networks under highly congested scenarios,” IEEE 802.11-23/1920r2
[18] Akira Kishida, et al., “Considerations on UHR PAR and KPIs,” IEEE 802.11-22/1919r4