## Slide 1: Power Save Protocols for UHR – Follow Up
Date: 2024-09-09
Authors:
Name | Affiliation | Address | Phone | Email
Sherief Helwa | Qualcomm Inc. |  |  | shelwa@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
Duncan Ho |  |  |  | 
Sanket Kalamkar |  |  |  | 
Giovanni Chisci |  |  |  | 

## Slide 2: Introduction
Power save is one important topic that is being addressed in UHR by introducing multiple protocols such as:
  Short-term PS schemes:
    Dynamic PS (DPS): A STA can switch back and forth between High Capability (HC) and Low Capability (LC) modes using control-level signaling to save power.
    Cross-link PS: Giving an MLD STA the flexibility to enable/disable PS mode on different links while reporting its links PS status to its associated AP MLD using one active link.
  Long-term PS schemes:
    Scheduled PS: TWT-like scheme that let a STA go into doze mode and switch back to active mode at a scheduled/preannounced time.
In this contribution, we continue our discussion on DPS and make proposals for further details.

## Slide 3: DPS Protocol and Open Items
The DPS protocol can summarized as follows:
  A STA can enable the DPS protocol using management-level signaling.
  A STA with DPS mode enabled, is expected to operate in a LC mode.
  The peer STA of the DPS STA needs to initiate frame exchanges/TXOPs with an ICF which requests the DPS STA to switch to HC mode.
  The DPS STA responds with and ICR frame confirming HC operation.
  The ICF frame may need to include padding to give enough time to the DPS STA for transition from LC to HC modes.
  To successfully transition from LC to HC during padding period, the DPS STA needs to error check the frame first, hence the need for an intermediate FCS field prior to padding.
Open items we address in this contribution:
  Intermediate FCS presence for DPS and location of intermediate FCS in ICF.
  Padding details.

## Slide 4: Intermediate FCS location within ICF
In DPS operation, the fields needed in the ICF are:
  Padding (long enough to fulfill the DPS STA request).
  Intermediate FCS preceding the padding field (when padding is needed).
In case a Trigger frame variant is used as an ICF, we discuss two methods on how to include the Intermediate FCS and Padding subfields in the Trigger frame.
Option 1:
  Include the Intermediate FCS subfield in a “special” User Info field.
  Use the Trigger frame padding to add sufficient padding duration for DPS.
Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
AID12 (> 2007) | Intermediate FCS | Padding (variable length)

## Slide 5: Intermediate FCS location within ICF
Option 2:
  Include the Intermediate FCS subfield within the Trigger frame Padding field and after the first 2 octets all set to 1’s.
  The needed amount of padding can be included right after the intermediate FCS subfield
  Beneficial to have an explicit indication of the inclusion of intermediate FCS in the ICF.
    If no explicit indication, then it should be implicitly understood that the STA will expect an intermediate FCS in the IFC after it enters DPS mode.
Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
1111111111111111 | Intermediate FCS | Padding (variable length)

## Slide 6: Padding
The required padding duration must be announced by the STA prior to switching to the DPS mode.
  This way, its peer STA knows how long the padding should be.
The required padding duration can be announced in information elements (e.g., UHR Capabilities, UHR Operation IE) or in Action frames used for DPS mode enablement.
The proposed range of padding duration values is from 0 us to 256 us.
  The maximum value 256 us is expected to cover all possible LC to HC transition delays.
  Also, we propose to start the range from 0 us as an indication that a DPS STA can possibly ask for no padding.
  In the case of no padding, it follows that no intermediate FCS is required in the ICF.

## Slide 7: Conclusion
In this contribution, we covered some details related to ICF padding for DPS and the needed intermediate FCS.
Two options were discussed on how to include the Intermediate FCS and Padding subfields in a Trigger frame that acts as ICF.
For padding, we proposed that a DPS STA has to advertise its needed ICF padding duration between 0 us to 256 us.

## Slide 8: Straw Poll 1
Do you support that an UHR STA that uses the power save mode to transition from lower capability (LC) mode to higher capability (HC) mode, advertises the amount of padding it needs in a received initial control frame?
  Padding values range between 0 and 256 us with a TBD resolution

## Slide 9: Straw Poll 2
Do you support that if a UHR STA (UHR non-AP STA or UHR Mobile AP) operates with the power save mode where the STA transitions from a lower capability mode to a higher capability mode upon reception of an initial control frame (that we call here DPS), then its associated peer STA, that supports transmitting intermediate FCS, shall include an intermediate FCS, if needed by the STA, in the initial control frame that it transmits to the STA.
  Mandatory/optional support for transmitting intermediate FCS is TBD