## Slide 1: Secure Control frames-Follow Up
Date: 2024-09-24
Authors:
September 2024
Notes: September 2012

## Slide 2: Introduction
UHR is focused on improving reliability, reducing latencies and lowering power consumption at devices.
To achieve these goals, UHR will rely on control information
  E.g., acknowledgment, NAV setting, triggering, initiation of frame exchanges (ICF/ICR), etc.
However, the frames carrying this information are not protected
  BAR, BA, Trigger, etc.
A malicious player can attack a link by targeting frames containing control information
  leading to data stream disruption, denial of service, power drainage, resource wastage, etc.
Data stream disruption is especially problematic for UHR
  Since it directly affects the reliability of the communication link
Therefore, it is an important issue that needs to be addressed to meet UHR’s goals
  And if the other abovementioned issues are solved on the way, then much better
September 2024

## Slide 3: Proposal
Provide means to protect:
  At least for certain control frames
And since control info., in general, needs to be generated quickly:
  Provide message integrity check (MIC),
    Perhaps not worrying about encryption (more complex)
In the following we discuss mechanisms to protect at least:
  Trigger, (Multi-TID) BAR, and Multi-STA BlockAck (M-BA) frames
Aiming at solving the issue at both the AP and the STA side since an attacker can exploit the vulnerability of these frames
  To disrupt/corrupt the data paths between two STAs
September 2024

## Slide 4: Example of Attacks
MU BAR Trigger frames solicits TB PPDUs from one or more STAs
  PPDUs are generated from the intended recipients of the Trigger frame
    Each TB PPDU contains a C-BlockAck or M-BA frame
      All buffered QoS Data up to SSN of the BAR are reordered and passed to the next MAC process
      BA scoreboards are shifted to align with the value of the SSN of the BAR
  Now if this frame is sent by an attacker, then there will be a misalignment of
    QoS Data delivery status and BA scoreboards between the originator and recipient
  Same issue exists with Multi-TID BAR and C-BAR frames
M-BA frame is sent to acknowledge received QoS Data frames
  BlockAck Bitmap indicates receive status of the received QoS Data frames
    Originator uses this information to update the BA scoreboard
  Now if this frame is sent by an attacker, then again there will be a misalignment
    But also, false indications of receive status of Data frames at the recipient
Hence, misalignment, wrong classifications, packets discarded, etc.
C-BA 1
MU BAR
backoff
C-BA 2
Data 1
Basic Trigger
Data 2
M-BA
September 2024

## Slide 5: Proposal: Control MIC
Define a container Control MIC Field (CMF)
  This container is similar to MME used for beacon protection
    i.e., may carry one or more of Key ID, PN and MIC.
      Expected sizes: X=1 bit, Y=6 octets, Z=16 octets, respectively
    The container could be spread across fields in a frame
Add CMF to at least the following control frames
  Trigger, M-BA, BAR, Multi-TID BAR (covering DL and UL SU sequences)
In such a way that it is backwards compatible (whenever necessary)
  E.g., a group addressed control frame able to address both UHR and non-UHR STAs
Discuss need for extra padding when the control frame is protected
  Since MIC check may need some extra processing time
    Also see later slide on key look-up considerations
 | Key ID | PN | MIC
 | X | Y | Z
September 2024

## Slide 6: CMF Location – e.g., Trigger frame
Add CMF to provide Trigger frame protection
  MIC is calculated over the fields (whichever needs protection)
    Including the Common Info and User Info List fields
  Applicable to supporting UHR STAs (& unassoc. UHR STAs that know the key)
    Other STAs (e.g., HE/EHT) simply ignore CMF, but keep processing the Trigger frame
MIC is carried in the CMF and follows the “useful” User Info List
  GMAC for MIC calculation & temporal key (TK) to compute MIC
  Separate PN for Trigger frame replay protection
UHR STAs discard a received Trigger frame in case of a MIC mismatch
  Hence, no need to generate TB PPDUs, saving power, keep data path intact, etc.
A side benefit is that the receiving UHR STA does not have to wait for FCS check
  MIC verification pass is sufficient.
 | Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
Octets: | 2 | 2 | 6 | 6 | 8 or more | variable | variable | 4
CMF 1
CMF n
Trigger frame
September 2024

## Slide 7: Where to carry the CMF in Trigger frame
Option 1: In User Info fields
  Identified with an unassigned value of the AID12 field (e.g., 2023/2024)
    Each User Info field is 5 bytes
    Number of such special User Info fields depend on the length of the CMF
Option 2: In Padding field, (immediately) after the first two octets
  First two octets are a sequence of 1s to indicate start of padding
  Next Y+Z octets of Padding field would be the CMF, and rest will be padding
    Possibly a CMF length field (while avoiding the all 1s combination to not confuse with padding)
In either option we may need a bit indicating the frame is protected (i.e., Protected bit) and possibly the Key ID field early in the frame
  e.g., in Common Info or Special User Info
  Placing these in early portion of the frame helps receive side processing
 | Key ID | PN | MIC
 | X | Y | Z
September 2024

## Slide 8: Secure M-BA frame
Add CMF to provide M-BA frame protection
  MIC is calculated over the preceding fields of the frame (whichever needs protection)
    Including the BA Control and the preceding Per AID TID Info fields
  Applicable to supporting UHR STAs
    Other STAs (e.g., HE/EHT) simply ignore CMF, but keep processing the M-BA frame
PN and MIC is carried in the CMF and follows “useful” Per AID TID Info List
  GMAC for MIC calculation & temporal key (TK) to compute MIC
  Separate PN for M-BA frame replay protection
A single bit KeyID and Protected bit can be carried within the BA Control field (i.e., frame’s early portion)
Padding: can be achieved with STA Info fields addressed to other STAs or to nobody
UHR STAs discard a received M-BA frame in case of a MIC mismatch
  Hence, no update of BA scoreboards or modification of data path
Octets: | 2 | 2 | 6 | 6 | 2 | variable | 4
 | Frame Control | Duration/ ID | RA | TA | BA Control | BA Information | FCS
Per AID TID Info 1
…
Per AID TID Info n
Repeated for each
<AID, TID> tuple
CMF
Padding
September 2024

## Slide 9: Where to carry the CMF in M-BA frame
Also applicable to Multi-STA BlockAck frame, wherein
  CMF is in a Per AID TID Info field that is identified by an AID11 field that is currently unassigned (say e.g., 2023)
    The FN subfield of the BA SSC could indicate the CMF length
Octets: | 2 | 2 | 6 | 6 | 2 | variable | 4
 | Frame Control | Duration/ ID | RA | TA | BA Control | BA Information | FCS
Per AID TID Info 1
…
Per AID TID Info n
Repeated for each
<AID, TID> tuple
2 | 0 or 2 | 16, 32
AID TID Info | Block Ack Starting Sequence Control | CMF
Bits: | 11 | 1 | 4
 | AID11 | Ack Type | TID
September 2024

## Slide 10: Secure Multi-TID BlockAckReq frame
By now, notice the pattern
  CMF follows the last useful BAR Information
  The first bit of the Per TID Info field is set to 1 to indicate CMF
    Possibly they can also indicate the length (e.g., use 2 bits and nonzero)
  Single bit Key ID and Protected bit can be carried within the BAR Control field
  Padding can be achieved with useless BAR Information fields or defining a padding field
Note: We can add CMF to C-BlockAckReq frames as well
CMF
Padding
September 2024

## Slide 11: Temporal Keys
Traditionally we use
  Integrity group temporal key (IGTK) for protecting group addressed frames
    This key is only used by the AP (note: Beacon has its own key, namely BIGTK)
  Pairwise temporal keys (PTKs) for protecting individually addressed frames
    This key is used by the AP and by non-AP STAs, and
    There are at least as many as there are associated STAs
It is natural to consider (equivalent of) IGTK and PTKs for protected control frames
  However, with more keys, more time may be needed for key lookup (especially for AP)
    Could be problematic when generating control frames (on-the-fly)
    Hence, it may be worth evaluating the use of padding to give time for key retrieval
It is preferred to have separate keys from security point of view
  Using the same key for two different security algorithms (e.g., integrity protection and encryption) can lead to related-key-attack.
As a result, propose to define
  Control integrity group temporal key (CIGTK) for group addressed control frames
    used only by AP
  Control pairwise temporal keys (CPTK) for individual addressed control frames
September 2024

## Slide 12: Conclusions
We discussed security issues with certain control frames and discussed mechanisms for securing them
The idea is that securing control information
  Will solve security issues with (at least some) Control frames, and ensure reliable exchanges between UHR STAs
And as side benefits of securing Triggers, it can reduce
  STA’s draining their power (useless response PPDUs),
  Waste medium resources (useless TXOPs),
  False wake transitions (eMLSR, Coex, DPS, DSO, etc.)
September 2024

## Slide 13: SP1
Do you agree to define in TGbn protection for the following Control frames
  Trigger
  Compressed BAR and Multi-TID BAR
    Other variants of BAR frames to be protected is TBD
  Multi-STA BA
    Other variants of BA frames to be protected is TBD
September 2024

## Slide 14: SP2
Do you support to include the following signaling in a Control frame that is defined to be protected?
  Key ID field
    The size of the key ID field is one bit
  PN field
    The size of PN is 6 bytes
  MIC field
    The size of MIC is 16 bytes
September 2024

## Slide 15: SP3
Do you support that key ID field is indicated in BA Control field of the protected Multi-STA BA?
September 2024

## Slide 16: SP4
Do you support that key ID field is indicated in BAR Control field of the protected compressed BAR variant and protected Multi-TID BAR variant?
September 2024

## Slide 17: SP5
Do you support that in the protected M-BA frame a special AID (reserved value TBD) is used to indicate that the Block Ack Bitmap field contains PN and MIC fields rather than Block Ack bitmap?
    Note – The indication for the size of Block Ack Bitmap field is reused for backward compatibility
September 2024

## Slide 18: SP6
Do you support that the PN and MIC fields are included after BAR Information field in a protected compressed BAR variant and protected Multi-TID BAR variant?
September 2024