## Slide 1: Tgbi: Group vs Individual epochs
Authors:
Date: 2024-03-12
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
J. Levy | Interdigital |  |  | 

## Slide 2: Scope
Trigger discussion on the differences between group and individual epochs, to facilitate agreement and writing of specification
Current IEEE 802.11bi/DXX has defined two types of epochs:
  Group epoch: all or selected STAs simultaneously transition their MAC+other parameters based on AP trigger
  Individual epoch: each STA transitions its MAC+other parameters simultaneously

## Slide 3: Group epoch
Main idea: hide in the group
The AP and STA negotiates:
  Epoch duration
  Epoch starting time
  Others: e.g., AID offset, MAC address generation mechanism
The Epoch is periodic with interim periods where two MAC addresses are used simultaneously (the new one for the new epoch and the previous one for remaining frames in buffer, retx, etc..)
Epoch parameters are exchanged on protected frames
Open questions:
  New MAC address is exchanged or generated?
  What happens if there is a MAC address collision
  Is there a minimum set of STAs to be included in the epoch to consider it valid?
  May we have multiple different group epochs simultaneously in the bss?

## Slide 4: Individual epoch
Main idea: confuse observer
Change MAC address independently and very often
  Reduce number of parameters to be exchanged with AP – autogenerate as much as possible
  Change them potentially in a very short period
Open points
  There is a variety of Tx Ops, will they change MAC independently of their duration?
  Can we use individual and group epochs simultaneously?
  Makes sense to use this even if you are the only one in the bss doing it?
  What happens with retx out of the tx op? are they using new or old parameters?
  Makes sense to define individual epochs of longer duration?