## Slide 1: Enhancements on AP Power Save
Date: 2024-05-07
Authors:

## Slide 2: Introduction
Many contributions have been submitted to enable AP Power Save
  Dynamic Power Save [1-4]
  Scheduled/Unscheduled AP Power Save [5-8]
Dynamic Power Save mode allows a STA to maintain a lower capability mode when the STA doesn't participate in frame exchanges
Consequently, the power-saving benefits derived from Dynamic Power Save increase as the STA stays more time in the lower capability mode

## Slide 3: Recap: Dynamic Power Save [1]
STA is in Listen State unless solicited for transition to Awake State
  Listen State (lower capability mode): STA is only capable of RX PPDUs of certain configuration
    E.g., non-HT (dup) PPDUs, and mandatory data rates
  Awake State (higher capability mode): STA is capable of RX PPDUs with higher BW/NSS
    E.g., as advertised in most recent Caps/OMN/OM Control (for both AM and PS modes)
Initial Control Frame (ICF) triggers transition from listen to awake state

## Slide 4: Limitations on Dynamic PS for an AP
An AP associated with multiple non-AP STAs may receive multiple ICFs, while a non-AP STA receives ICF only from its associated AP
  The AP's inability to sustain a lower capability mode for an extended duration restricts the potential power-saving benefits of the Dynamic Power Save mode
ICF
ICR
Frame exchanges
ICF
Frame exchanges
ICR
ICF
Frame exchanges
ICR
AP
Non-AP STA1
Non-AP STA2
Non-AP STA3
HCM
HCM
HCM
LCM
LCM
LCM
Frame exchanges
Frame exchanges
Frame exchanges
    *LCM : Lower capability mode
    *HCM : Higher capability mode

## Slide 5: Proposal: Semi-Dynamic PS mode
Allows an AP to transition selectively to the higher capability mode after receiving an ICF
  When an AP decides to transition to a higher capability mode
    The AP responds with ICR and performs data frame exchanges
  When an AP decides not to transition to a higher capability mode
    The AP records information (e.g., AID, requested capabilities, etc.) of the non-AP STA that transmitted ICF
      The AP may respond with ICR which indicates the AP’s decision to maintain a lower capability mode
        If ICR can be transmitted during the lower capability mode (e.g., non-HT, basic rate, 20 MHz, etc.)
    Later, after transition to a higher capability mode due to the other reason except that ICF
      The AP transmits at least one Trigger frame to solicit pending UL traffic from the recorded non-AP STA(s)
      That is, the ICF transmitted by the non-AP STA servers to reserve resources

## Slide 6: ICF/ICR for the Semi-Dynamic PS mode
To ensure timely transmission of LL traffic, ICF transmitted by non-AP STAs may include an indication of LL traffic
  When a non-AP STA intends to transmit LL traffic, it informs an AP using this indication
    The AP might decide to transition to a higher capability mode when a LL traffic transmission is indicated
  When a non-AP STA intends to transmit non-LL traffic, it transmits the ICF for reserving resources
To help non-AP STA operation, the ICR transmitted by the AP may include transition timing information
  After receiving the ICR, the non-AP STA may manage its power state based on the indicated transition timing
  Indication may be done implicitly
    a scheduled wake-up interval (similar with TBTT)
    an announced maximum triggering delay (delay bound of the corresponding triggering frame for an ICF)

## Slide 7: Illustration: Semi-Dynamic PS mode
ICF
ICF
TB PPDU
(80 MHz, 2-SS)
ICR
AP
Non-AP STA1
Non-AP STA2
Non-AP STA3
HCM
ICF
ICR
LCM
TB PPDU
(40 MHz, 1-SS)
TF
ICR
Requirements
BW = 40 MHz (or buffer status)
N_SS = 1
LL traffic = false
Requirements
BW = 80 MHz
N_SS = 2
LL traffic = false
Requirements
BW = 40 MHz
N_SS = 2
LL traffic = true
Frame exchanges
BA
Frame exchanges
LCM
Transition
= false
Transition
= false
Transition
= true
ICF
Requirements
BW = 160 MHz
N_SS = 4
LL traffic = false
ICR
Transition
= true
HCM
UL PPDU
(160 MHz, 4-SS)

## Slide 8: Combinations on the PS modes (Semi-Dynamic PS + Scheduled PS)
Type 1 (For uninterrupted service)
  An AP transitions between lower and higher capability modes within the Scheduled PS period
    During the Scheduled service period, the AP and non-AP STAs can do frame exchanges w/o ICF
    During the Scheduled PS period, the AP may transition to the higher capability mode upon receiving an ICF with LL traffic indication
ICF
ICR
ICF
TB PPDU
ICR
Frame exchanges
AP
Non-AP STA1
Non-AP STA2
Non-AP STA3
Awake
LCM
TF
TB PPDU
BA
LCM
Scheduled service period
(Full-capabilities)
Scheduled PS period
(LCM by default)
Scheduled PS period
(LCM by default)
LL traffic indication = false
BSRP
BSR
BSR
DL MU PPDU
ICF
LL traffic indication = true
ICR
HCM
Frame exchanges
LCM

## Slide 9: Combinations on the PS modes (Semi-Dynamic PS + Scheduled PS)
Type 2 (For PS effectiveness)
  An AP transitions between Doze and Awake states according to the scheduled service period
    Within the Scheduled service period, the AP and the non-AP STAs perform Dynamic PS-related operations
ICF
ICF
Frame exchanges
AP
Non-AP STA1
Non-AP STA2
Non-AP STA3
Doze
LCM
Scheduled service period
(Semi-Dynamic PS)
Scheduled PS period
Scheduled PS period
LL traffic indication = false
ICF
LL traffic indication = true
ICR
HCM
Frame exchanges
Doze
ICR
ICR
TB PPDU
TF
TB PPDU
BA

## Slide 10: Summary
We have discussed enhancements on the power-save modes for the AP
  Semi-Dynamic AP Power Save mode
    Allows an AP to transition selectively to the higher capability mode after receiving an ICF
    Aimed at increasing power-saving efficiency
  Semi-Dynamic AP Power Save + Scheduled AP Power Save
    Replacement of the Awake or Doze duration of Scheduled AP Power Save mode with Semi-Dynamic PS mode operation

## Slide 11: Straw Poll 1
Do you support to define a power save mode for an UHR AP wherein the AP transitions between lower and higher capability modes following TBD conditions?
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, etc.)
  Higher capability mode (e.g., parameters advertised in Capability/Operation elements, OM Control, etc.)
  Conditions for transition are TBD

## Slide 12: Straw Poll 2
Do you agree that an UHR AP may decide to remain in a lower capability mode after receiving an initial control frame from a non-AP STA following TBD conditions?
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, etc.)
  The conditions for maintaining lower capability mode are TBD

## Slide 13: References
[1] 11-23/1965 Dynamic Power Save– follow up (Alfred Asterjadhi , Qualcomm)
[2] 11-23/1936 AP MLD power save follow up (Liwen Chu, NXP)
[3] 11-24/451 AP state transitions in DPS mode (Vishnu Ratnam, Samsung)
[4] 11-23/2127 11bn Power Save (Jeongki Kim, Ofinno)
[5] 11-23/2040 Enabling AP power save – Follow Up (Alfred Asterjadhi , Qualcomm)
[6] 11-23/1835 AP Power Management (Yongsen Ma, Samsung)
[7] 11-24/97 AP Power Management Follow-up (Yongsen Ma, Samsung)
[8] 11-24/352 Enabling Unscheduling AP PS Follow-up (Guogang, Huawei)
[9] 11-24/589 Dynamic TTLM for AP MLD Power Save (Yongsen Ma, Samsung)