## Slide 1: Thoughts on functionality and security architecture for UHR seamless roaming
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | Email
Thomas Derham | Broadcom |  |  | thomas.derham@broadcom.com
Nehru Bhandaru |  |  |  | 
Manoj R Kamath |  |  |  | 
Sindhu Verma |  |  |  | 
Shubhodeep Adhikari |  |  |  | 
Matthew Fischer |  |  |  | 
Brian Petry |  |  |  | 

## Slide 2: Introduction
There seems to be general agreement (e.g. [1], [2]) on some technical requirements for UHR seamless roaming, whereby:
  the non-AP MLD remains in State 4 throughout a successful roam from one AP MLD to another AP MLD
  the non-AP MLD has only a single point of connection to the DS at a given time
    with possible exception for the non-AP MLD to exchange buffered DL frames with serving AP MLD after switching its point of connection to the target AP MLD
  during roaming procedure, the context related to a non-AP MLD is exchanged between AP MLDs such that the data exchange context is preserved
    a request/response frame exchange is defined for the non-AP MLD to initiate roaming procedure, and the context exchange to be triggered and completed
In this submission, we discuss and propose:
  High-level requirements for UHR seamless roaming
  A description of new capabilities to achieve these requirements
  Security framework requirements
    with a caution against some alternative proposals to share PTK(SA) across multiple AP MLDs
  A high-level design for these new capabilities as an extension of FT protocol

## Slide 3: High-level requirements Generic sequence implied by so-far agreed requirements
non-AP MLD
AP MLD2
AP MLD1
s1
s1
s4
s1/s2
s4
State 4 (s4) data path with AP MLD1
Limited DL data path for “buffered data delivery” from AP MLD1
State 4 (s4) data path with AP MLD2
Non-AP MLD is always in State 4 with one AP MLD in the network
  Additionally, for a short period after roam to target AP MLD2, a limited data path for “buffered data delivery” continues to exist with serving AP MLD1 to allow remaining DL data to be flushed
Roam signaling exchange(s) trigger (*):
  (0) initiation of roaming procedures
  (1) capability exchange (per-link and per-MLD) and security setup
  (2) context exchange to AP MLD2
  (3) establishment of OTA data path (State 4) with AP MLD2
  (4) DS mapping update (to forward DL traffic to AP MLD2)
initial auth/assoc to AP MLD1
roam to AP MLD2
s4limited
* This list does not imply the ordering of triggers or the number of signaling messages

## Slide 4: High-level requirements Problem statements and solution requirements
Problem (1): Roams may not be triggered when needed, especially in mobility, resulting in “emergency scans” when current link fails, causing outage/disruption to data flows
  Client devices cannot continuously scan for off-channel transition candidates due to (a) power consumption limitations and (b) impact on existing link (depending on implementation)
  Networks cannot continuously monitor for client devices from other off-channel APs
    Client devices rarely transmit off-channel, especially if using passive scan
  Hence, measurement data needed by roaming/steering algorithms may be unavailable or unreliable
    Incomplete and/or stale bidirectional RSSI measurements
    Incomplete, unreliable and/or unprotected link/AP scoring metrics (e.g. channel utilization, WAN capacity/latency)
  In addition, roaming/steering algorithms tend to be conservative in triggering roams in order to:
    avoid link disruption due to (frequent) roam events
    avoid ping-pong / thrashing roams, particularly if both network-side and client-side roaming/steering algos are active
    avoid higher-layer disruption (e.g. IP change), bill shock, etc, if algorithm triggers network switch (e.g. to cellular)
Active measurement/metric collection (*)
Passive measurement/metric collection (**)
Transition candidates assessment
No_action
Roam_trigger[AP_MLD_Addr]
Collection_trigger
  Solution requirements:
    More efficient, protected, exchange of measurements/metrics – minimize signaling and off-channel operations
    Exchange information on capabilities and activity of client-side and network-side algos
    Support exchange of metrics to intelligently determine collection_trigger events (e.g. network topology)
(*) e.g. active scan, off-channel passive scan, send measurement request to peer
(**) e.g. current link metrics (PER, MCS, ...), on-channel passive scan, receive unsolicited measurement report from peer

## Slide 5: High-level requirements Problem statements and solution requirements (2)
Problem (2): Once a roam is triggered, roam procedures themselves cause outage/disruption to data flows
  Data exchange suspended during off-channel authentication/reassociation exchanges with target AP
    except, potentially, for clients capable of simultaneous Tx/Rx on both channels
  Data exchange with target AP may be suspended, inefficient or insufficiently prioritized until MAC states are re-established (e.g. BA agreement, MSCS/SCS rules)
  Data packet loss and/or duplication (e.g. DL packets buffered at serving AP may be lost, dirty scoreboard on roam)
    alternatively, implementations might defer roam until buffers are empty and scoreboard is clean, which can lead to similar “emergency roam” scenario as on previous slide
  Roam failures or delays (e.g. association comeback procedures) occur with non-negligible probability
    e.g. security (SA Query / PMF) related [can also be due to insufficient link quality or excessive roams - see previous slide]
  Solution requirements:
    Allow all roam setup exchanges with target AP (e.g. reassoc req/resp) to be tunneled over DS via serving AP
      For scenarios where roam is triggered while link quality with serving AP is still good
    Enable roam setup to occur with a minimal number of exchanges
      For scenarios where roam exchanges are directly with target AP due to poor link quality with serving AP
    Enable context transfer over DS to target AP, to avoid post-roam exchanges for MAC state re-establishment
    Provide mechanisms for retrieval of buffered data at serving AP, and optimization of delivery order requirements, depending on higher-layer requirements of flows in a given TID
    Ensure roaming security framework is robust to avoid security-related roam failures / delays

## Slide 6: Description of new capabilities Roam triggering
UHR AP MLD and non-AP MLD exchange transition candidate information within roam setup request/response frames (e.g. Reassoc Req/Resp)
  Enables both peers to obtain initial information without need for additional management frame exchanges (e.g. Neighbor Report Req/Resp, BTM Query/Req, Beacon Req/Resp)
  In request frame, Non-AP MLD includes Neighbor Report elements for each link of the other AP MLDs (in same ESS) that were viable but non-selected join/transition candidates
    Define RCPI element as a new subelement for Neighbor Report, so non-AP MLD indicates the beacon RCPI
    Consider also including Actual Measurement Start Time when RCPI measurement was made (similar to Beacon Report)
  In response frame, AP MLD includes Neighbor Report elements for each link of the AP MLDs (in same ESS) that are its topological neighbors
    RCPI subelement indicates, if available, a measured RCPI for some frame the non-AP MLD transmitted on that channel
    NR elements should include subelements with metrics for transition candidate scoring (e.g. BSS Load subelement)
With the above extensions, management frame exchanges can be used to provide updated information post-association, e.g.
  (AP MLD querying non-AP MLD): Beacon Report Request/Response
    Non-AP MLD should respond at least when off-channel scan is not required (e.g. Table mode, or current channels only)
    APs of a managed network should avoid requesting all beacon contents since that information is already known
  (non-AP MLD querying AP MLD): BTM Query/Request
    Consider a new Request Mode with more deterministic requirements – e.g. if request using this mode specifies a target AP, the non-AP MLD must attempt to roam to the target except if specified conditions (indicated in response) are met

## Slide 7: Description of new capabilities Roam triggering (2)
UHR AP MLD and non-AP MLD exchange information about network topology and activity of roaming/steering algorithms within roam setup request/response frames (e.g. Reassoc Req/Resp)
  In response frame, AP MLD also indicates basic network topology and recommended transition RSSI (if known) for each setup link
    e.g. by including ESS Report element (with new extensions?) in each per-STA profile
  In request frame, non-AP MLD indicates activity of its roaming algorithm
    e.g. none (on link failure only) vs proactive, typical off-channel scan cadence, etc
  In response frame, AP MLD indicates activity of its steering algorithm
    e.g. none, colocated APs only vs ESS-wide steering, unassociated STA scan capability by other (co-channel and/or off-channel) APs in network, etc
UHR non-AP MLD can probe a transition candidate AP MLD via serving AP MLD
  Tunneled probe request/response, potentially targeting multiple candidates AP MLDs, either as standalone exchange (e.g. based on FST Action using OCT) or bundled with other roam exchanges
    Note: In general, non-AP MLD needs contents of Probe Response (or Beacon(s)) of candidate target AP MLDs to make roam decision (*); i.e. Neighbor Report alone is not sufficient
    Note: Implementations might still prefer to go off-channel to obtain RSSI for link quality scoring, however topology information (see above) could be sufficient
(*) e.g. BSS Load, WAN metrics, BSS Membership Selectors, VSIEs, ...

## Slide 8: Description of new capabilities Roam signaling
Use robust management frames to tunnel roam exchanges with target AP MLD via serving AP MLD
  Serving AP forwards the exchanges to/from target AP MLD over DS using RRB or similar
Define a new mechanism to protect roam signaling to/from an AP MLD where an active pairwise PTK does not exist
  Sharing a PTK (used with CCM/GCM cipher) across roams should be avoided – see later slides
  e.g. define a dedicated UHR Management Privacy Key (PTK-PRIV), which is solely used to protect unicast management frames sent by a given non-AP MLD to any AP MLD in the ESS for which no PTKSA exists
    extracted from existing master keys (e.g. PMK, R0-Key-Data) during initial association to the ESS
      a secret between one non-AP MLD and all the AP MLDs in the ESS (or mobility domain)
    PTK-PRIV is distributed over the DS to other AP MLDs in the network (e.g. along with PMK / PMK-R1)
    PTK-PRIV is always used with AES-SIV (RFC 5297), which is nonce-misuse resistant (see later slides on PTK sharing)
      Note: AES-SIV is already used in 802.11 to encrypt parts of FILS Reassociation frames
    Non-AP MLD incorporates a fresh nonce in the AAD for each exchange to avoid tracking if the data payload is the same
Ensure the signaling messages that execute the roam are cryptographically bound to proof-of-possession of a pairwise key
  e.g. include MIC of the message using PTK-KCK
  avoids roam failure scenarios caused by PMF protection mechanisms (SA Query) when unprotected (re)association signaling is used

## Slide 9: Description of new capabilities Roam signaling (2)
non-AP MLD
target AP MLD
SNonce
ANonce
MIC(key=PTK-KCK, SNonce || ANonce || msg3)
MIC(key=PTK-KCK, SNonce || ANonce || msg4)
non-AP MLD
target AP MLD
SNonce
ANonce, MIC(key=PTK-KCK, SNonce || ANonce || msg2)
MIC(key=PTK-KCK, SNonce || ANonce || msg3)
non-AP MLD
target AP MLD
ANonce
SNonce, MIC(key=PTK-KCK, SNonce || ANonce || msg2)
MIC(key=PTK-KCK, SNonce || ANonce || msg3)
AP MLD initiated, 3-message
non-AP MLD initiated, 3-message
non-AP MLD initiated, 4-message
Efficiently derive new PTK during roam procedure out of critical path
  Embed ANonce, SNonce and PTK-confirming MICs in roam signaling that will occur anyway
    e.g. messages that trigger context exchange, State 4 establishment, DS mapping update, deliver per-link group keys, etc
    Note these messages might be exchanged directly with target AP MLD, or tunneled via serving AP MLD
  Example sequences when embedding within 4-message or (AP MLD or non-AP MLD initiated) 3-message exchanges are shown below

## Slide 10: Description of new capabilities Delivery of buffered DL data at (previously) serving AP after roam
Post-roam retrieval of already-buffered DL data from (previously) serving AP MLD to non-AP MLD has been proposed as a way to achieve zero-packet loss on roam
  Relatively simple network implementation – no need for transfer of buffered data between AP MLDs over DS
Design should include:
  Signaling within roam exchanges to indicate buffer state at serving AP MLD (i.e. whether buffered data exists)
  Signaling of remaining buffer state during data delivery (e.g. so non-AP MLD knows when it has received all data)
  Definition of which class 3 frames that can be transmitted in this state: DL Data (unicast only?), BA, mgmt?
  Security design – assume buffered data is sent using serving AP MLD’s PTK and PN space
    Note: Even in a “shared PTK” design, a separate replay counter is needed for the buffered data and the link with target AP MLD
  Consider frame exchanges to assist concurrent operation by multi-radio non-AP MLDs
    Note: The affiliated APs of source and target are not part of the same MLD; therefore MLO features (e.g. STR, eMLSR, cross-link PM) cannot be used per-se across the two links
  Ability for non-AP MLD to choose whether to retrieve any or all of the buffered data for a given TID
    Buffered data retrieval implies some disruption to data path with target AP MLD, especially when on different channels
    For some flows. zero-packet loss might not be useful or desirable, e.g. “stale” packets – see Annex slide
    AP MLD should not attempt to send buffered data if the non-AP MLD indicates it will not collect it
An alternative option is for the already-buffered DL data to be transferred over DS to the target AP MLD, for delivery to the non-AP MLD
  This may be a good solution for certain network architectures, but may be suitable/viable for some other architectures
  It can generally be achieved as vendor implementation without formal support in the standard (see Annex slide)

## Slide 11: Description of new capabilities Control plane context exchange
Block ACK
  Experimental results (see later slides) indicate that ADDBA exchanges take a few ms to start, and then take a few more ms to complete, and this is the dominant cause of outage in an optimized design
    Data transfer does not start (or is inefficient) until ADDBA exchanges complete
  Most gains can be achieved with simple exchange of semi-static parameters only (see next slides)
SCS
  Disruption to QoS-sensitive flows might occur if there is a delay in re-establishing SCS state after roam
  SCS parameters are generally semi-static so can be transferred over the DS with minimal downside
    e.g. any changes to SCS agreements after a context exchange has been initiated would be lost
MSCS
  Similar considerations to SCS, but should allow current derived MSCS rules (IP tuple->UP) at serving AP MLD to be transferred to target AP MLD, in addition to the (semi-static) contents of MSCS Descriptor
Note: If other TID assignment policies exist (e.g. based on DPI), they should also be transferred to target AP MLD in a proprietary manner
- If TID assignment of packets is different on serving and target AP MLDs, any attempts to preserve the TID’s state (e.g. BA agreement) would be futile
Other MAC states (e.g. TWT)
  Maybe nice-to-have in theory, but complex to transfer synchronized timing state, and may need renegotiation
    e.g. conflict with existing TWT agreement at target AP MLD
    Generally less impactful on link performance even if state is not transferred and need to be reestablished

## Slide 12: Description of new capabilities Control plane context exchange (2)
Block ACK agreement parameters
  A ‘simple’ form of Block ACK agreement context exchange involves simply exchanging the existence of, and semi-static parameters of, the Block ACK agreements for each TID
    i.e. fields in ADDBA’s Block Ack Parameter Set field (TID, Block Ack Policy, Buffer Size, etc), BA Timeout
    Various low-complexity design options exist for this context exchange, e.g.
      lightweight context exchange over DS, OR
      lightweight context transfer from non-AP STA (e.g. embedded within protected roam setup exchanges), OR
      implicit setup with default (mandatory-support) parameters – can be “upgraded” later [no explicit transfer needed]
    In this design, dynamic parameters (e.g. WinStartR/B, WinEndR/B, scoreboard) would be reset
      The next slides show impact of this on retransmission, duplicate detection, and in-order delivery functions
        assuming “buffered data delivery” path described on previous slide
  A slightly more advanced form of Block ACK agreement context exchange additionally involves transferring WinStartB (*) for each uplink TID in real-time (e.g. in roam signaling)
    This has the same properties as above, but allows non-AP MLD implementations to continue to use already-allocated SN values for MSDUs in transmit queue
  The most ‘advanced’ form of Block ACK agreement context exchange involves also transferring the current scoreboard, and all WinStart/End values, maintained at AP MLD for each TID
    Described further in Annex; does not appear to provide sufficient gains to justify complexity
(*) Note: WinStartB of UL TID is the SN of the first MSDU not yet successfully received (and so not yet passed up to DS)

## Slide 13: Description of new capabilities Control plane context exchange (3)
DOWNLINK TID example
AP MLD1
AP MLD2
DS
non-AP MLD
switch
server: packets: 1, 2, 3, 4, 5, 6, 7, 8
packets: 1, 2, 3, 4
packets: 5, 6, 7, 8
Packet index | SN | Status
4 | 104 | ✅
3 | 103 | ❌
2 | 102 | ❌
1 | 101 | ✅
Packet index | SN | Status
8 | 3 | ✅
7 | 2 | ✅
6 | 1 | ✅
5 | 0 | ✅
Packet index | SN | Status
4 | 104 | ✅
3 | 103 | ✅
 | 102 | ❌
1 | 101 | ✅
Packet index | SN | Status
8 | 3 | ✅
7 | 2 | ✅
6 | 1 | ✅
5 | 0 | ✅
Retransmissions
  Retransmission of DL packets from serving AP MLD1 (i.e. packet index 2) is handled by “buffered data delivery” path
Duplicate detection
  There is no issue with duplicate transmission of the same DL packets by AP MLD1 and AP MLD2, since DS forwards a given packet to one AP MLD or the other; therefore, duplicate detection (e.g. packet 3) can be handled for each AP MLD separately
In-order delivery
  Packets sent by DS to AP MLD1 are presumed older than packets sent by DS to AP MLD2; therefore non-AP MLD can ensure in-order delivery by delivering all packets from AP MLD1 (1 thru 4) to higher layers [unless those packets reach retry/lifetime limits, or non-AP MLD “gives up” on the packets] prior to delivering any packets from AP MLD2
Note: “Packet index” is simply an index that indicates the order of the packets sent by higher layers (it does not refer to PN)

## Slide 14: Description of new capabilities Control plane context exchange (4)
UPLINK TID example
AP MLD1
AP MLD2
DS
non-AP MLD
switch
Packet index | SN | Status
4 | 104 | ✅
3 | 103 | ✅
2 | 102 | ❌
1 | 101 | ✅
Packet index | SN | Status
8 | 3 | ✅
7 | 2 | ✅
6 | 1 | ✅
5 | 0 | ✅
Packet index | SN | Status
4 | 104 | ✅
3 | 103 | ❌
2 | 102 | ❌
1 | 101 | ✅
Packet index | SN | Status
8 | 3 | ✅
7 | 2 | ✅
6 | 1 | ✅
5 | 0 | ✅
Retransmissions
  If a UL packet is not Ack’d by AP MLD1 (e.g. packet 2), the non-AP MLD re-sends it “fresh” to AP MLD2
Duplicate detection
  There is a small risk of undetected duplicates, e.g. non-AP MLD might re-send packet 3 to AP MLD2 because the Ack from AP MLD1 was not received; resulting in both AP MLDs forwarding the packet to the DS (although STAs could do the same today)
In-order delivery
  Option 1: Regular behavior by AP MLD1 (i.e. packets 3-4 will not be forwarded to DS because packet 2 is pending retransmission). Non-AP MLD freshly re-sends all packets that are ahead of any un-Ack’d packets to AP MLD2 (i.e. packets 2-4)
  Option 2: AP MLD1 releases packets ahead of any un-Ack’d packets (i.e. packets 3-4) once roam completes, then signals (over DS) to AP MLD2 that it can release newly received packets to the DS; non-AP MLD drops earlier un-Ack’d packets (packet 2)
server

## Slide 15: Security considerations Concerns with other proposals of sharing PTK across network
A number of other submissions have proposed sharing the PTK across AP MLDs in the network
  Even though, as shown on previous (and later) slides, efficient derivation of a new/unique PTK on each roam is possible without compromising roam performance
  Note that PTK compromise allows the attacker to passively decrypt, or actively inject or modify packets
    e.g. see Appendix A “Importance of Uniqueness Requirement on IVs” of NIST SP 80038D [5]
  There is an expectation that new versions of technologies improve security, and certainly avoid regressions
  Several concerns with PTK sharing are highlighted in these slides:
(A) Regression in key hygiene / key separation
  In all RSN security mechanisms in baseline, there is a clear key hierarchy, and a PTK is a pairwise secret
    Between a given AP and non-AP MLD
    If a PTK is compromised, there is no impact on security of the connection between the non-AP MLD and any other AP MLD
      Note: PTKs are designed as short-term pairwise secrets because they directly encrypt traffic sent over the air, and therefore are particularly vulnerable to attack
    PTK sharing is not comparable to PMK Caching - since PMK is a key-generating key, not an encryption key
      also note in 802.11, PMK caching is only defined for use with the same AP MLD (so-called OKC is proprietary)
  On the contrary, in other proposals in which it is suggested the same PTK is used as a non-AP MLD roams across many AP MLDs in the network, knowledge of the PTK is shared by many parties
    In a “push” model, N + 1 entities know the PTK, where N is # AP MLDs in the “seamless roaming” domain
    In a “pull” model, M +1 entities know the PTK, where M is # AP MLDs that non-AP MLD connects to during PTK lifetime
  This increases the attack surface and risk, for PTK to be compromised by some implementation vulnerability
    Such vulnerabilities might be related to over the air transmissions between the non-AP MLD and any AP MLD, or might be related to the transport and/or synchronization between all the AP MLDs with which the PTK is shared

## Slide 16: Security considerations Concerns with other proposals of sharing PTK across network (2)
(B) Regression in competitive positioning with respect to alternative technologies
  3GPP defines concept of “forward security” for roaming (aka handover) in 5G RAN (see [6] and Annex slide)
  Data plane encryption key KUPenc (equivalent to TK component of PTK) is derived by KDF from base-station specific key KgNB (roughly equiv. PMK-R1)
    KUPenc is a pairwise secret between ME (equiv. non-AP MLD) and gNB (equiv. AP MLD)
    KgNB is a pairwise secret between ME and AMF (within core network; for initial connection) or source gNB (for handover)
  For “vertical” handover, new KgNB is derived (via intermediate key NH) from root key KAMF (equiv. PMK-R0)
    KAMF is a pairwise secret between ME and (source) AMF
    NH is a secret of three parties – ME, AMF and source gNB
    Provides “forward security” for KgNB – i.e. if a KgNB is compromised, all other past and future KgNB are still secure
  For “horizontal” handover, new KgNB is derived by KDF from previous KgNB
    Does not provide full “forward security” for KgNB, although an older KgNB can’t be derived from a compromised newer KgNB
  In both handover cases, KgNB (and, therefore, the encryption key KUPenc) is unique after each handover
    “PTK sharing” (i.e. sharing of KUPenc) is never used, so no issues with nonce reuse across multiple handovers
    “PMK sharing” (i.e. sharing of KgNB) across base stations is never used either
  3GPP handover security properties have been the subject of significant academic research studies, e.g. see [7]
    Expect UHR seamless roaming to be of similar interest; researchers will stress-test implementations for vulnerabilities

## Slide 17: Security considerations Concerns with other proposals of sharing PTK across network (3)
(C) Complexity and slow roams with existing FT deployments in mixed-technology networks
  Network deployments with mixed-technology APs (UHR and non-UHR) are likely to exist
  Since FT is already widely deployed, it is expected it will continue to be used – both for legacy (non-UHR) STAs / non-AP MLDs, and also for UHR non-AP MLDs when connecting to non-UHR APs in the network
  In an FT-based seamless roaming design, UHR enhancements (e.g. tunneled OTDS, context exchange triggers) can be used seamlessly together with legacy FT operations in the same MD
  However, in a “shared PTK” design – assuming it uses a separate (non-FT) key hierarchy and AKM – separate full authentication procedures for UHR and FT would be required
    Implies roam performance degradation when the second key hierarchy is established, e.g. see figure below
    Also requires STA to maintain both key hierarchies
UHR AP MLD1
UHR AP MLD2
non-UHR AP MLD3
non-UHR AP4
non-AP MLD
context exchange
FT key (PMK-R1) distribution (FT domain)
UHR key distribution (UHR domain)
Initial connection at (1)
- “Shared PTK” initial assoc
Roam 12
- FT Initial Mobility Domain assoc
Roam 23
- FT protocol roam
Roam 34
- “Shared PTK” roam
Roam 41
- “Shared PTK” roam
1
2
3
4
Initial connection
Roam 1 2 is a “slow” procedure including 4-way handshake

## Slide 18: Security considerations Concerns with other proposals of sharing PTK across network (4)
(D) Risk of nonce reuse from flawed PN context exchange or management across AP MLDs
  In order to use the same PTK across all AP MLDs, the PTKSA needs to be included in the context exchange
  It is essential that the IV/nonce (i.e., for GCMP, A2 || PN) is never reused with the same PTK
    Note: A2 is the TA (or the MLD address for unicast frames between MLDs)
    This means a given MLD must never reuse a PN with the same PTK
    Note: Nonce reuse with GCMP can allow attacker to decrypt, replay and bidirectionally forge packets
  In the uplink, it can be assumed the non-AP MLD implementation avoids PN reuse for the entire PTK lifetime
  However, in the downlink, when a roam occurs back to the same AP MLD as used previously, PN reuse in downlink must be strictly avoided since A2 will return to the same value as before. This implies one of the following:
    the AP needs to maintain state of previously used PN ranges with a given PTK, even after non-AP MLD roams away, or
    the PN needs to be synced/transferred across AP MLDs as part of context exchange, e.g.
      “last PN” is transferred, and first PN used by next AP MLD is equal to {last PN + N}, or
      part of PN space is assigned to a “roam counter”, which is transferred and incremented on each roam
  Any of these approaches are particularly fragile to imperfect implementations, e.g.
    e.g. synchronization race conditions, improper coordination, loss/reset of state due to power outage/crash
    compare to baseline (per-UHR) case where a single entity is responsible for avoiding PN reuse and handling rekeying
  Several examples of potential vulnerabilities are shown in the next slides:
  Note that designs in which PTK rekeying is attempted some time (shortly) after the roam do not mitigate the issue
    e.g. attacker can try to cause the rekeying or roam to fail, resulting in continued use of the same PTK and/or roam back to the original AP before rekeying is successful

## Slide 19: Security considerations Concerns with other proposals of sharing PTK across network (5)
  Some examples of potential nonce reuse fragility are shown on the next slides
    Note: These are a limited set of examples. A design that addresses these particular cases is not necessarily robust against other similar-but-different scenarios or attacks
  For the purpose of these examples, some assumptions are made on signaling/design using a shared PTK:
    Non-AP MLD can initiate roam by signaling to either (a) Serving AP MLD or (b) Target AP MLD
    In case (a), Context Exchange (CX) is included with tunneled add link request to target AP MLD, and acknowledged by target AP MLD in the response
    In case (b), a context exchange request is included with tunneled delete link request to target AP MLD, and CX is included with tunneled delete link response
non-AP MLD
AP MLD2
AP MLD1
LLC XID to DS (update switch port mapping for non-AP MLD)
Roam Request/Response (e.g. UHR Add Link Reconfig)
Downlink data path
Context Exchange (CX) [includes PN for shared PTK]
AddLinkReq(MLD2)
DelLinkReq(MLD1)
Uplink data path
X
Downlink PN = X
TUN{AddLinkReq(MLD2)}
CX(PN)
RoamID
Roam Request/Response tunneled over DS between AP MLDs
TUN{AddLinkResp(MLD2, SUCCESS)} RoamID
AddLinkResp(MLD2, SUCCESS)
DelLinkResp(MLD1, SUCCESS)
AddLinkReq(MLD2)
DelLinkReq(MLD1)
AddLinkResp(MLD2, SUCCESS)
DelLinkResp(MLD1, SUCCESS)
TUN{DelLinkReq(MLD1)}
CXReq
RoamID
TUN{DelLinkResp(MLD1, SUCCESS)}
CX(PN)
RoamID
Assumed AP MLD1AP MLD2 Roam signaling for shared PTK
(a) via Serving AP
(b) via Target AP
Each CX exchange is referenced to a (unique/random) RoamID in tunneled Request and Response over the DS
If CX is not completed, Add Link Resp. status = failure
On each roam, downlink PN in CX is equal to last used PN + N (where value N might be large)
Note: These assumptions are based on a design that tries to mitigate/avoid basic nonce reuse issues

## Slide 20: Security considerations Concerns with other proposals of sharing PTK across network (6)
non-AP MLD
AP MLD2
AP MLD1
Switch (on DS)
0
100
105+N
105
100+N
  Nonce reuse fragility: Example (1)
    “Delayed / out-of-order CX”
    Non-AP MLD initiates roam by signaling to Target AP MLD (AP MLD2)
    AP MLD2 requests CX from serving AP MLD1
    However, the CX response is delayed on the DS, so AP MLD2 does not respond to non-AP MLD (or sends Failure response)
    In the meantime, while processing the DelLinkReq, AP MLD1 sent a few more packets to non-AP STA that were already queued for delivery
    Non-AP MLD tries the roam again
    This time, AP MLD2 requests and receives CX from AP MLD1 (with slightly increased PN), sends Success response to non-AP MLD, roam completes, and sends DL frames using new PN
    Shortly after, the original delayed CX response is received by AP MLD2
    AP MLD2 incorrectly accepts and updates the current PN with the PN in the delayed CX, since it did not internally invalidate the original RoamID in time. This causes subsequent packets to be sent using nonce that was used a few packets earlier (PN=105+N, ...)
AddLinkReq(MLD2)
DelLinkReq(MLD1)
TUN{DelLinkReq(MLD1)}
CXReq
RoamID=1
TUN{DelLinkResp(MLD1, SUCCESS)}
CX(PN=100+N)
RoamID=1
AddLinkResp(MLD2, SUCCESS)
DelLinkResp(MLD1, SUCCESS)
TUN{DelLinkResp(MLD1, SUCCESS)}
CX(PN=105+N)
RoamID=2
TUN{DelLinkReq(MLD1)}
CXReq
RoamID=2

## Slide 21: Security considerations Concerns with other proposals of sharing PTK across network (7)
non-AP MLD
AP MLD2
AP MLD1
Switch (on DS)
0
  Nonce reuse fragility: Example (2)
    “Ping-pong roam race condition”
    Non-AP MLD roams from AP MLD2 to AP MLD1
    Some time later, non-AP MLD initiates roam to AP MLD2 by signaling to Serving AP MLD (AP MLD1)
    Before Serving AP MLD1 has processed the request, the non-AP MLD changes its mind due to RSSI change and sends request to the Serving AP MLD to return back to AP MLD1
    The first request causes AP MLD1 to send CX to AP MLD2, while the second request causes AP MLD2 to request CX from AP MLD1. These two messages are received by AP MLD2 about the same time. AP MLD2 sends CX back to AP MLD1 containing the same PN as when the prior roam happened (i.e. without having yet updated its internal PN based on the incoming CX).
    AP MLD1 receives the CX, sends success response back to non-AP MLD, and updates its PN based on the CX.
    When AP MLD1 continues sending packets to non-AP MLD, it reuses nonce values that it used when the non-AP MLD first roamed to it.
TUN{DelLinkReq(MLD2)}
CXReq
RoamID=2
TUN{DelLinkResp(MLD2, SUCCESS)}
CX(PN=50+N)
RoamID=2
AddLinkResp(MLD1, SUCCESS)
DelLinkResp(MLD2, SUCCESS)
TUN{AddLinkReq(MLD2)}
CX(PN=100+2N)
RoamID=1
AddLinkReq(MLD2)
DelLinkReq(MLD1)
AddLinkReq(MLD1)
DelLinkReq(MLD2)
50+N
100+N
50+N
50

## Slide 22: Security considerations Concerns with other proposals of sharing PTK across network (8)
non-AP MLD
AP MLD2
AP MLD1
Switch (on DS)
L
  Nonce reuse fragility: Example (3)
    “Distributed responsibility for rekeying”
    Non-AP MLD has been connected to AP MLDs in the network for some significant period of time, and the PN has reached some large value L
    The AP MLDs in the network are configured with a consistent threshold for PN exhaustion warning (dot11PNWarningThreshold), which triggers them to initiate a PTK rekey
    Non-AP MLD initiates roam from AP MLD1 to AP MLD2 just before the warning threshold PN value is reached
    The PN value exactly equal to the warning threshold is used by AP MLD1 to deliver already-buffered packets. Since AP MLD1 has already sent CX to AP MLD2, it assumes AP MLD2 will handle rekeying.
    However, the first PN value used by AP MLD2 (incremented by N) is already greater than the threshold and does not trigger AP MLD2 to rekey either
    As a result, the APs continue to increment the PN until it wraps around, resulting in nonce reuse when non-AP MLD roams back to the same AP MLD it used on first connection
AddLinkReq(MLD1)
L+50+N
L+50
L+150
L+90
PN=dot11PNWarningThreshold
TUN{AddLinkReq(MLD2)}
CX(PN=100+2N)
RoamID=1
AddLinkResp(MLD2, SUCCESS)
TUN{AddLinkResp(MLD2)}
RoamID=1
PN>dot11PNWarningThreshold
0

## Slide 23: Proposed extensions to FT protocol Background - baseline FT (11r) protocol
non-AP MLD
AP MLD2
AP MLD1
s1
s1
s4
s4
State 4 (s4) data path with AP MLD1
State 4 (s4) data path with AP MLD2
s2
s3
SAE/EAP/OWE(*) auth
FT Initial MD Assoc
4-way
FT Auth (OTA or OTDS)
FT reassoc (AP MLD2 opens 802.1X port)
It is proposed that the security framework and new capabilities for roam signaling, as described in earlier slides, are designed as enhancements to FT protocol
Baseline FT (11r) protocol already meets some of the requirements for seamless roaming
  Non-AP MLD always has exactly one full “state 4 connection” to the DS
    Note: State 4 with AP MLD1 remains until Reassoc Resp received from AP MLD2 (see 12.3.5.4; Annex)
  New PTK derivation (with AP MLD2) occurs while still associated to serving AP MLD1
    Note: New PTK is derived from AP MLD2’s PMK-R1. and SNonce/ANonce exchanged in FT Auth frames
    Note: Reassoc Req/Resp just contain MIC (CMAC/HMAC using PTK-KCK) to confirm the PTK liveliness
      AP MLD2’s PMK-R1 is derived by AP MLD1 (R0KH **) from the PMK-R0, and securely transported over the DS to AP MLD2
      MIC protection means roam failure scenarios caused by PMF protection mechanisms (SA Query) are avoided
s2
(*) FILS auth in FT Initial MD Assoc is also supported (no 4-way needed)
initial auth/assoc to AP MLD1
roam to AP MLD2
(**) R0KH is part of Authenticator, performed by AP’s SME (see 3.1, 4.10.1)

## Slide 24: Proposed extensions to FT protocol Background – baseline FT (11r) protocol (2)
Higher-layer procedures that could delay connectivity after roam are skipped
  e.g. skip DHCP and ARP to gateway’s IP; since AP MLDs in FT Mobility Domain are known to be on same DS
New PTK key derivation is not in critical path, does not contribute to connectivity outage
  Particularly for OTDS case, since FT authentication frames are sent via serving AP MLD1 without need to go off-channel (when AP MLD1 and AP MLD2 are non-co-channel)
  New PTK is derived prior to non-AP MLD changing its point of connection to DS
Choice of OTA and OTDS mechanisms allows optimization for the roam scenario
  e.g. OTDS is generally preferred when link quality with serving AP MLD1 is still good, but OTA might be preferred if the link quality with serving AP MLD1 is already poor (or non-existent) at the time roam is triggered
FT defines a clear security key hierarchy with well-bounded roles for each key holder, e.g.
  the PMK-R0 is a pairwise secret between one AP MLD (the R0KH) and the non-AP MLD
  each PMK-R1 is a secret of only 3 entities: the R0KH, the corresponding AP MLD (R1KH), and non-AP MLD
  each PTK is a pairwise secret between the corresponding AP MLD and non-AP MLD
Flexible and scalable options for implementing security key distribution across APs
  “push” model – R0KH proactively generates PMK-R1s for all APs in Mobility Domain and pushes to the APs
  “pull” model – R0KH generates PMK-R1 for a given AP either proactively or on-demand, and provides it to a given AP on request (e.g. when STA initiates roam to target AP)
  even in large Mobility Domains (N x AP MLDs) where PMK-R1s are proactively generated (e.g. in central controller), computational complexity (N x KDFs *) and storage requirements are low
(*) In an experiment using open-source AP daemon hostapd, derivation of PMK-R1s (wpa_derive_pmk_r1()) for 1000 APs took only 7 ms

## Slide 25: Proposed extensions to FT protocol Performance of existing baseline FT implementations
AP1
AP2
DS
STA
Experimental setup (as an example of behavior)
APs
  Both APs operate on same channel, advertise same FT MD
  Based on commodity Wi-Fi chipset modules, open-source host daemon (*)
  TxBF and MU disabled
STA
  (STA-A): Commercial smartphone
  (STA-B): Reference Wi-Fi module with minor experimental driver optimizations
  Static IP assignment
Data traffic
  Bidirectional iperf isochronous flows between STA and bridge on DS (small packets every 1ms)
  Target AP sends LLC XID packet to DS with SA=STA_MAC, to update DS mapping when FT Reassoc Resp is Ack’d
    i.e. DL frames will be forwarded to AP2 even before STA sends its first data packet to AP2 in uplink
Security / Roaming
  FT-SAE OTDS; BTM-triggered (also, for STA-B, Supplicant-triggered)
sniffer
(TSF timestamped)
switch
  packet capture (on switch)
(*) Trunk hostapd as of April 2024, https://w1.fi/cgit/hostap/log/

## Slide 26: Proposed extensions to FT protocol Performance of existing baseline FT implementations (2)
BTM Req/Resp
FT Action (Auth Req/Resp)
STA
AP2
AP1
STA-A (commercial smartphone)
BTM-triggered
FT Reassoc Req/Resp
4 ms
3 ms
47 ms
5 ms
ADDBA
5 ms
2 ms
36 ms
Note: Data paths are only shown if the Tx frames captured by sniffer are ACK’d by receiver and appear in Rx interface capture
Probes
UL
DL
UL
DL
7 ms
12 ms

## Slide 27: Proposed extensions to FT protocol Performance of existing baseline FT implementations (3)
FT Action (Auth Req/Resp)
STA
AP2
AP1
STA-B (reference Wi-Fi module with minor experimental driver optimizations)
BTM-triggered
FT Reassoc Req/Resp
4 ms
19 ms
7 ms
ADDBA
Probes
UL
DL
11 ms
10 ms
2 ms
Note: Data paths are only shown if the Tx frames captured by sniffer are ACK’d by receiver and appear in Rx interface capture
BTM Req/Resp
16 ms
1 ms
DL
UL
Experimental optimizations:
  Delay suspending of uplink data FIFO until the short period during FT Reassociation state changes
  Delay canceling packet filter for serving AP’s BSSID until FT Reassociation

## Slide 28: Proposed extensions to FT protocol Performance of existing baseline FT implementations (4)
FT Action (Auth Req/Resp)
STA
AP2
AP1
STA-B (reference Wi-Fi module with minor experimental driver optimizations)
Supplicant-triggered
FT Reassoc Req/Resp
4 ms
15 ms
6 ms
ADDBA
Probes
UL
DL
UL
DL
7 ms
6 ms
1 ms
Note: Data paths are only shown if the Tx frames captured by sniffer are ACK’d by receiver and appear in Rx interface capture
Note: In this supplicant-triggered case, target BSSID’s channel is not specified in roam trigger; STA does full scan prior to roam decision
(off-channel probes – 100+ ms)

## Slide 29: Proposed extensions to FT protocol Performance of existing baseline FT implementations (5)
Observations from experimental results with existing commercial implementations:
  Connectivity outage during roam broadly consistent with previous results in literature, e.g. 40-70 ms (e.g. [3])
  The time for STA (host) to make roam decision based on BTM Request is significant, but not in the critical path
  Uplink traffic stops several 10s of ms before FT Reassoc exchange
    This is because typical STA drivers/supplicants suspend data path with serving AP (e.g. suspend Tx FIFO, clear A2 Rx filter, block 1X controlled port, and/or delete PTK), during process of authenticating/reassociating with the target AP
      This is not required by the standard – see Annex excerpts
  As expected, serving AP maintains PTK (and active interface) until (after) the roam is complete
  Traffic with target AP does not begin until ADDBA exchanges are complete, however ADDBA signaling overhead per-se does not dominate the delay (from Reassoc Resp until first data frames)
    Note – the time taken for host to install key in driver/hardware can be significant. Some host implementations attempt to install the key as soon as FT Authentication is complete (i.e. prior to reassociation), but this is not supported by many existing drivers (e.g. see open-source examples below of host FT key installation functions)
With minor STA-side optimizations, outage is reduced to ~12 ms (half of which is due to ADDBA setup) and can be optimized further
With optimized implementations, the perception of FT as “non-seamless” (e.g. [4]) would not exist
hostapd
wpa_supplicant

## Slide 30: Proposed extensions to FT protocol New roam signaling capabilities as extensions to FT protocol
s4
FT Auth
FT Reassoc
s2
non-AP MLD
AP MLD2
AP MLD1
s4
FT Auth
FT Reassoc
s2
The new roam signaling capabilities described on earlier slides can be implemented as relatively simple extensions to FT protocol as follows:
(1) Extend FT OTDS to allow Probe Request/Response and FT Reassociation Request/Response frames to also be sent over-the-DS to the target AP MLD
  Since both FT Auth and Reassoc frames are encapsulated in FT Action frames, fingerprinting privacy is ensured
  Allow OTDS Reassoc Response to also be duplicated OTA by target AP MLD
    to avoid stranding non-AP MLD if link with serving AP MLD fails during the exchange (i.e. non-AP MLD moves to target AP MLD’s channel)
  Consider allowing deferral of DS data path mapping, and deferral of terminating assoc state with serving AP MLD, until a direct OTA exchange with target AP MLD is complete
    to avoid stranding non-AP MLD if link quality with target AP MLD has not yet been confirmed and is too weak
  Note: Can reuse existing RRB transport used for FT Authentication frames in baseline FT OTDS
Baseline FT OTDS
UHR FT Auth+Reassoc OTDS
(tunneled) probe

## Slide 31: Proposed extensions to FT protocol New roam signaling capabilities as extensions to FT protocol (2)
(2) Use the dedicated UHR Management Privacy Key (PTK-PRIV) to encrypt over-the-air FT Authentication and Reassociation frames
  Note: As mentioned earlier, we cannot assume an OTDS mechanism can always be used
    e.g. if link quality to serving AP is already poor/nil when roam trigger occurs (see diagram in Annex), or if non-AP MLD is anyway going off-channel to obtain RSSI
  Note: For privacy protection of the Initial MD association, mechanisms being defined in 11bi might be used
(3) Bundle signaling to trigger context exchange and DS mapping update in FT Auth / Reassoc frames
  e.g. by inclusion of additional elements
  if needed, minimum number of messages can be reduced to 3 by bundling FT Auth and Reassoc contents
    e.g. (1) FTAuthReq(SNonce) || FTReassocReq ; (2) FTAuthResp(ANonce, MIC) || FTReassocResp; (3) FTConf(MIC)
    note all messages are protected either by PMF (OTDS) or PTK-PRIV
  note, even in a “shared PTK” design, multiple messages are required during roam procedure to trigger context exchange, DS mapping update, deliver group keys, etc
(4) To ensure implementations maintain an active dath path throughout the roam procedure
  UHR non-AP MLD is required to maintain the existing PTKSA with serving AP MLD until (at least) the time that reassociation with target AP MLD completes
    Non-AP MLD should also maintain active data flow (Tx FIFO, packet filters, 1X port) with serving AP MLD during this time
    If “buffered data delivery” is used, PTKSA with serving AP MLD would be maintained until this is complete
  Implementations should install PTK in driver ready for use as soon as it is derived (after FT Auth)
  After roam, data path should be unblocked even if other exchanges (e.g. sounding) are still pending completion

## Slide 32: Proposed extensions to FT protocol .... but you said (FT) “reassociation”!
In other submissions, various rationales have been discussed for “avoiding reassociation” due to non-seamless reassociation behavior observed in baseline implementations
  However, all those issues are addressed by the FT enhancements proposed in the previous slides
  i.e. enhanced FT reassociation with context transfer has the same seamless performance as other proposals
Support for context transfer can be added to baseline reassociation procedures with simple changes
  i.e. in 11.3.5.4, the list of “states, agreements, and allocations [that] shall be deleted or reset to initial values” would be modified such that parameters exchanged in the context exchange would instead be maintained
On the other hand, adding support for roaming between AP MLDs to other mechanisms such as ML Reconfiguration would involve substantially more work and duplication of implementation effort
  ML Reconfiguration is currently only defined for adding/removing links to the same AP MLD, not for adding/removing links with a different AP MLD with separate MAC SAP, MLD MAC state management, etc, hence various reassociation concepts would need to be ported to this mechanism, e.g.
    rules for opening/closing 802.1X controlled port
    association state management, and associated Tx/Rx rules for each class of frames
    roam failure handling, e.g. rules for roam rejection based on MLD-level capabilities and policies
  In addition, fundamental MLO concepts that currently apply when a new link is added (e.g. STR/eMLSR, TID-to-link mapping) would not apply across the links of the serving and target AP MLDs
  To avoid confusion, it is better to not override ML Reconfiguration and instead enhance existing and mature reassociation rules as needed

## Slide 33: Summary
High-level requirements for UHR seamless roaming have been proposed
  both with regards to roam triggers and roam signaling/execution
New capabilities to achieve these requirements have been described
Details of context transfer in data and control planes have been discussed and proposed
Security framework requirements have been discussed
  with a caution against some alternative proposals to share PTK(SA) across multiple AP MLDs
  all seamless roaming requirements can be achieved without taking such risks
A high-level design for these new capabilities as an extension of FT protocol has been proposed
  Avoid regression in security characteristics and concerns on new attack vectors
  Extensible existing signaling (e.g. to trigger context exchange, DS mapping update)
  No need to define new concepts such as “SMD association”, “non-collocated” or “virtual” AP MLDs, add/delete link pertaining to a different AP MLD, or make changes to addressing
  Seamless integration of UHR roaming into existing mixed-technology FT networks

## Slide 34: Annex: Considerations on data transfer over the DS
A potential alternative approach to data plane “buffered data delivery” from serving AP MLD is for the already-buffered DL data to be transferred from serving AP MLD to target AP MLD over the DS, and then transmitted by target AP MLD after the roam
This is already (theoretically) a network implementation option today, i.e.
  serving AP MLD gathers MSDUs from its Tx buffers, send over some secure data tunnel on DS between AP MLDs (or via controller), and target AP MLD transmits
Some optimizations could be possible to ensure in-order DL delivery
  i.e. by also transferring (more of) the Block Ack context
Unlikely for mass-market adoption, but could be attractive in certain deployments e.g. enterprise
  Higher AP MLD implementation complexity: Implementation involves multiple data queues at different levels of the stack (e.g. within OS kernel, driver, hardware, etc). Extracting buffered data from those queues in order to transfer it to another AP MLD is non-trivial
  Implies secure data paths need to be established pairwise between every AP MLD in the network, or data is sent via a central controller with additional backhaul and processing overhead
Note: Any data transfer is likely to be of MSDUs (or possibly plaintext MPDUs), not encrypted MPDUs
  Most buffered data is within larger OS kernel queues
  Most AP MLD implementations perform MPDU encryption in hardware immediately prior to transmission
    Note: While certain network architectures currently use centralized encryption engines, these are not in the majority and on-chip encryption is expected to become even more dominant as data rates continue to increase
Should remain an implementation option without requiring significant formal support in the standard

## Slide 35: Annex: Considerations on full BA agreement context transfer
  The most ‘advanced’ form of Block ACK agreement context exchange involves also transferring the current scoreboard, and all WinStart/End values, maintained at AP MLD for each TID
    The description below is with respect to the figures in earlier slides on Block ACK context transfer
    This could help avoid the small possibility of UL duplicates
    However, it would not help with either of the following issues:
      end-to-end out-of-order DL delivery if the switching of DS data interface from AP MLD1 to AP MLD2 is “glitchy”
        i.e. if some packets the DS forwards to AP MLD2 are older than some packets the DS forwards to AP MLD1
        since SN assignment at each AP MLD is based on order of arrival of MSDUs at that AP MLD, the order of packets in terms of SN might not be the same as the original order of packets from the source
      inefficiencies in ensuring UL in-order delivery to the DS (see previous slide)
        e.g. even if non-AP MLD retransmits packet 2 to AP MLD2 using the original SN (102) and the full BA context is shared, it would require real-time coordination between the two AP MLDs to ensure AP MLD2 forwards packet 2 to the DS prior to AP MLD1 forwarding packets 3-4 to the DS
          in cases where the scoreboard has multiple holes, the two APs would need to coordinate to round-robin forward MSDUs to the DS in SN order, which would be extremely inefficient
        ... and even if this could be done, it would not necessarily ensure end-to-end in-order UL delivery since the DS paths from AP MLD1 and AP MLD2 to the gateway may have different delays
        Note: The in-order delivery requirement per TID applies at the 802.11 layer (not explicitly to the gateway)
    In addition, full BA context exchange implies need to suspend the uplink data path while it is transferred
      The goal should be to avoid significant data outage during roam, even if the probability of UL packet duplication of out-of-order delivery to the gateway is slightly increased

## Slide 36: Annex: Considerations on utility of retrieving buffered DL data from (previously) serving AP
In non-real-time use cases (e.g. downloads, buffered audio/video), the buffered data might often be usable by the application, but it might be more efficient for the packets to be dropped and higher-layer retransmissions (e.g. TCP, QUIC) be invoked
  Particularly where retrieval of the packets involves off-channel operations that disrupt new link
  However there may be exceptions - e.g. on end-to-end links with high bandwidth-delay product, or highly constrained northbound links, the impact of TCP congestion window collapse due to dropped packets could be significant
In real-time use cases (e.g. conversational or XR audio/video), the buffered data might often be “stale” due to newer data already being transferred with the target AP MLD
  For example, if a new VoIP packet has already been received from the target AP MLD, then in principle buffered data that contains previous VoIP packets is useless since the codec would have already reconstructed the missing packets
  In addition, under the current in-order delivery requirements, the new VoIP packet would not be delivered to the higher layers until the older packets are retrieved, effectively further increasing the number of missing (or late) packets at the codec
  However some important exceptions may exist - e.g. if the buffered data contains a video I-frame, it may be needed to render subsequent P-frames
  For such cases, it should be possible for the non-AP MLD to opt-in to out-of-order delivery of the corresponding TID, so that retrieval of the (potentially useful) buffered data does not delay delivery of the most recently received data in the same TID

## Slide 37: Annex: 3GPP 5G handover key handling
(from [6])
vertical handover
horizontal handover

## Slide 38: Annex: Challenges with roaming triggers
AP1 [p]
AP2 [t]
STA
STA
AP3
6 GHz
2.4GHz
2.4GHz
2.4GHz
6 GHz
6 GHz
A STA in mobility can rapidly move out of coverage of serving AP (depending which bands it has active links with)
Since it cannot always be guaranteed a clear roam target can be determined while the link quality with serving AP remains good, there is a need to support both OTDS and OTA roaming mechanisms

## Slide 39: Annex: Relevant excerpts from REVme D5.0
(12.2.5)
(12.5.4.3.1)
(12.3.5.4)
(11.3.5.4)
(13.7.1)

## Slide 40: References
[1] IEEE 802.11-23/1884r2 Seamless Roaming SPs, D. Ho et al, Jan 2024
[2] IEEE 802.11-23/2157r2 Seamless Roaming within a Mobility Domain, B. Gupta et al, Nov 2023
[3] Performance Study of Fast BSS Transition using IEEE 802.11r, S. Bangolae et al, 2006
[4] IEEE 802.11-23/1908r2 Seamless Roaming Procedure, Y. Yoon et al, Nov 2023
[5] NIST SP 800-38D “Recommendation for Block Cipher Modes of Operation: GCM and GMAC”
[6] 3GPP TS 33.501 V18.4.0
[7] https://people.inf.ethz.ch/rsasse/pub/5G-handover-WISEC21.pdf