## Slide 1: TGbi – Epoch Structure Proposal
Date: 04-10-2024
Authors:
Name | Affiliations | Address | Phone | email
Jerome Henry | Cisco |  |  | jerhenry@cisco.com
Domenico Ficara | Cisco |  |  | dficara@cisco.com
Ugo Campiglio | Cisco |  |  | ucampigl@cisco.com
Jarkko Kneckt | Apple |  |  | jkneckt@apple.com
Javier Contreras | Cisco |  |  | jacontre@cisco.com

## Slide 2: Epochs
11-24/0604 defines 2 types of epoch structures:
One (or more) group structure
Individual Structures
The AP can support multiple groups (different epoch periodicity)
After association and upon learning about the default and the other groups, the STA can:
Stay in the default group
Request to join another group
Request individual epoch

## Slide 3: Discovery Phase
Association Request[EPCE]
Association Response
Beacon, Probe Responses[EPCE]
Enhanced Privacy Capabilities (RSNXE)
10.71.2.1, 10.71.2.2
“I support group EDP”
“I support Individual STA settings”
10.71.2.1, 10.71.2.2
“I support group EDP”
“I support Individual STA settings”
AP signals support in beacons/probe responses
STA signals support in (re)association request
Bit | Information
8 | Group Epoch Support
9 | Individual Epoch Support

## Slide 4: Default Group Assignment
4-way handshake M3[EPE]
10.71.2.4
“I support group epoch”
(may or may not support Individual epoch)
If AP & STA supports group epoch -> STA is automatically assigned to the default group epoch 0
AP signals group 0 structure and AID scheme in M3 of 4-way handshake
4-way handshake [M4]
 | Element Id | Length | Element Id Extension | Group EDP Epoch
Octets: | 1 | 1 | 1 | 0 or 12
 | Smallest Anonymized AID | AID Range | Group Epoch Duration | Next Epoch | Reserved | Current Epoch Number
Bits: | 11 | 11 | 14 | 11 | 1 | 48
Enhanced Privacy element
Group EDP Epoch field
Group Epoch Length Unit subfield value | Group Epoch Length Unit time value (TBTTs) | Min Epoch Duration (w/default TBTT dur.) | Max Epoch Duration (approx.)
0 | 0.05 | 5.12 ms | 10.5 s
1 | 0.5 | 51.2 ms | 1 min 45 s
2 | 5 | 512 ms | 17 min 28 s
3 | 50 | 5.12 s | 2 h 54 min 41 s
4 | 500 | 51.2 s | 1 d 5 h 6 min 46 s
5 | 5000 | 8 min 32 s | 12 d 3 h 7 min 44 s
6 | Reserved |  | 
7 | Reserved |  | 
 | Group Epoch length Unit | Group Epoch Duration
Bits: | 3 | 11

## Slide 5: Other Groups Advertisement
AP advertises group epochs:
Advertisement after 4-way handshake
On demand advertisement each time a group changes.
See previous slide
 | Element Id | Length | Element Id Extension | Group Count | Group ID | Group EDP Epoch | Number of Participating STAs
Octets: | 1 | 1 | 1 | 1 | 1 | 12 | 3
TWT Group ID is 8 bits -> 254 groups (+default GID0);
(in 802.11-2020 for TWT, 7 bits (Fig. 9-689))
Enhanced Group Privacy Availability (EGPA) element
 | Participating STA Count | Participating STA percentage
Octets: | 2 | 1
Participating STA count: rhe number of STAs are currently in the group
Participating STA percentage: STAs in the group represent X% of all associated STA (e.g. 50 STAs in BSS, 10 in the group -> percentage = 20)
Action[EGPA]
10.71.2.4
“I support group epoch”
(may or may not support Individual epoch)

## Slide 6: STA’s Options
At association, STA that expresses support for group EDP receives the default group parameters (M3), then the other groups parameters (right after 4-way handshake)
STA can decide to stay in the default group -> no action required
STA can decide to join another group
STA can request its own epoch parameters
STA can request to not participate in any scheme
-> STA-specific epoch setting action frame exchange

## Slide 7: STA Specific Epoch Setting Exchange
At any time, STA can send the request:
If request is group target, EPE is not present
If group ID is 255 -> EPE present (AID section reserved, STA requests epoch parameters)
AP responds:
with okay (EPE present)
Can’t do (no can’t do -> EPE not present; can’t do what you ask, but can do this (EPE present)
STA-specific Epoch Setting element (SESE)
Action[SESE]
10.71.2.5
“I want specific epoch setting”
Action[SESE]
 | Element Id | Length | Element Id Extension | Dialog | Target Group ID | Group EDP Epoch
Octets: | 1 | 1 | 1 | 1 | 1 | 0 or 12
1: STA request
2: AP acceptance response
3: AP rejection response
4: STA request to ‘not’ participate in any group
5: STA request to ‘not’ participate in this group

## Slide 8: Collision Warning
STA and AP can compute in advance future epoch header parameters
(computation method out of scope for this contribution)
AP can foresee parameters (e.g., otaMAC) collision in future epoch between STA 1 and STA2
AP sends a collision warning frame to STA1 or STA2
“skip epoch 556 parameters, jump to epoch 557 parameters”

## Slide 9: otaMAC Collision Warning Exchange
At any time before the colliding epoch, the AP can send a warning:
In m epochs after this one, you may collide, skip epoch m and use epoch m+n settings at that time
STA responds:
with okay (will act as requested)
With rejection
otaMAC Collision Warning element (oMCWE)
Action[]
10.71.2.8
“avoid collision in 2 epochs”
Action[oMCWE]
Current epoch+m
 | Element Id | Length | Element Id Extension | Collisions Status | Colliding Epoch | STA-specific Epoch Number Offset
Octets: | 1 | 1 | 1 | 1 | 1 | 1
n
1: collisions warning
2: warning reject
0: Success (warning acknowledged, will act)

## Slide 10: Summary
This document summarizes the epoch steps described in 11-24/604
At association, a STA automatically joins the default epoch group, but can then opt to join another group, or get its own epoch parameters.

## Slide 11: Comparison With 11-24/0645r0
11-24/604
AP announces capability in probe responses/beacons, STA in (re)assoc request
STA is placed in auto-group by default (no negotiation needed)
After assoc, AP informs the STA of groups
STA can then leave default group to join other group, or request individual parameters
11-24/645
AP/STA capability announcement TBD
STA may start by sending its requested epoch parameters in (re)association request
STA can also start by sending EDP Sequence Request after assoc. AP can accept/decline/suggest override
AP can send group information to STA (after asssoc), STA seems to directly just apply the group settings
Without exchange, STA does not rotate parameters

## Slide 12: Comparison With 11-24/0645r0
11-24/604
Group and individual settings:
  Group membership or individual settings not limited in time (until STA leaves the group/requests different settings)
  All STAs in a group rotate at the same time
  Epoch duration can range from 1 TBTT to 1+ day
  AP can announce support for 0 or N groups
  STA join group of its choice, can change at any time
11-24/645
Group and individual settings:
  Group membership or individual settings either not limited in time, or only valid for N epochs
  STAs rotates at epoch boundaries +/- rand value
  Epoch duration can range to 65535 “units”
  AP can announce one group, STA silently applies group settings