## Slide 1: STA initiated TXOP Sharing via Unicast CF-End
Date: 2024/04/11
Authors:
Name | Affiliations | Address | Phone | Email
Pei Zhou | TCL | Building G1, TCL International-E City, Shenzhen, Guangdong, China. |  | zhoupei36@gmail.com
Yuxin Lu | TCL |  |  | 
Zhanjing Bao |  |  |  | 

## Slide 2: Introduction
In this contribution, we propose the mechanism and related rules to support a non-AP STA shares its obtained TXOP with associated AP through unicast CF-End frame.

## Slide 3: Re-cap: STA initiated TXOP Sharing
The following references (including but not limited to) proposed non-AP STA initiated TXOP sharing for 802.11bn
  [1] 11-23/0581, Non-AP initiated TXOP sharing,
  [2] 11-23/1847, Follow-up on a non-AP STA initiated TXOP sharing,
  [3] 11-23/1874, Reverse TXOP sharing proposed.
Benefits of non-AP STA initiated TXOP sharing: [3]
  Efficient resource utilization
  Low latency and control traffic prioritization
  QoS management
  …
Existing solution(s):
  [1] [2]: Control frame (could be a new variant trigger frame) transmitted by a non-AP STA
  [3]: The 802.11 specification changes required in UHR are minimal. They can simply be an extension of the 11be TXS modes 1 and 2.
  Drawback(s) of using Trigger (a new variant or MU-RTS TXS TF) frame:
  Trigger frame is too long and contains many unnecessary fields for non-AP STA’s TXOP sharing
  So far, 802.11 baseline doesn't support non-AP STA transmitting Trigger (a new variant or MU-RTS TXS TF) frame

## Slide 4: Re-cap: CF-End frame and Truncation of TXOP
The frame format for the CF-End frame is defined as below: [4]
  When transmitted by a non-DMG and non-S1G STA, the Duration field is set to 0.
  When transmitted by a non-DMG STA, the RA field is the broadcast address. When transmitted by a DMG STA, the RA field is the MAC address of the STA that is the intended immediate recipient of the individually addressed Data or Management frame, or the broadcast address.
  Truncation of TXOP [4]
  By transmitting the CF-End frame, the STA is explicitly indicating the completion of its TXOP.

## Slide 5: Proposal: Unicast CF-End frame for STA initiated TXOP Sharing
TXOP obtained by the non-AP STA
In 802.11bn, we propose to define the following new mechanism and rules to support STA initiated TXOP Sharing:
  Mechanism: Non-AP STA shares its obtained TXOP with associated AP by transmitting an unicast CF-End frame.
  STA rules:
    1) Non-AP STA sets the RA field of CF-End frame to a unicast address (i.e., AP’s MAC address);
    2) (Optional) When the RA field of CF-End frame is set to a unicast address (i.e., AP’s MAC address), the non-AP STA may indicate the shared TXOP duration in the Duration field of CF-End frame;
    3) The BSSID(TA) field is set to the non-AP STA’s MAC address.
  AP rules:
    1) When an AP receives a CF-End frame and finds that the RA field is equal to its MAC address (which means the RA is set to an unicast address, rather than a broadcast address), the AP assumes that the non-AP STA transmitting the frame announces to share its TXOP;
    Note: Only associated AP receives the unicast CF-End frame. Other STAs don’t assume the truncation of the current TXOP.
    2) (Optional) the duration of shared TXOP is signaled in the Duration field of the unicast CF-End frame;
    3) AP uses the shared TXOP to initiate new transmissions with other non-AP STAs SIFS (TBD) after the CF-End frame.
AP
3
Non-AP STA
CF-End frame (unicast)
0
Operations controlled by AP
TXOP shared by the non-AP STA
xIFS
PPDU
…
TXOP sharing

## Slide 6: Discussions and Next Steps
How does AP return the shared TXOP (if there is still remaining time)?
  Is it necessary to return?
    If not necessary, AP can simply broadcast CF-End frame to terminate the current TXOP and start new channel contention.
    If necessary, AP may use MU-RTS TXS TF (as defined in 11be) to share the remaining time to the “original” non-AP STA.
    How does non-AP STA indicate its shared bandwidth (channel)?
  By default, shared bandwidth = non-AP STA’s operation bandwidth
  Other methods TBD.
    How does AP expand more bandwidths (channels) than non-AP STA’s sharing?
  AP performs backoff on other channels
  AP performs PIFS CCA on other channels
  Other methods TBD.

## Slide 7: Straw Poll 1
Do you agree to add the following text to the TGbn SFD:
Non-AP STA can sharing it obtained TXOP with associated AP.
Note: the detailed method is TBD.
Y/N/A

## Slide 8: Straw Poll 2
Do you agree to add the following text to the TGbn SFD:
Non-AP STA can sharing it obtained TXOP with associated AP by transmitting an unicast CF-End frame, and the RA field is set to associated AP’s MAC address.
Note: the detailed rules are TBD.
Y/N/A

## Slide 9: References
[1] 11-23-0581-00-0uhr-non-ap-initiated-txop-sharing
[2] 11-23-1847-00-00bn-non-ap-initiated-txop-sharing-follow-up
[3] 11-23-1874-00-00bn-reverse-txop-sharing
[4] Draft P802.11REVme_D5.0