## Slide 1: Thoughts on Preemption
Date: 2024-09-10
Authors:

## Slide 2: Background and Problem Statement
UHR PAR has the goal of providing improved low latency support
Preemption has been proposed as a mechanism to achieve lower latency for event-based/ aperiodic traffic in other presentations [1-5]
However, preemption comes at a cost:
  Reduced throughput because long PPDUs need to be split into shorter PPDUs, with longer IFS (PIFS) between shorter PPDUs to provide preemption opportunities
  Potential for misuse by the STAs leading to unfair advantage to some STAs
  Fairness concerns for legacy STAs
Hence, the use of preemption needs to be closely managed and authorized by the AP, to balance between the LL gains and undesired impacts from the preemption
  e.g. if no client needs preemption for its LL traffic, then AP should not enable preemption
In this presentation we share some considerations on managing use of preemption by the AP

## Slide 3: Preemption Management (1)
It is not desirable to enable preemption always in the BSS - due to the undesired impact of reduced throughput, potential of misuse by STAs and unfair disadvantage to legacy STAs
Hence, preemption should only be enabled when AP can identify that there are associated STAs with urgent LL event-based traffic
In addition, some LL event-based traffic may not be urgent in a particular deployment, and such traffic would not need preemption
Hence, event-based flows that can trigger preemption should be authorized by the AP, to avoid misuse of preemption
Further, when there are authorized LL flows that need preemption, AP needs to dynamically manage enabling and disabling preemption:
  …so preemption is only enabled when there is high likelihood of event-based LL traffic arriving (e.g. based on STA’s estimates or AI/ML based prediction), and preemption is not enabled always

## Slide 4: Preemption Management (2)
Accordingly, we propose following steps for AP to manage preemption use within a BSS
Step 1: Identifying need for preemption
Step 2: Authorizing use of preemption
Step 3: Enabling preemption

## Slide 5: Step 1: Identifying need for preemption
A mechanism is needed for AP to identify when flows that need preemption (PR) are present
Event-based traffic from STAs can have different LL requirements
  Delay, burst size, min data rate can be different, e.g. delay could vary from 2-10 msec.
  LL traffic from STAs can be only in UL, DL or in both directions
Propose to define a mechanism for STAs to register their LL event-based traffic with AP
  Define an Extended QoS Characteristics element for event-based traffic (or repurpose current QoS Char)
  Extended QoS Characteristics element indicates (at a minimum) direction (UL, DL, both), Delay bound, min data rate, burst size and TID for event-based traffic
  STA indicates whether preemption is desired in Extended QoS Characteristics
    Max rate of preemption desired (e.g. one TXOP every few msec/sec/min)
  STA sends SCS request with Extended QoS Characteristics and TCLAS to the AP
    Desirable to provide App ID/FQDN based flow identification for AP to identify & authorize preemption use
Based on STAs registrations of event-based SCS flows, AP identifies set of event-based flows which need preemption

## Slide 6: Step 2: Authorizing use of preemption
Some LL event-based traffic may not be critical in some deployments and won’t need preemption
  E.g. an industrial alarm which triggers an automated control vs an alarm which is for the operator
Hence, flows that can trigger preemption need to be authorized by the AP, based on urgency need for that deployment (to avoid misuse of preemption)
AP can determine which event-based flows should be authorized for preemption based on traffic requirements indicated by the STA and AP’s flow-specific policy for that deployment
  AP may not authorize preemption use by a flow based on its deployment specific policy
AP notifies a STA that an event-based SCS flow is authorized for preemption in:
  the SCS Response, or
  an unsolicited SCS Response (if preemption authorization provided later)
When preemption is later enabled by the AP, STAs should use preemption mechanism for delivery of LL traffic only for preemption authorized SCS flows
Step 1 and Step 2 get executed as part of SCS registration for LL event-based traffic

## Slide 7: Step 3: Enabling preemption (1)
After preemption (PR) is authorized for a LL event-based flow (from Step 2), typically LL traffic needing PR may be active only intermittently
  e.g. in manufacturing a robotic arm operation may need preemption for a short period of time (e.g 100 msec to 1 sec) when performing critical/precise operation, other times it can tolerate higher latency
Hence, even if flows are authorized for PR it does not result in enabling PR always
STA can signal PR-Start and PR-End in A-Control
  STA signals start of period when LL event-based flows needing PR are active, based on its estimate, and indicates end of period when PR is no longer needed
  STA indicates preemption Start (PR-Start) and PR-End in a UHR A-Control field, e.g. at a fine time granularity per its knowledge of LL flows.
  Avoids management frame overhead + added delays when LL flows needing PR become active/inactive
AP enables preemption in the BSS considering:
  Preemption authorized flows
  PR Start/End indication from STAs
  AP’s policy and its determination of when LL flows needing PR could be active (e.g. AI/ML prediction)

## Slide 8: Step 3: Enabling preemption (2)
AP’s policy for preemption can be advertised in Beacon (e.g. in UHR Operation element):
  Short PPDU length (e.g. 1 msec), Max Number of PR in a TXOP (e.g. may limit to 1)
  AP and STA indicate support for preemption e.g. in UHR Capabilities element
AP signals that the preemption is enabled/allowed in the BSS:
  Through PPDU level signaling - a) UHR A-Control field, or b) in UHR preamble
  Indicates whether PR is enabled for DL, UL or both
  Can be signaled in Beacon, Probe Response as well e.g. when PR is enabled for longer than TBTT
When AP signals PR is enabled in UL, supporting STAs also signal PR is enabled in their UL PPDU through - a) UHR A-Control field, or b) in UHR preamble
When PR is enabled in DL, AP splits the long PPDUs into short PPDUs
When PR is enabled in UL, preemption supporting STAs split long PPDUs into short PPDUs
Preemption can be triggered by the STA or the AP for authorized LL flows only when PR is enabled/allowed in the corresponding direction

## Slide 9: Summary of Steps 1-3
SCS Req to register LL event-based flow. AP indicates preemption authorization in SCS Resp
Dynamic PR-Start and PR-End signaling from STAs to indicate periods when preemption is needed
In-band PR enabled signaling from AP to indicate when preemption is enabled/allowed
  AP can also consider deployment specific network policy/prediction to determine when to enable/disable PR
  When preemption is no longer needed, then AP signals that PR is disabled

## Slide 10: Conclusion
We highlighted that it is not desirable to enable preemption always in the BSS, due to the undesired impact of reduced throughput, potential for misuse by STAs and impact on legacy STAs
Hence, preemption use needs to be closely managed and authorized by the AP, to balance between LL gains and undesired impacts from preemption
We proposed following steps for AP to manage preemption use within a BSS:
  Step 1: Identifying need for preemption - STAs use SCS to register even-based or other LL flows needing preemption with the AP
  Step 2: Authorizing use of preemption – AP authorizes preemption use for a flow based on traffic requirements indicated by the STA and AP’s flow policy for that deployment
  Step 3: Enabling preemption – AP enables preemption considering STA’s estimates of preemption periods with PR Start/End and AP’s policy & prediction of when PR could be needed for LL flows.

## Slide 11: References
[1] IEEE 802.11-23/0018 Low latency support in UHR
[2] IEEE 802.11-23/0092 Preemption
[3] IEEE 802.11-23/1174 TXOP Preemption Follow-Up
[4] IEEE 802.11-23/1229r1 Preemption-for-low-latency-application-follow-up
[5] IEEE 802.11-23/1886r0 Preemption-techniques-to-meet-low-latency-ll-targets

## Slide 12: SP1
Do you agree to define in 11bn that a STA can provide preemption requirements and QoS characteristics for its event-based and other low latency flows that need preemption to the AP?

## Slide 13: SP2
Do you agree to define in 11bn that the use of TxOP preemption for low-latency flows of a STA is authorized by the AP?

## Slide 14: SP3
Do you agree to define in 11bn that the TxOP preemption is only used by a STA (non-AP or AP STA) when the preemption is enabled by the AP in the corresponding direction (UL or DL)?