## Slide 1: Cross-link Wake-up to Go Deeper in Power Save
Date: 2024-05-08
Authors:

## Slide 2: Abstract
In this contribution, we discuss promising solutions into a deeper power save for UHR STAs considering impact on the critical traffic service

## Slide 3: Background
UHR Proposed PAR [1] states
  Reducing power consumption of WLAN devices is required to prolong the battery life of untethered devices (e.g., non-AP STA, Mobile APs), reduce device cost, and lower energy bills of customers deploying non-AP and AP STAs in most scenarios (e.g., residential, enterprise, industrial, venues)
  AP Power Save encompasses different scenarios, including periods of low utilization while minimizing the impact on the service
Several contributions have made efforts to improve power efficiency for different types of UHR STAs

## Slide 4: Re-cap: Power Save Mode Transition
[2-6] proposed to define a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame (ICF)
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
Whether that applies for a non-mobile AP is TBD
ICF still requires STA to keep certain “lower” capability

## Slide 5: Re-cap: Cross-link Power Save with MLO
[6,7] proposed to define cross link power save signaling mechanism
  Allowing a non-AP MLD to indicate to its associated AP MLD that supports the mechanism, in a frame sent on one enabled link, the power management mode for one or more of its affiliated non-AP STAs
Scheduled PS cannot handle certain case when sudden/unscheduled critical traffic arrives during doze time, may impact service performance
Case a
Case b

## Slide 6: Problem Statement: Can We Go Deeper in PS? To save power to more extent
Deep Doze State
  Property 1: Need not to maintain ability to receive ICF, or simply become unavailable for certain period
    Whether to maintain NAV timer is TBD
  Property 2: Can resume service in case sudden/unscheduled critical traffic arrives
    As compared to full doze state/shutdown in [8] that introduce more service delay due to shutting down, especially for APs

## Slide 7: Potential On-hand Tools and Limitations
Option 1: TID-to-link mapping (TTLM)
  Link disablement: To save power to more extent, a link may be disabled
  If used by AP, associated LL STAs have to “move” to ensure LL performance
  Even if such doze could be temporary for AP, the associated STAs cannot know the duration
  To re-enable, perform TTLM (negotiation) again, which could be time consuming
  TTLM is not a high efficiency solution to deeper PS/deep doze
Option 2: Intra-PPDU power save
  Per PPDU enabled, shall transition to the awake state at the end of the PPDU
  May be quite frequent, per-PPDU based state transition could be power consuming
  Not sure it indeed can save power
Overall, only Property 1 can be satisfied, what about Property 2?
  Property 2: Can resume service in case sudden/unscheduled critical traffic arrives

## Slide 8: Problem Statement: Can We Go Deeper in PS? Critical Traffic Consideration
During scheduled PS period, STA cannot handle sudden/unscheduled arrival of critical traffic either DL/UL
  Such critical traffic has to wait until the scheduled PS period comes to an end
A wake-up call is in need, in case of critical traffic arrival
  If through ICF, the STA has to maintain certain “lower” MAC and PHY capability and cannot enter deep doze to save more power
  Additional motivations/benefits are also described in [9]

## Slide 9: Proposal: Exploit Cross-link Wake-up to Go Deeper in PS
Introduce cross-link wake-up, such that
  STA22 on link2 can enter deep doze considering its power status
  In case STA22 enters deep doze, it can still be woken up by STAs on link1
  Even if STA22 is in scheduled PS, critical traffic arrived at STA12 can notify MLD2 ASAP, would not need to wait until the scheduled PS period ends
  Link2 need not to be disabled to enter deep doze, nor re-enabled to be active
The cross-link wake-up frame can be a cross-link variant of a Control frame
  such as a cross-link Trigger frame, a cross-link PS-Poll frame
  frame format detail is TBD
It can indicate whether carrier sense is required when STA22 wakes up, since STA12 may be TXOP holder on link2
Since cross-link message may introduce additional processing time and delay, the lifetime of such message may be included
In case STA23 is also in deep doze, the wake up frame can wake up both STA22 and STA23

## Slide 10: Proposal: Example 1
When STA22 on link2 goes into deep doze mode with limited capability, it can still be up via cross-link frame by STA11 on link1
e.g. in case STA22 (on 5GHz link) is in doze of scheduled PS (such as TWT), STA12 has LL traffic arrived for STA22
This wake-up frame can indicate the PM mode for MLD1’s affiliated non-AP STAs
STA22 can indicate its availability using frames such as PS-Poll

## Slide 11: Proposal: Example 2
If STA22 is AP, it can perform DL MU gathering associated STAs’ PM modes and considering DL buffer status
e.g. AP can use MU-RTS to initiate DL MU
Not required to wake up immediately, leaving the choice to AP (problem also describe in [10])

## Slide 12: Proposal: Example 3
If STA12 is TXOP holder on link 2, it can indicate carrier sense is not required when STA22 wakes up to reply
e.g. STA12 can use CTS-to-Self to protect/reserve the TXOP
STA12 can use padding if needed
STA22 replies CTS frame a certain time after receiving the wake-up frame, to retrieve data from STA12

## Slide 13: Proposal: Example 4
e.g. STA12 can use CTS-to-Self to protect/reserve the TXOP
STA12 can use padding if needed
STA22 replies QoS Null or data frame a certain time after receiving the wake-up frame, transmitting data to STA12

## Slide 14: Proposal: Summary
Proposed a cross-link wake-up call for deeper power save for UHR STAs
Benefits:
  To save power to more extent, a link need not to be disabled to enter deep doze, nor re-enabled to be active
  (Unscheduled) critical traffic arrival can be alerted ASAP via another link, limiting impact on service performance

## Slide 15: References
11-23/480r3, UHR Proposed PAR
11-23/0010r0, Considerations for enabling AP power save
11- 23/1875r1, Power save proposal for non-AP/mobile AP
11- 23/1936r0, AP MLD Power Save Follow-up
11- 23/1965r2, Dynamic Power Save – follow up
11- 23/2003r1, Client power save
11-24/0602r0, Multi Link Power Management for MLO
11-24/0659r1, Thoughts on AP Power Save
11-24/0694r0, Cross-link power save state indication
11-24/0671r0, Enhancements on AP Power Save