## Slide 1: OBSS TWT management for Multi-AP
Date: 2024-07-01
Authors:

## Slide 2: Abstract
In this contribution, we highlight some medium access functionalities during an R-TWT SP for multi-AP coordination in 802.11bn

## Slide 3: Introduction
  Multi-AP (MAP) Coordination is one of the key features considered for IEEE 802.11bn.
  By coordinating among overlapping BSSs, MAP coordination technology promises better network efficiency.
  Coordinated (R-)TWT is seen as one of the most promising scheme for MAP coordination.

## Slide 4: Coordinated TWT principle
Many contributions (e.g. [2][3][4]) presented Coordinated SPs of an OBSS schedule, based on R-TWT:
  Coordinated Medium Access allows several APs to coordinate their medium access to provide enhanced latency sensitive traffic delivery [2]
  An AP can announce whether it respects the R-TWT SPs of its neighbor AP, and indicate that the associated R-TWT STAs need to respect neighbor AP R-TWT SPs [3]
  AP and STAs will stop the TXOP at the beginning of an neighbor AP TWT SP [2][3][4]
The term “OBSS TWT” designates replication of a (neighbor) first BSS TWT in a second BSS.
Following slides will provide possible STA operations to reduce OBSS interferences during an OBSS TWT SP.

## Slide 5: Medium access during OBSS TWT SP
An AP2 (see next slide) sends to its STAs an OBSS TWT element defining (second) TWT SPs timely aligned* with (first) TWT SPs of a first AP1, such that it can adjust the communication policy of its own STAs:
  Option 1: OBSS TWT element forbids the stations of the AP2 BSS to access the medium during the second TWT SPs
  Option 2: OBSS TWT element defines a waiting time for the stations of AP2 BSS to access the medium that is larger than a waiting time for stations of AP1 BSS to access the medium during the first TWT SPs. Typically, STAs perform a CCA (channel sensing) during a larger time.
    e.g. degraded AIFSN value may be set by the second AP to a Minimum TWT Wake Duration negotiated with the first AP
  Option 3: OBSS TWT element indicates a temporary operating channel for stations of AP2 BSS to switch to for their communication during the second TWT SP
    E.g. Channel Switch Announcement, DSO, Secondary Channel Access , …
(*: “timely aligned” means SP starting times are fully aligned in time)

## Slide 6: Illustration of options 1 and 2
Option 1: access forbidden
  very low risks of interference to the detriment of communication efficiency in the AP2 BSS
Option 2: waiting time
  stations not interfering with the AP1 BSS are not subject to OBSS limitation
AP1
STA11
AP2
STA21
beacon
Probe Resp
STA22
First
BSS
Second
BSS
beacon
OBSS TWT IE
beacon
OBSS TWT IE
MAP Req
MAP Resp
OBSS TWT SP
R-TWT SP
OBSS TWT SP
Sensing period
Beacon
Beacon
Beacon
R-TWT SP
option 1
option 2
Access forbidden
Waiting time

## Slide 7: Summary
To reduce OBSS interference among a Multiple AP set, we introduced concepts and solutions for reduced communication activities for stations of neighbouring BSS during the coordinated R-TWT (OBSS TWT) SPs.
Three modes/options of operation are identified (forbids STAs to access, waiting time to access, channel switch).
Next steps: provide simulation results about the various options

## Slide 8: Straw Poll
Do you agree that 802.11bn SFD introduces a mode of operation wherein APs of a Multi-AP set, modify their STAs medium access policy during overlapped coordinated R-TWT (aka OBSS TWT) schedule(s)?
- objective is to reduce interferences encountered by one BSS of the MAP set during the scheduled period;
- detailed mechanisms are TBD.

## Slide 9: References
[1] 802.11bn PAR
[2] 11-23/226 Considerations for AP coordination in UHR: Coordinated Medium Access, Abdel Ajami (Qualcomm)
[3] 11-23/250 AP Coordination, Liwen Chu (NXP)
[4] 11-23/291 R-TWT Multi-AP Coordination, Kumail Haider (Meta)