## Slide 1: Tx EVM Setting for MIMO Detection
Date: 2024-04-02
Authors:
Name | Affiliations | Address | Phone | email
Genadiy Tsodik | Huawei |  |  | Genadiy.tsodik@huawei.com
Rani Keren |  |  |  | 
Shimi Shilo |  |  |  | 
Doron Ezri |  |  |  | 
Yoav Levinbook |  |  |  | 
Oded Redlich |  |  |  | 

## Slide 2
In [1], [2] we presented an analysis of the impact of Tx EVM on nonlinear MIMO detection
We explained that a higher (worse) Tx EVM causes a significant degradation of nonlinear MIMO detector performance, and also showed that current Tx EVM requirements better fit linear MIMO detectors
We showed that lower (better) Tx EVM improves MIMO performance - for both linear and nonlinear detectors - and that nonlinear detectors outperform linear detectors for all simulated MCSs
We also simulated different PA models and showed that the behavior is similar in case of a more linear PA
Recap
7dB

## Slide 3
Lower (improved) Tx EVM may lead to an improvement of 3-8dB compared with operating at standard Tx EVM
The difference between Tx EVM that leads to best performance and standard Tx EVM depends on MCS and PA model (this difference is within a range of 2-8dB)
An improvement in Tx EVM should be accompanied by proper signaling (or any other means) so that the receiver (e.g. AP) can improve detection performance – for example via employing an advanced receiver
  Otherwise – the AP has no practical means to know that the STA’s Tx EVM is significantly improved
Main Understanding So Far

## Slide 4
Tx EVM has a significant impact on MIMO performance; current Tx EVM requirements are more fit for linear detection
Previous WLAN amendments 11ac and 11ax defined Tx EVM (for 256-QAM and 1024QAM respectively) when focused mainly on SISO. In particular, nonlinear detectors were not considered [3, 4]
  It has been mentioned that MU-MIMO transmission requires better (lower) Tx EVM [3]
Formalization of Tx EVM requirements for MIMO transmissions in the spec will be a good solution that may encourage implementation of nonlinear detectors – this will lead to a very large performance gain, which in turn means higher throughput and also reduced latency and improved reliability
A very significant gain in MIMO transmissions may be achieved with relatively simple standard modifications
  A possible solution may be a new Tx EVM table and/or a simple mechanism that allows an a receiver to indicate the required Tx EVM per transmission (e.g. AP indicating the required Tx EVM in TB PPDU)
Summary and Standard Perspective

## Slide 5
[1] 11-23-1944-01-00bn-impact-of-tx-evm-on-mimo-detection
[2] 11-24-0417-01-00bn-impact-of-tx-evm-on-mimo-detection-follow-up
[3] 11-11-0029-00-00ac-256-qam-tx-evm-and-rx-sensitivity
[4] 11-15-1070-03-00ax-1024-qam-proposal
References

## Slide 6
Do you agree that 802.11bn will define Tx EVM requirements that are designed for nonlinear MIMO detection?
  Yes
  No
  Abstain
SP 1

## Slide 7
Do you agree that 802.11bn will define a mechanism that allows an AP to indicate which Tx EVM is required?
  Yes
  No
  Abstain
SP 2