## Slide 1: Extra dRUs Construction
Date: 2024-05-11
Authors:

## Slide 2: Introduction
A DRU is constructed by distributing tones of a rRU[1-3]. Then, the Tx power per tone can be boosted and SNR can be increased.
The dRU hierarchical structure can follow the same rules as in the rRU case[2], i.e., a larger dRU is formed by combining several smaller dRUs.
For example, 52-tone dRU 1 is formed by combining 26-tone dRU 1 and 2.
However, some dRU tone plan designs are with low utilization efficiency.
For example, the utilization efficiency of a 52-tone dRU is 86.0% (52*8/484) in a 40 MHz PPDU. About 14% frequency resource is wasted.
dRU logical structure in 40 MHz PPDU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
26-tone dRU | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
52-tone dRU | 1 |  | 2 |  | / | 3 |  | 4 |  | 5 |  | 6 |  | / | 7 |  | 8 | 
106-tone dRU | 1 |  |  |  |  | 2 |  |  |  | 3 |  |  |  |  | 4 |  |  | 
242-tone dRU | 1 |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 
484-tone dRU | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 3: Extra dRU in 40 MHz PPDU
In a 40 MHz PPDU, if tones of a dRU are distributed evenly[2], then
  The tone separation distance of a 26-tone dRU is 18
  The tone separation distance of a 52-tone dRU is 9
Based on that observation, there can be at most nine 52-tone dRUs in a 40 MHz PPDU.
  Eight of them follow the same indexing as rRUs, and
  The extra 52-tone dRU should be allocated a new dRU index.
The extra (9th) 52-tone dRU can be formed by combining 26-tone dRU 5 and 14.
Based on the tone plan in [1], the tone indices of the 52-tone dRU 9 are: [-234:9:-9, 18:9:243]
The power boost gain of the novel 9th 52-tone dRU is the same as other same-size dRUs in 40 MHz PPDU.
Updated dRU logical structure in 40 MHz PPDU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
26-tone dRU | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
52-tone dRU | 1 |  | 2 |  | 9 | 3 |  | 4 |  | 5 |  | 6 |  | 9 | 7 |  | 8 | 
106-tone dRU | 1 |  |  |  | / | 2 |  |  |  | 3 |  |  |  | / | 4 |  |  | 
242-tone dRU | 1 |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 
484-tone dRU | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Extra dRUs in 80 MHz PPDU
In a 80 MHz PPDU, if tones of a dRU are distributed evenly[2], then
  The tone separation space of a 26-tone dRU is 36. The max number of 26-tone dRU is 36
  The tone separation space of a 52-tone dRU is 18. The max number of 52-tone dRU is 18
  The tone separation space of a 106-tone dRU is 9. The max number of 106-tone dRU is 9
Note: 26-tone dRU may not be defined.
In an 80 MHz PPDU,
The first extra (17th) 52-tone dRU can be formed by combining 26-tone dRU 5 and 14.
The second extra (18th) 52-tone dRU can be formed by combining 26-tone dRU 24 and 33.
The extra (9th) 106-tone dRU can be formed by combining 52-tone dRU 17, 18 and 2 extra tones.
The power boost gain of the extra dRUs may be different from that of other same-size dRUs in 80 MHz PPDU.
Updated dRU logical structure in 40 MHz PPDU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
26-tone dRU | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37
52-tone dRU | 1 |  | 2 |  | 17 | 3 |  | 4 |  | 5 |  | 6 |  | 17 | 7 |  | 8 |  | / | 9 |  | 10 |  | 18 | 11 |  | 12 |  | 13 |  | 14 |  | 18 | 15 |  | 16 | 
106-tone dRU | 1 |  |  |  | 9 | 2 |  |  |  | 3 |  |  |  | 9 | 4 |  |  |  |  | 5 |  |  |  | 9 | 6 |  |  |  | 7 |  |  |  | 9 | 8 |  |  | 
242-tone dRU | 1 |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 
484-tone dRU | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
996-tone dRU | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Summary
Extra dRUs can improve the frequency utilization efficiency in 40 and 80 MHz PPDUs.
In this contribution, we proposed methods of constructing extra dRUs.
In a 40 MHz PPDU, 1 extra 52-tone dRU are defined;
In an 80 MHz PPDU, 2 extra 52-tone dRUs and 1 extra 106-tone dRU are defined.

## Slide 6: References
[1] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[2] 11-23-2021-01-00bn-principle-and-methodology-for-dru-tone-plan-design
[3] 11-23-1988-01-00bn-considerations-on-dru-design-and-application