## Slide 1: Discussion on NPCA and SR
Date: 2024-04-26
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Spatial reuse (SR) was a mechanism introduced in 11ax to increase the system throughput;
Non-primary channel access (NPCA) is a feature discussed in TGbn to improve the latency and throughput;
Both SR and NPCA are enable the concurrent transmission when primary channel is occupied by OBSS transmission;
When both SR and NPCA are supported in a BSS, the AP and the non-AP STAs may select different mechanisms. As a result, none of them could work well.

## Slide 3: Example: SR
After received PPDU1 from OBSS, AP1 transmit A-MPDU1 to STA1 through SR;
AP1 and STA1 operating on primary channel during SR.

## Slide 4: Example: NPCA
After received PPDU1 from OBSS, AP1 and STA1 switch S40 based on NPCA and then transmit A-MPDU1 to STA1;
AP1 and STA1 operating on non-primary channel during NPCA.

## Slide 5: Solution 1 – Select One of The Two
Both SR and NPCA can potentially improve the efficiency and delay, but the use case may be different;
  SR is preferred when the distance between two BSS is far, while NPCA is more preferred when the distance between two BSS is close;
  NPCA is preferred when there are large opportunity to get a free non-primary channel when the primary channel is occupied. While the condition of non-primary channel doesn’t need to be considered for SR.
Base on AP’s decision, AP can dynamic select SR or NPCA which have better performance for its BSS.
Solution 1 is simple, but may not be the optimal solution. Because SR will be better for some OBSS TXOP, while NPCA will be better for other OBSS TXOP.

## Slide 6: Solution 2 – Coexistence With Each Other
AP can choose enable SR and NPCA simultaneously;
In this case, a guide rule is needed to help AP and non-AP STAs select the same mechanism (SR or NPCA) when a OBSS PPDU is received;
A simple way is select do the selection base on the received RSSI of OBSS PPDU
  When the RSSI < OBSS PD, SR will be used
  When the RSSI >= OBSS PD level, NPCA will be used
Consider the RSSI may different at AP side and non-AP STA side, that will makes AP and non-AP STA select differently. A NPCA PD level (> OBSS PD level) may help
  When the RSSI < OBSS PD, SR will be used
  When the OBSS PD <=RSSI <NPCA PD , none of the two will be used
  When the RSSI >= NPCA PD, NPCA will be used

## Slide 7: Summary
When a OBSS PPDU is received, both SR and NPCA may be triggered, the coexistence issue of SR and NPCA need to be considered;
A simple but sub-optimal way is just enable SR or NPCA at one time period;
SR and NPCA can coexistence with each other, but a rule is needed to help the AP and non-AP STAs to do the same selection when a OBSS PPDU is received.