## Slide 1: The Switching Time In NPCA
Date: 2024-05-05
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
A STA that supports non-primary channel access (NPCA) will switch to a non-primary channel when an OBSS PPDU is received;
The switching time is important for NPCA, because the AP and the non-AP STAs need to switch to the non-primary channel at the same time;
The switching time in several cases are discussed in this presentation.

## Slide 3: NAV Setting
Normally, the NAV will be updated at the end of a received PPDU
  “This NAV update operation is performed when the PHYRXEND.indication primitive is received, except when the PHY-RXEND.indication primitive is received before the end of the PPDU. In this exception, the NAV update is performed at the expected end of the PPDU.” (IEEE802.11 REVme D4.0)
A natural way is switching to the non-primary channel at the end of received PPDU, but it is not always the case, and may not be a good choice for NPCA.

## Slide 4: Long PPDU
When the NAV be set after successfully decoded a long PPDU, the remain TXOP may be very small or even zero. Please see below example;
The long PPDU exists in many scenarios
  A large Management frame;
  A long TB PPDU;
  A large beamforming report frame;
  …
A better solution is switch to the non-primary channel after the PHY SIG (time T1) of a long PPDU.
  T1: the end of PHY SIG field
  T2: the end of the PPDU

## Slide 5: NAV Set For 11ax And 11be Frames
There are two ways to set NAV base on a received OBSS HE or EHT PPDU. And the same design will possibly be used in a UHR PPDU;
  Way 1: Set NAV base on preamble; Or
    BSS Color field and TXOP field are carried in HE SIG A field and EHT U-SIG field;
  Way 2: Set NAV base on Duration field in MAC header
Currently, a receiving STA can choose either way to set the basic NAV;
In NPCA, a different way to set NAV means a different switching time to non-primary channel
  Please remember that the Duration filed in MAC header will not be validated before the end of the first successfully received MPDU in an A-MPDU, or before the end of the whole frame
All NPCA supported STAs switch to non-primary channel after HE-SIG-A field or U-SIG field will be more efficient.

## Slide 6: (MU)RTS/CTS Frames
A STA that receives an OBSS PPDU will set or update the basic NAV at the end of this PPDU, except the received frame is a RTS or MU-RTS frame which will trigger a NAV reset rule;
  The STA will reset the basic NAV to 0 if neither a CTS frame nor a PPDU follows CTS frame is received
For the STA that correct set basic NAV base on (MU)RTS frame also have two different switching time;
  The STA that received CTS will confirm the basic NAV set after CTS;
  The STA that doesn’t received CTS will confirm the basic NAV set after receive the frame follows CTS frame.

## Slide 7: Summary
The switching time from primary channel to non-primary channel in NPCA is very important, because the AP and its associated STAs need to switch to the non-primary channel simultaneously;
There are some cases that a receiving STA choose different switching time
  Long PPDU
  A PPDU with TXOP field in PHY preamble
  (MU)RTS/CTS
The spec need to give a guide line to help the AP and its associated STAs to sync their switching time.