## Slide 1: Dynamic Bandwidth Selection Signaling Details
October 15, 2024
Authors:
Name | Affiliation | Phone | email
Binita Gupta | Cisco Systems |  | binitag@cisco.com
Malcolm Smith | Cisco Systems |  | mmsmith@cisco.com
Brian Hart | Cisco Systems |  | brianh@cisco.com
Jerome Henry | Cisco Systems |  | jerhenry@cisco.com

## Slide 2: Recap - Real Time Dynamic Bandwidth Selection (DBS)
In [1] it was highlighted that 160 and higher MHz channels are unlikely to be deployed in enterprise networks
Radio Resource Management (RRM, non real time) prefers WLAN stability and typically employs conservative frequency reuse (e.g. 10+), leading to mostly adoption of 40MHz (for 5GHz) and 40-80MHz (for 6 GHz)
With MAPC, neighboring APs can coordinate & identify opportunities for BW expansion in real-time, e.g. from 40 to 160MHz expanded BW (E-BW)
      Exploiting variations in neighboring BSS load and interference conditions
RT-DBS enables opportunistic use of wider BW in enterprise deployments, improving spectrum efficiency and network performance
[1] proposed two modes of RT-DBS operation:
      Long-term based RT-DBS (e.g. over seconds)
      TXOP based RT-DBS
Here we propose next level of details for Long-term based RT-DBS

## Slide 3: DBS Coexistence with NPCA
Several presentations have proposed NPCA [2,3] and NPCA is in 11bn SFD [4]
DBS does not change P20 of the BSS. When BSS BW is dynamically expanded (to E-BW), NPCA operation can take E-BW into consideration
      AP can announce a different NPCH within E-BW, if preferred based on channel conditions
      STAs that support DBS can switch to the NPCH in E-BW for NPCA
      Non-DBS STAs, would temporarily disable NPCA if NPCH is outside BSS operating BW
      Even with DBS, AP can keep same NPCH as before BW expansion, based on the mix of DBS and non-DBS STAs and/or channel conditions.
    Similar NPCA behavior would apply with DBS E-BW

## Slide 4: Long-term based DBS
Steps involved:
Step 1: Multi-AP coordination to identify DBS opportunity
Step 2: Dynamic bandwidth selection signaling in BSS
Step 3: BSS operation with Dynamic bandwidth selection
Step 4: Termination of Dynamic bandwidth selection

## Slide 5: Step 1 – MAPC to identify DBS opportunity
  Neighboring APs coordinate to determine BW expansion opportunity
    BSS load/channel usage shared between neighboring APs
    Per-subchannel OBSS CCI can be estimated by APs (e.g. using a scan radio)
    Based on neighboring APs channel load, CCI measurements and other factors, network/AP determines BW expansion for an AP (e.g. for AP with higher load)
      Puncturing can be used in E-BW to puncture out BW of some neighboring AP’s
    Network determines start time for dynamic BW expansion (e.g. x TUs in future) and expected duration for E-BW usage
  To simplify scope, DBS coordination messaging between APs can be exchanged over-the-DS (no need to define OTA signalling)
    Since primary use case is for APs in the same management domain

## Slide 6: Step 2 – Dynamic BW selection signaling (1)
  BW expansion via legacy (E)CSA mechanisms is not a good option
    Many STAs respond to (E)CSA by roaming away and then roam back. Causing roaming impact to legacy STAs due to DBS is not acceptable
      Some legacy STAs will not associate with an AP that supports (E)CSA
    (E)CSA is designed for use with non-real time RRM, not for real-time changes
    Using (E)CSA to announce BW changes, could cause legacy interop issues:
      (E)CSA would change BW for all STAs, including legacy STAs, those STAs are not tested for frequent BW change – may result in field interop issues
      (E)CSA is used for changing primary channel, which is not the case for DBS, where P20 remains same and only BW changes - this again may cause field interop issues.
  Changing BSS operating BW dynamically in BSS operation element or using OMN is not a good option either
    legacy STAs are not tested for such freq BW changes – may cause interop issues
    STAs in PS may not receive Beacons and/or OMN and can miss BW changes
  Hence, we propose to define a new signaling mechanism to notify UHR STAs of dynamic BW changes in advance
    this avoids any DBS impact on pre-UHR STAs

## Slide 7: Step 2 – Dynamic BW selection signaling (2)
  AP and STA both indicate capability support for DBS and Max DBS BW supported in management frame(s)
    Note: BSS Operating BW is signaled separately
  DBS parameters signaling by STAs
      A non-AP STA can dynamically enable/disable DBS support
      STA can signal its DBS support, Max DBS BW, DBS BW Switch Delay to AP
        e.g. in (Re)Assoc Request or in another management frame for DBS
        DBW BW switch delay accounts for STA’s delay for expanding the BW
      At times, STA may have constraint to expand to Max DBS BW, e.g. due to power save. STA can dynamically signal an updated/lower Max DBS BW. Later, when no longer constrained, it can signal its original/higher Max DBS BW.
        signaled through a DBS mgmt. frame, or in-band in an A-Control field
      AP uses latest Max DBS BW indicated by associated STAs to determine parameters for DBS announcement

## Slide 8: Step 2: Dynamic BW selection signaling (3)
  Dynamic BW Selection announcement by AP
      We propose to define a mechanism for Dynamic Bandwidth Selection Announcement (DBSA) by AP in Beacons and Probe Response
      AP determines DBS expanded-BW (E-BW) based on the set of associated STAs that support DBS, and their Max DBS BW supported
        e.g. if STAs support Max DBS BWs of 80 & 160MHz, AP may select E-BW of 160MHz
      AP announces DBS E-BW within a DBSA element that includes:
        BW Indication fields - DBS E-BW, Disabled Subchannel bitmap, and optionally Channel Center Frequency
        DBS start time (e.g. in units of TUs, # of TBTTs, or a future TSF time)
        DBS duration (e.g. in units of TUs)
      Puncturing can be used in DBS E-BW
        To signal odd E-BWs e.g. 120MHz signaled as 160MHz with 40MHz punctured
        To puncture out operating BW of a neighboring BSS
      DBSA is advertised in advance in Beacons to notify STAs of upcoming E-BW
      DBSA is also advertised for the duration when DBS E-BW is active

## Slide 9: Step 3 – Operation with Dynamic bandwidth selection (1)
  Once a DBS E-BW becomes active (at DBS start time), AP and supporting STAs can use expanded BW for their transmissions
  AP and STA select expanded BW (for that STA) based on STA’s Max DBS BW and DBS E-BW announcement in the Beacon
    STA’s E-BW = min (STA’s Max DBS BW, E-BW in DBSA) – see table below
  AP can use selected STA’s E-BW in its DL/UL OFDMA to that STA (along with other DBS and non-DBS STAs)
  A DBS supporting STA can operate with the selected STA’s E-BW for its UL EDCA
BSS Operating BW | STA Max DBS BW | E-BW in DBS Announcement | Selected E-BW for STA
40 MHz | 80 MHz | 80 MHz | 80 MHz
40 MHz | 160 MHz | 160 MHz | 160 MHz
40 MHz | 160 MHz | 80 MHz | 80 MHz
40 MHz | 80 MHz | 160 MHz | 80 MHz

## Slide 10: Step 3 – Operation with Dynamic bandwidth selection (2)
  During an active DBS duration, a STA may have a use case to signal a change in its Max DBS BW e.g. from 160 to 80 MHz due to power save
    signaled in-band using A-Control or via a management frame
    Both AP and STA would use the updated Max DBS BW to select a revised STA’s E-BW for use in subsequent TXOPs with the DBS duration
    Ex: If for a STA Max DBS BW changes:160 ->80, STA & AP operate with 80MHz for that STA
  BW Switching delay of STA and AP needs to be accounted by both peers at the start and end of DBS duration

## Slide 11: Step 4 – Termination of Dynamic bandwidth selection
  When the DBS duration expires for a DBS E-BW, DBS operation terminates
  AP and DBS supporting STAs go back to using the BSS operating BW
  Alternatively, AP may also extend or shorten the DBS duration in DBS announcement, based on real time measurements (BSS load, CCI) from neighboring APs.
  All DBS announcement related changes in Beacon must be considered critical updates and get reflected in BSS Parameters Change Count (BPCC)

## Slide 12: Conclusion
  Most enterprise deployments are stuck at 40 MHz today, despite wider BWs being available
  Real-time DBS enables enterprise deployments to opportunistically make use of wider BWs, while still honoring RRM goal of WLAN stability
  We proposed procedure and signaling to support Long-term based DBS for UHR STAs:
    Dynamic bandwidth expansion opportunity can be realized using MAPC for DBS (OTDS to simplify the scope)
    DBS E-BW announced in advance by AP in Beacons, Probe Response
    Once DBS E-BW is active, AP and supporting STAs select E-BW based on STA’s Max DBS BW, and can operate with selected E-BW for UL/DL PPDU exchange
    Once DBS duration ends, DBS is terminated and AP/STAs go back to using BSS operating BW

## Slide 13: Straw Poll 1
Do you agree to define in 11bn a mechanism for dynamic bandwidth selection (DBS) in real-time to expand operating bandwidth for UHR STAs that support DBS operation?

## Slide 14: References
[1] 11-24/0088 “Maximizing channel bandwidth in dense AP deployments”
[2] 11-23-1891 “Nonprimary channel access - follow up”
[3] 11-23-2005 “Non-primary channel access (NPCA)”
[4] 11-24/0209 “Specification Framework for TGbn”