## Slide 1: Opportunistic Transmission in C-TDMA
Date: 2024-09-09
Authors:

## Slide 2: Introduction
In [1], allowing the transmission of AP within the duration of shared TXOP when the AP is hidden to the shared AP is proposed
There were two options to carry out this procedures
  Option 1: Using the NAVTimeout
  Option 2: Change the duration field of MU-RTS TXS TF
In this contribution, more detail operations and conditions for conducting this procedures are proposed

## Slide 3: Recap: Opportunistic Transmission in C-TDMA
In [1], opportunistic transmission (OT) in C-TDMA is proposed
  Sharing AP (AP 2) shares its TXOP to Shared AP (AP 3)
  OT AP (AP 1) and Shared AP (AP 3) are hidden to each other
  If transmission of OT AP (i.e., AP 1  STA 1) do not affect on the transmission of shared AP (i.e., AP 3  STA 6), then the transmission of OT AP (i.e., AP 1  STA 1) is allowed within the shared TXOP duration

## Slide 4: Recap: Opportunistic Transmission in C-TDMA
However, this opportunistic transmission in C-TDMA can be result in the collision at the sharing AP when the shared AP returns its TXOP to the sharing AP. This is because the OT AP and the sharing AP are not hidden to each other.

## Slide 5: Recap: Framework for C-TDMA
Frameworks for C-TDMA operations were proposed in [2]-[4]
  There are two types of C-TDMA operations (i.e., C-TDMA operation for periodic or aperiodic traffic)
During the C-TDMA configuration setting phase, Configurations of C-TDMA operation (e.g., capabilities of each AP, periodic traffic information (e.g., SCS)) can be set among APs
  This can be the part of the M-AP configurations setting procedure
  Information about periodic traffics can be shared among the APs during the C-TDMA configuration setting procedure  By using information obtained in this phase, the amount of periodic traffic can be predicted

## Slide 6: Recap: Framework for C-TDMA
During the pre C-TDMA information exchange procedure, information /signaling for the short-term C-TDMA operation (e.g., request the C-TDMA resource) may be conducted
  The possible solution for this procedure can be exchange of BSR or NFR  By conducting this procedure, information of aperiodic traffic can be obtained

## Slide 7: TXOP Return Operation
Based on the prerequisite, the sharing AP may predict the amount of TXOP for shared AP before C-TDMA operation
If amount of TXOP is well predicted, the TXOP return procedure may not be needed
In addition, support of TXOP return operation can be optional as 11be (i.e., TXOP Return Support In Triggered TXOP Sharing Mode 2 in 11be)

## Slide 8: Hidden Node Problem in C-TDMA
Due to the OBSS Transmission, the transmission of Shared AP may be unsuccessful which can be result in the waste of resources
  For example, when Sharing AP (AP 2) shares its TXOP to Shared AP (AP 3), and the shared AP transmits data to the STA in its BSS (STA 6). However there is OBSS transmission around the STA (STA 6), the STA (STA 6) can not receive the data from Shared AP (AP 3)

## Slide 9: Control Frame Exchange
Control frame exchange (e.g., RTS-CTS) may prevent the hidden node problem in C-TDMA
Example)
  Basic NAV of STA 6 is set by the OBSS transmission
  When AP 3 transmits a control frame (e.g., RTS) to the STA 6, but STA 6 can not reply due to the Basic NAV, therefore AP 3 may not transmit a data frame to the STA 6
  AP 3 may use the shared TXOP to other STAs

## Slide 10: Opportunistic Transmission in C-TDMA
Network Topology and Assumption
  Sharing AP (AP 2) shares its TXOP to Shared AP (AP3)
  OT AP (AP 1) and Shared AP (AP 3) are hidden to each other
  Before starting the data transmission in the shared TXOP, Control frame exchange (e.g., RTS-CTS) is conducted to prevent the hidden node problem
  Return of the shared TXOP is not allowed

## Slide 11: Opportunistic Transmission in C-TDMA
Proposed operation of opportunistic transmission in C-TDMA
  After a OT AP (i.e., NOT the shared AP) receives the TXOP sharing message (e.g., MU-RTS TXS TF) from the sharing AP, the OT AP reset its NAV after duration of M-APNAVTimeout only when the return of TXOP is not allowed
  M-APNAVTimeout value can be (3SIFS + CTS + Control + Resp. of Control) (Different from current NAVTimeout value)
  If the NAV of OT AP is reset after M-APNAVTimeout , the OT AP tries to do EDCA access and transmit data within the duration of shared TXOP

## Slide 12: Hidden Node Problem in OT
Due to the OT, the transmission of Shared AP may be unsuccessful
  For example, if the shared AP (AP 3) transmits data frames to the STA in its BSS (STA 5), OT AP (AP 1) may start its transmission because OT AP (AP 1) can not detect the transmission of shared AP (AP 3). The transmission of OT AP (AP 1) may result in the collision at the STA associated with the shared AP (STA 5).

## Slide 13: Control Frame Exchange
Control frame exchange (e.g., RTS-CTS) may prevent the hidden node problem in OT
  For example, if Shared AP (AP 3) transmits a data frame to the STA in its BSS (STA 5) after the control frame exchange, NAV reset procedure (after M-APNAVTimeout) at OT AP (AP 1) failed due to the control frame exchange procedure in the shared TXOP.

## Slide 14: Summary
Opportunistic transmission in C-TDMA is proposed in limited condition to enhance the medium efficiency
  Opportunistic transmission is available only when the return of shared TXOP in C-TDMA is not used
  Control frame exchange is highly recommended in C-TDMA operation to prevent the hidden node problems
Remaining Problems to be solved
  TXOP return is needed in certain cases
    Amount of TXOP to share can not be perfectly predicted
    Transmission of shared AP can be failed if the target STA of shared AP is affected by OBSS transmissions
  NAV protection can be needed in the certain cases
    If the NAV of OT AP is set by OBSS transmissions which was initiated by the hidden node of Sharing AP, it may affect on the OBSS transmissions when OT AP reset its NAV.
  The target STA of OT AP may not response to the control frame of OT AP
    STA transmits CTS only when RTS is transmitted by TXOP holder, however, OT AP may not the TXOP holder at that time (Only direct data transmission is possible)

## Slide 15: References
[1] 23/1846r1, “Protection of Extended TXOP Sharing”
[2] 23/1871r2, “M-AP Coordinated Transmission framework”
[3] 23/1912r1, “Coordinated TDMA Procedure”
[4] 24/0512r0, “Considerations for Coordinated TDMA”

## Slide 16: Straw Poll #1
Do you agree to define a mechanism to allow an AP to share a portion of its obtained TXOP with one or more of other APs/STAs?

## Slide 17: Straw Poll #2
Do you agree to define a mechanism that may allow an AP to be able to transmit while the TXOP on the channel is shared within a set of APs[Note 1] under certain conditions[Note 2]
  [Note 1] Definition of set of APs is TBD and the set may consist of at least one other AP
  [Note 2] Certain conditions are TBD, e.g.
    An AP which is hidden to the shared AP
    Another type of NAVTimeout is applied etc.