## Slide 1: Dynamic SCS
Date: 12-11-2024
Authors:

## Slide 2: Problem Statement
  The SCS with QoS Characteristics procedure defined in IEEE 802.11be is for Quasi-static traffic flow, i.e., the underlying assumption is that the traffic characteristics do not change too frequently. However, there are many scenarios where the users’ traffic patterns change too frequently—
  - Webex call: During Webex, Zoom or other video or live content-sharing application, the codec rate can change dynamically. Based on the changes in the codec rate, the traffic characteristics also change.
  - XR application: In various XR application, the pose data from the hand-held device often needs to be transmitted to either the head-mounted device (HMD) or to the companion device in a very short time (highly latency sensitive) in order to ensure a smooth XR experience. This requires a fast/dynamic change in the QoS characteristics between the hand-held device and the HMD or the companion device.
  Currently, there is no mechanism defined in the 802.11 specification that would allow for a non-AP STA to dynamically change QoS expectation or QoS flow with the associated AP. This may disrupt the latency sensitive applications for the clients.

## Slide 3: Dynamic nature of QoS
  A non-AP STA can set up a QoS flow of certain QoS characteristics with an AP, where the characteristics of the QoS setup or QoS flow can change dynamically.
  After the initial QoS flow is set up (e.g. with SCS negotiation), the characteristics of the QoS flow can change dynamically. A ‘dynamic change’ in the QoS flow or QoS setup often has the following characteristics—
    A fast change in the QoS characteristics of the traffic
    The change is rather predictable—the new flow is often drawn from a predetermined set of QoS characteristics or “QoS profiles”
  In such scenarios, the non-AP STA could perform one negotiation (e.g. one SCS negotiation (new mode of SCS)) with the AP such that that single transaction would negotiate for multiple QoS flows/profiles.
    A successful negotiation would mean that the AP is ‘OK’ with all such profiles, and the STA can dynamically request to switch from one profile to another.
    Such an SCS that entails a multitude of QoS profiles and a switching among them is referred to as “Dynamic SCS” in this presentation.

## Slide 4: Fast QoS Switch (Dynamic SCS)
  For the scenario where a non-AP STA sends to an AP a D-SCS request, where the D-SCS request contains X number of SCS or QoS profiles corresponding to the request, if the AP accepts the request, then it would indicate that the non-AP STA can request to dynamically switch from one QoS profile to another QoS profile within the set of QoS profiles included in the D-SCS request.
  One QoS profile can correspond to one QoS Characteristics element within the SCS Descriptor element.

## Slide 5: SCS Parameter Change Request/Response
  After an initial D-SCS is set up between a non-AP STA and an AP, a control frame can be sent by the non-AP STA to indicate a switch from one profile to another.
    A-control frame or some other control frame can be used for this purpose.
    The frame would contain a list of <parameter, value> pairs. The list would indicate the SCS ID of the existing D-SCS setup for which the parameter change request applies and a value of the target profile within that D-SCS.

## Slide 6: Provisioning
  For the scenario where a non-AP STA sends to an AP a D-SCS request, where the D-SCS request contains X number of QoS profiles corresponding to the request, if the AP accepts the request, then the AP can provision sufficient resources to the first STA so that the QoS requirement indicated by the most recent QoS profile indication is fulfilled.
  For example, the AP can trigger the non-AP STA sufficiently according to the most recently indicated QoS profile indicated by the non-AP STA.

## Slide 7: Example frame exchanges
  Upon the initial successful setup of the Dynamic SCS or D-SCS, a particular QoS profile may be activated.
  Later on, with the changes in the traffic patterns, the non-AP STA can send a control frame (e.g., QoS Activation Request frame in the figure below) to indicate its desire to switch to another QoS profile (within the same negotiated D-SCS) to cater the updated traffic pattern better.

## Slide 8: SP1
  Do you agree to enhance the existing SCS framework in 11bn to enable a non-AP STA to dynamically switch from one QoS profile to another QoS profile for an SCS stream?
  The new QoS profile is selected from one of the previously accepted QoS profiles for that SCS stream.
  TBD on mechanism for QoS profile switch indication.

## Slide 9: Thank you