## Slide 1: Reliable Transmission in ML TWT for UHR
Date: 2024-05-12
Authors:

## Slide 2: Introduction
According to the 11bn PAR[1], one of key features of UHR is to provide a more reliable transmission in WLAN environment
In this contribution, we propose a method to increase the reliability of transmission during ML TWT

## Slide 3: Background: ML Flexible Wake Time
TGbe [2] provides multi-link based flexible wake time operation
To reschedule a TWT SP in a link, the AP MLD can transmit the TWT Information frame on another link when the link is not available to transmit the TWT Information frame
  TWT Information frame will contain Multi-link element indicating a link that the contents of the TWT Information frame are applied to
This will support faster low latency traffic delivery well
AP1
STA1
AP2
STA2
Link 1
Link 2
AP MLD & Non-AP MLD
TWT SP
TWT Info frame
(Link 2)
LL Traffic mapped to Link 2 is arrived
Doze state
TWT SP`
Ack
LL Data
BA

## Slide 4: Motivation
When an AP receives the LL traffic for the non-AP STA, the AP will try to transmit the LL traffic as soon as possible based on latency requirements of the LL traffic
However, each STA may have different capability regarding the transition delay of the multi-link based power state
  For example, the ML power state transition delay of a low-end device will be longer than that of a high-end device
When the AP MLD reschedules TWT SP using ML Flexible TWT, if AP MLD does not consider non-AP MLD’s capability, the non-AP MLD may not receive DL frame in the rescheduled TWT SP successfully
AP1
STA1
AP2
STA2
Link 1
Link 2
AP MLD & Non-AP MLD
TWT SP
TWT Info frame
(Link 2)
LL Traffic mapped to Link 2 is arrived
TWT SP`
Ack
LL Data
BA
Non-AP MLD 1’s
ML PS transition delay
Non-AP MLD 2’s
ML PS transition delay
Non-AP MLD 2 may miss LL data

## Slide 5: Reliable ML Flexible Wake Time
When the AP MLD reschedules TWT SP using ML Flexible TWT, AP MLD should consider non-AP MLD’s capability for multi-link(ML) based power state (PS) transition
AP1
STA1
AP2
STA2
Link 1
Link 2
AP MLD & Non-AP MLD1
TWT SP
TWT Info frame
(Link 2)
LL Traffic mapped to Link 2 is arrived
TWT SP`
Ack
LL Data
BA
Non-AP MLD 1’s
ML PS transition delay
AP1
STA1
AP2
STA2
Link 1
Link 2
AP MLD & Non-AP MLD2
TWT SP
TWT Info frame
(Link 2)
LL Traffic mapped to Link 2 is arrived
TWT SP`
Ack
LL Data
BA
Non-AP MLD 2’s
ML PS transition delay

## Slide 6: Conclusion
We proposed a method to provide more reliable transmission during multi-link based TWT SP
  When the AP MLD reschedules TWT SP using ML Flexible TWT, AP MLD will consider non-AP MLD’s capabilities for the multi-link based power state transition

## Slide 7: References
[1] 11bn PAR 23/0078
[2] P802.11 be Draft 5.1

## Slide 8: Straw Poll
Do you agree to add the following text to TGbn SFD?
  When an AP MLD reschedules a TWT SP of a non-AP MLD MLD using ML Flexible wake time, the AP MLD should consider non-AP MLD’s multi-link power state transition delay
    The details are TBD