## Slide 1: Improving Stability during Roaming Process
Date: 2024-5-11
Authors:

## Slide 2: Introduction
Roaming is one of the main topics discussed by the TGbn group. Multiple companies have suggestions of how the roaming may accomplished [1-4].

## Slide 3: Recap
One of the main ideas regarding roaming is defining a new entity, which will handle seamless roaming process. We call it controller in this presentation.

## Slide 4: Back and Forth Roaming between AP-MLDs
If the non-AP MLD is in between two AP MLDs with fluctuating relative received signal power levels, non-AP MLD may roam back and forth between AP MLDs. Such an action would cause the roaming procedure to be inefficient.

## Slide 5: Cancellation of Roaming
A roaming cancellation message could be introduced for non-AP MLD cancel the roaming process without waiting for its finalization, as soon as it detects a change in the relative signal power level.
After the reception of the roaming
cancellation frame, received AP MLD
informs Controller and Controller
informs other AP MLD about the
cancellation.

## Slide 6: Conclusion
A method to improve stability during the roaming process is introduced.
The method will enable cancellation of the roaming process. A non-AP MLD may be allowed to cancel the process to prevent inefficiency in back and forth roaming process.

## Slide 7: References
[1] 11-23/279r0 Considerations on Seamless Roaming
[2] 11-23/1416r0 Seamless Roaming Follow-up
[3] 11-23/1184r0 Seamless Roaming
[4] 11-24/0052r0 Seamless Roaming Details