## Slide 1: Unequal Modulation Insights
Date: 2024-07-04
Authors:

## Slide 2: Introduction
In [1-4], there exist detailed discussions on UEQM gains and UEQM pattern selection.
In this contribution, we present our insights on UEQM.

## Slide 3: Simulation Methodology
For each channel model (B-LOS and D-NLOS) and for each scenario (e.g. 2x2, 4x4), at each SNR, we randomized ~1000 channel realizations
For each channel realization we tested the performance of each MCS (single stream) or combination of MCS/modulation (multi-stream)
Based on the results, and assuming perfect link/rate-adaptation, we choose the MCS (or combination of MCS values) that yields the highest goodput for each channel realization
  For example, in a certain 4x4 channel realization, 1 stream may be chosen (depending on SNR and channel realization)
  Compared between EQM and EQM+UEQM
We used perfect link/rate-adaptation and perfect channel estimation (in both sounding NDP as well as data PPDU), and ignored sounding overhead
We generated the goodput assuming as well as the MCS/modulation combinations that were chosen

## Slide 4: 2x2 results
The results for the 2x2 case are given below; we see that UEQM yields ~1-2dB at the medium to high SNR range
Limiting to modulation order difference of 2 has a small impact

## Slide 5: 4x4 results
The results for the 4x4 case are given below; we see that unlimited UEQM yields ~1-3dB at the medium to high SNR range
Limiting to modulation order difference of 2 has a small impact, however the combinations suggested in [1] reduce the gain at high SNR by ~1.5dB

## Slide 6: Chosen Combinations
The following modulation combinations were chosen for the 2 stream case:
Ch = 2x2 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 31
1 | 2 | 0 | 28.1
2 | 0 | 0 | 21.1
3 | 3 | 0 | 17.7
4 | 4 | 0 | 1.9
Ch = 3x3 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 48.7
1 | 0 | 0 | 30.2
2 | 2 | 0 | 16.9
3 | 3 | 0 | 4.2
Ch = 4x4 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 52.5
1 | 0 | 0 | 39.2
2 | 2 | 0 | 7.6
Ch = 2x2 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 2 | 0 | 34.7
1 | 1 | 0 | 26.5
2 | 3 | 0 | 21.8
3 | 0 | 0 | 14.8
4 | 4 | 0 | 1.92
Ch = 3x3 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 46.0
1 | 2 | 0 | 26.9
2 | 0 | 0 | 19.2
3 | 3 | 0 | 7.8
Ch = 4x4 NSS = 2 (>1%) |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 56.2
1 | 0 | 0 | 29.9
2 | 2 | 0 | 12.7
2 | 3 | 0 | 1.2
B-LOS
D-NLOS

## Slide 7: Chosen Combinations
The following modulation combinations were chosen for the 3 stream case:
B-LOS
D-NLOS
Ch = 3x3 NSS = 3 (>1%) |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 1 | 1 | 0 | 17.9
1 | 3 | 1 | 0 | 13.6
2 | 4 | 3 | 0 | 13.0
3 | 3 | 2 | 0 | 12.9
4 | 2 | 1 | 0 | 12.6
5 | 2 | 2 | 0 | 9.3
6 | 3 | 3 | 0 | 7.8
7 | 4 | 2 | 0 | 4.9
8 | 0 | 0 | 0 | 3.2
9 | 4 | 4 | 0 | 2.1
Ch = 4x4 NSS = 3 (>1%) |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 2 | 1 | 0 | 27.9
1 | 3 | 1 | 0 | 23.5
2 | 3 | 2 | 0 | 10.5
3 | 2 | 2 | 0 | 7.6
4 | 1 | 1 | 0 | 6.5
5 | 0 | 0 | 0 | 5.8
6 | 1 | 0 | 0 | 5.6
7 | 2 | 0 | 0 | 3.6
8 | 4 | 3 | 0 | 3.2
9 | 4 | 2 | 0 | 2.8
10 | 3 | 3 | 0 | 1.5
Ch = 3x3 NSS = 3 (>1%) |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 1 | 1 | 0 | 16.4
1 | 3 | 1 | 0 | 15.4
2 | 4 | 3 | 0 | 15.3
3 | 3 | 2 | 0 | 15.0
4 | 2 | 1 | 0 | 12.1
5 | 2 | 2 | 0 | 9.0
6 | 3 | 3 | 0 | 6.6
7 | 4 | 2 | 0 | 6.5
8 | 0 | 0 | 0 | 1.3
Ch = 4x4 NSS = 3 (>1%) |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 2 | 1 | 0 | 28.5
1 | 3 | 1 | 0 | 28.1
2 | 3 | 2 | 0 | 10.7
3 | 1 | 0 | 0 | 5.7
4 | 2 | 2 | 0 | 4.9
5 | 0 | 0 | 0 | 4.7
6 | 1 | 1 | 0 | 4.6
7 | 4 | 2 | 0 | 3.9
8 | 2 | 0 | 0 | 3.8
9 | 4 | 3 | 0 | 2.8
10 | 3 | 0 | 0 | 1.2

## Slide 8: Chosen Combinations
The following modulation combinations were chosen for the 4 stream case:
B-LOS
D-NLOS
Ch = 4x4 NSS = 4 (>1%) |  |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Percentage(%)
0 | 4 | 4 | 4 | 0 | 12.2
1 | 4 | 3 | 2 | 0 | 9.7
2 | 3 | 3 | 3 | 0 | 7.8
3 | 2 | 2 | 2 | 0 | 7
4 | 3 | 2 | 1 | 0 | 6.6
5 | 3 | 3 | 2 | 0 | 6.4
6 | 2 | 2 | 1 | 0 | 5.7
7 | 1 | 1 | 1 | 0 | 5.2
8 | 4 | 4 | 2 | 0 | 4.9
9 | 3 | 3 | 1 | 0 | 4.6
10 | 4 | 4 | 3 | 0 | 3.9
11 | 4 | 4 | 1 | 0 | 3.6
12 | 0 | 0 | 0 | 0 | 3.4
13 | 4 | 3 | 1 | 0 | 3.2
14 | 3 | 2 | 0 | 0 | 2.1
15 | 4 | 2 | 1 | 0 | 2.1
16 | 3 | 2 | 2 | 0 | 1.7
17 | 3 | 1 | 1 | 0 | 1.4
18 | 2 | 2 | 0 | 0 | 1.2
19 | 5 | 4 | 3 | 0 | 1.0
Ch = 4x4 NSS = 4 (>1%) |  |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Percentage(%)
0 | 4 | 4 | 4 | 0 | 11.1
1 | 4 | 3 | 2 | 0 | 11.0
2 | 3 | 2 | 1 | 0 | 7.7
3 | 3 | 3 | 2 | 0 | 7.5
4 | 3 | 3 | 3 | 0 | 7.1
5 | 2 | 2 | 2 | 0 | 6.8
6 | 2 | 2 | 1 | 0 | 5.9
7 | 4 | 4 | 2 | 0 | 5.1
8 | 1 | 1 | 1 | 0 | 4.7
9 | 3 | 3 | 1 | 0 | 4.3
10 | 4 | 4 | 1 | 0 | 3.7
11 | 4 | 4 | 3 | 0 | 3.5
12 | 4 | 3 | 1 | 0 | 3.4
13 | 4 | 2 | 1 | 0 | 3.3
14 | 0 | 0 | 0 | 0 | 3.1
15 | 3 | 2 | 2 | 0 | 2.1
16 | 3 | 1 | 1 | 0 | 1.3
17 | 3 | 2 | 0 | 0 | 1.3
18 | 5 | 4 | 3 | 0 | 1.1
19 | 4 | 2 | 2 | 0 | 1.0
20 | 4 | 3 | 3 | 0 | 1.0

## Slide 9: Summary
Assuming perfect link/rate-adaptation, UEQM can yield 1-2dB gain over using only EQM
  This is a non-negligible benefit
  However, these results are achieved assuming perfect CHEST and perfect link/rate-adaptation, so gain is expected to be lower in practice
Considering the fact that spatial domain UEQM is relevant only when MIMO+BF is used, the impact it will have on practical link/rate-adaptation (far more valid options to choose from) and the required signaling & protocol changes (e.g. PHY preamble, possibly sounding feedback), we need to think if this is one of the important PHY approaches we want to promote in TGbn

## Slide 10: References
[1] 11-24-0469-00-00bn-new-mcss-for-11bn
[2] 11-24-0474-01-00bn-uhr-unequal-modulation-pattern-and-new-mcs
[3] 11-24-0498-01-00bn-unequal-modulation-in-mimo-txbf-and-new-mcs-for-11bn
[4] 11-24-0469-00-00bn-new-mcss-for-11bn
[5] 11-24-0438-00-00bn-ueqm-benefit-analysis
[6] 11-24-0439-00-00bn-ueqm-evaluation-and-simulation-results
[7] 11-24-0734-01-00bn-on-ueqm-and-ueq-mcs
[8] 11-24-0507-02-00bn-ueqm-further-details

## Slide 11: MCS pattern selection methodology – link adaptation based method
Besides Goodput based method shown in previous slides, we also tested other solutions.
For a specific channel (ChB NLOS, ChD NLOS), and a specific spatial configuration <4T,4R>, <3T,3R>, <2T,2R>:
  For EQM, the SNR threshold to achieved for 10% PER first.
  Then, for each channel realization (among 10,00 realizations*[0:1:50dB] SNR), the post-SNR of each SS is obtained respectively.
  For each channelization, the appropriate QAM and rate is chosen for SS with lowest SNR first and SNR threshold, then the appropriate QAM is chosen for other N-1 SS based on the SNR and SNR threshold respectively.
The method is to simulate a way of link adaptation, to choose MCS combinations based on SNR feedback.

## Slide 12: The MCS pattern probability for ChB NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <2T,2R,2SS are shown below. The number under the ith SS is the modulation order gap between the ith SS and the last/base SS.
Ntx = Nrx = 2, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 2 | 0 | 34.27
1 | 3 | 0 | 21.39
2 | 1 | 0 | 16.48
3 | 4 | 0 | 5.3
4 | 0 | 0 | 1.03

## Slide 13: The MCS pattern probability for ChB NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <3T, 3R, 3SS>, <3T,3R,2SS> are shown below. The number under the ith SS is the modulation order gap between the ith SS and the last/base SS.
Ntx = Nrx = 3, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 2 | 0 | 14.45
1 | 1 | 0 | 13.32
2 | 3 | 0 | 3.34
3 | 0 | 0 | 1.34
Ntx = Nrx = 3, NSS = 3 |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 3 | 2 | 0 | 15.2
1 | 4 | 2 | 0 | 11.54
2 | 4 | 3 | 0 | 10.87
3 | 3 | 1 | 0 | 7.79
4 | 2 | 1 | 0 | 4.73
5 | 3 | 3 | 0 | 3.22
6 | 5 | 3 | 0 | 2.99
7 | 5 | 4 | 0 | 2.8
8 | 2 | 2 | 0 | 2.11
9 | 4 | 1 | 0 | 1.67
10 | 4 | 4 | 0 | 1.37

## Slide 14: The MCS pattern probability for ChB NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <4T,4R,4SS>, <4T,4R,3SS>, <4T,4R,2SS> are shown below. The number under the ith SS is the modulation order gap between the ith SS and the last/base SS.
Ntx = Nrx = 4, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 1.37
Ntx = Nrx = 4, NSS = 3 |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 3 | 2 | 0 | 12.15
1 | 2 | 1 | 0 | 10.08
2 | 3 | 1 | 0 | 7.8
3 | 2 | 2 | 0 | 3.61
4 | 4 | 2 | 0 | 3.48
5 | 4 | 3 | 0 | 2.24
6 | 3 | 3 | 0 | 1.41
7 | 1 | 1 | 0 | 1.29
8 | 2 | 0 | 0 | 1.1
Ntx = Nrx = 4, NSS = 4 |  |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Percentage(%)
0 | 4 | 3 | 2 | 0 | 7.86
1 | 5 | 4 | 2 | 0 | 5.59
2 | 4 | 3 | 1 | 0 | 5.31
3 | 4 | 4 | 2 | 0 | 4.34
4 | 5 | 4 | 3 | 0 | 4.13
5 | 3 | 3 | 1 | 0 | 3.02
6 | 3 | 3 | 2 | 0 | 2.94
7 | 3 | 2 | 1 | 0 | 2.92
8 | 4 | 4 | 3 | 0 | 2.69
9 | 5 | 3 | 2 | 0 | 2.46
10 | 4 | 2 | 1 | 0 | 1.86
11 | 5 | 5 | 3 | 0 | 1.41

## Slide 15: The MCS pattern probability for ChD NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <2T,2R,2SS> are shown below:
Ntx = Nrx = 2, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 2 | 0 | 40.2
1 | 3 | 0 | 18.58
2 | 1 | 0 | 17.75
3 | 0 | 0 | 2.19
4 | 4 | 0 | 1.88

## Slide 16: The MCS pattern probability for ChD NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <3T,3R,3SS>, <3T,3R,2SS> are shown below:
Ntx = Nrx = 3, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 2 | 0 | 11.96
1 | 1 | 0 | 11.55
Ntx = Nrx = 3, NSS = 3 |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 3 | 2 | 0 | 21.9
1 | 4 | 2 | 0 | 11.72
2 | 2 | 2 | 0 | 10.74
3 | 4 | 3 | 0 | 7.88
4 | 3 | 1 | 0 | 7.75
5 | 2 | 1 | 0 | 5.4
6 | 3 | 3 | 0 | 4.1
7 | 1 | 1 | 0 | 3.01

## Slide 17: The MCS pattern probability for ChD NLOS
Using LA based method, the MCS pattern probability (>1%) for specific spatial configurations <4T,4R,4SS>, <4T,4R,3SS>, <4T,4R,2SS> are shown below:
Ntx = Nrx = 4, NSS = 3 |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Percentage(%)
0 | 2 | 1 | 0 | 12.5
1 | 3 | 2 | 0 | 9.72
2 | 3 | 1 | 0 | 6.56
3 | 2 | 0 | 0 | 1.33
Ntx = Nrx = 4, NSS = 4 |  |  |  |  | 
index | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Percentage(%)
0 | 4 | 3 | 2 | 0 | 15.48
1 | 3 | 3 | 2 | 0 | 14.43
2 | 4 | 3 | 1 | 0 | 5.59
3 | 2 | 2 | 1 | 0 | 3.92
4 | 3 | 3 | 1 | 0 | 3.64
5 | 4 | 4 | 3 | 0 | 3.18
6 | 3 | 2 | 1 | 0 | 3.17
7 | 5 | 4 | 2 | 0 | 3.05
8 | 4 | 4 | 2 | 0 | 2.93
9 | 5 | 4 | 3 | 0 | 2.65
10 | 2 | 2 | 2 | 0 | 2.22
11 | 5 | 3 | 2 | 0 | 1.39
12 | 4 | 2 | 1 | 0 | 1.3
13 | 3 | 3 | 3 | 0 | 1.1
Ntx = Nrx = 4, NSS = 2 |  |  | 
index | Stream 1 | Stream 2 | Percentage(%)
0 | 1 | 0 | 1.02