## Slide 1: Coexistence of Wi-Fi with Narrowband Technology
Date: 2024-07-16
Authors:
Notes: Explain line of thought, add pauses
Send Guido photos without labels to add blurring
My name and Prof. Lambadaris

## Slide 2: Abstract (1)
In 2020, CEPT/ECC opened the 5945 MHz to 6425 MHz band for license-exempt Wireless Access System/Radio Local Area Network (WAS/RLAN) operation in Europe [1]
  This decision also permits for Narrowband Frequency Hopping (NB FH) operation
The Bluetooth SIG [2] and other entities announced their interest to operate NB FH equipment in the license-exempt 6 GHz band
  In the future, NB FH devices are likely to share the wireless spectrum with devices operating according to the IEEE 802.11 standard [3]

## Slide 3: Abstract (2)
To estimate how IEEE 802.11 and NB FH devices may be coexisting in the future, we are subjecting commercial (enterprise) IEEE 802.11 devices with NB FH signals and measuring the IEEE 802.11 devices’ capability to detect NB FH transmissions as well as to receive IEEE 802.11 transmissions interfered by concurrent NB FH signals
Because of easier commercial availability, all tests are conducted with devices operating in the license-exempt 5 GHz
  Nonetheless, the gained insights are relevant for the discussion of the aspect of coexistence in the 6 GHz band, too

## Slide 4: Abstract (3)
The IEEE 802.11-2020 standards define a global framework for Wi-Fi devices [3]
  Section 17.3.10.6 defines requirements for clear channel assessment (CCA)
  According to the standard, the CCA mechanism shall detect the medium as busy within 4 μs of any signal with a received energy that is 20 dB above the most robust modulation and coding (MCS) rate sensitivity
  In the case of a 20 MHz channel, the standard defines this value as −82 dBm + 20 dB = −62 dBm, which will be referred to as the Energy Detection Threshold (EDT)

## Slide 5: Testbed Setup

## Slide 6: Test setup overview
Linux PC-2
Signal Analyzer
ATTN-2
USRP – B210
AP1
ATTN-1
AP2
⑫ RF Isolation Chamber
Linux PC-1
−30 dB ATTN
Coaxial
Ethernet
USB
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑪
−30 dB
−3 dB
−3 dB
⑩
−24 dB
−1.3 dB
−1.3 dB
⑬

## Slide 7: Impact on transmitting vs. receiving side
Test signal added to traffic source
  Analyzing energy detection
Interference signal added to traffic sink
  Analyzing robustness of receiver
Notes: Mention results will be presented in 2 parts

## Slide 8: Testbed settings (1)
All measurements rely on conducted setups
  Provides for a high isolation against external factors
  Additionally, equipment is operated within a Radio Frequency (RF) isolation chamber
Devices are operated on IEEE 802.11 5 GHz channel 36 (fc = 5180 MHz)
The Ettus Research USRP B210 Software Defined Radio (SDR) is used to generate arbitrary test signals
We observe the performance of an IEEE 802.11 link between a transmitting and a receiving device
  We use iperf3 to offer UDP traffic to the transmitting device
  Therefore, the receiving device does not transmit data packets and limits itself to transmitting Control frames (e. g. IEEE 802.11 ACK) and necessary Management frames
  When using OpenWRT between devices with different chipset vendors, iperf3 is run on the receiving device directly without the cost of extraneous CPU usage

## Slide 9: Testbed settings (2)
The traffic source offers slightly more traffic than the IEEE 802.11 link’s capacity
  Therefore, in all measurements (graphs etc.) the maximum throughput is 90 % of the nominal throughput
Where a Device under Test (DUT) records additional metrics, we use this data to further analyze the measurement results
  E. g., statistics related to transmitted and discarded packets, percentage that the wireless medium was observed occupied
To calibrate the testbed setup and to estimate absolute values, we use the Agilent (Keysight) MXA signal analyzer N9020A
  Power is measured with an integrated bandwidth of 20 MHz
Gaussian noise-based test signal
  A technology agnostic signal whose primary characteristics of interest are bandwidth and power

## Slide 10: Test setup, details
Transmitting AP
  Operated in bridge mode if possible
iperf3 traffic source
iperf3 traffic sink
Receiving STA/AP
  Operated in bridge mode if possible
SDR generating test signals
Antenna combiner, type A
Antenna combiner, type B
Antenna combiner, type B
Variable attenuator
Variable attenuator
Signal analyzer
RF isolation chamber
Antenna combiner, type A
DUT: Device Under Test
Notes: The antenna combiner next to AP2 is not numbered

## Slide 11: Static Gaussian Test Signals
Time-Domain Representation of Test Signals (MATLAB)
PSD Representation of Test Signals (Signal Analyzer)
PSD Representation of Test Signals (MATLAB)
Notes: Spend more time discussing the signal properties

## Slide 12: Dynamic (On-Off) 2 MHz Test Signals
Dwell Time defined as the active portion of signal block (on-time)
Duty Cycle defined as the percentage of the signal block that the signal is active
On-Off traffic is constructed by varying these time-domain parameters as shown to the right
2 MHz Test Signal with 100 µs Dwell Time and 10% Duty Cycle

## Slide 13: Frequency Hopping Emulation
67.5 ms
7.5 ms
Essentially a frequency hopping signal with a 7.5 ms Dwell Time and 10 % Duty Cycle

## Slide 14: Energy Detection capabilities
Energy Detection performance with signals of less than 20 MHz bandwidth

## Slide 16: Test 1: Energy Detection of Broadband vs. Narrowband
Experiment:
  Assess Energy Detection level of transmitting device using 20 MHz and 2 MHz test signals
    Country Code set to Canada
    EDT set to –62 dBm where applicable
    Test signal transmitted at center frequency of channel 36
Observations
  Narrowband test signal is measured differently than broadband test signal in both devices
  Experimental EDT differs between devices and between the IEEE 802.11-2020 prescribed value
Device 1
Device 2
Notes: 2 devices from 2 different vendors using 2 different chip manufacturers

## Slide 17: Test 1: Additional Supporting Metrics
Device 1 enables us to monitor live radio traffic statistics from the command line interface (CLI)
One useful metric is data retries over a 5 s window
Nominally, without a test signal present we expect ca. 2200 successful transmissions and 0 retries
We observe that although the throughput decreases, there is not a proportional increase in the number of retransmissions
  Indicates an inaccurate energy measurement of the signal and throttling of transmissions, not packet corruption
Without loss of generality, this was observed for all transmitter-side tests
Device 1

## Slide 18: Test 2: Detection of 312.5 kHz wide test signals
Experiment:
  Place a 312.5 kHz test signal at the center frequency, a random data tone (D24), a pilot tone (P7), and just right of the last sub-carrier (D47 + 312.5 kHz)
Observations:
  Device 1 is able to perform EDT consistently at different carrier frequencies within the channel
  Device 2 does not measure the test signal as accurately as the test 1 results, and is insensitive to the test signal at the center of the channel
Device 1
Device 2

## Slide 19: Test 3: Frequency Hopping—Part 1
Experiment
  Evaluate energy detection performance in presence of a 2 MHz test signal placed at increasing 1 MHz offsets from center of IEEE 802.11 5 GHz channel 36
Observations
  Both devices are less sensitive at the channel edge, in Device 2 CCA is not performed at all at 5189 MHz
    Indicates device 2 has a better out-of-band rejection filter as this frequency is outside the occupied channel bandwidth
Device 1
Device 2

## Slide 20: Test 4: Frequency Hopping—Part 2
Experiment
  Energy detection evaluation in response to an on-off 2 MHz test signal above the measured EDT at 5180 MHz
  Energy detection evaluation in the presence of a frequency hopping 2 MHz test signal above the measured EDT
Expected Throughput
  Offered load selected to yield 90 % of the nominal throughput without test signal present
  For a 10 % duty cycle, we would expect the device to perform CCA 10 % of the time, yielding an expected throughput of 0.9 × 90 % = 81 %
  For a 50 % duty cycle, we would expect the device to perform CCA 50 % of the time, yielding an expected throughput of 0.5 × 90 % = 45 %
Observations:
  Device 1 experiences expected throughput for longer dwell times
  Device 2 experiences better than expected throughput for short dwell times, and expected throughput for longer dwell times

## Slide 21: Receiver-side Tests
Packet reception performance in the presence of simultaneously inserted interference signals

## Slide 23: Test 1: Broadband vs. Narrowband
Experiment:
  MCS: IEEE 802.11a BPSK ½
  PRX: −50 dBm
  20 MHz vs. 2 MHz Gaussian interference signals centered @ fc = 5180 MHz
  The Wi-Fi station acting as an AP on the transmitter side dissociates on low acknowledgement
Observation:
  Both devices disconnect at the same power level for a 20 MHz signal at around –57 dBm and −58 dBm respectively
  Device 1 is more impacted by the 2 MHz signal, whereas device 2 is more impacted by the 20 MHz signal
Device 1
Device 2

## Slide 24: Test 1: Additional Supporting Metrics
On the receiver side, we observe the data retries concurrently with the throughput for device 1
We see that the number of retransmissions increases proportionally to the throughput drop, indicating that loss in throughput at the receiver side is due to packet loss
Without loss of generality, this trend holds true for all receiver side coexistence tests
Device 1

## Slide 25: Test 1: Additional Supporting Metrics—Device 2
Although we are unable to view the radio statistics on device 2, it needs to be verified that a loss of throughput is not a result of CCA
To rule out CCA as the reason for a throughput loss, varying PRX should vary the point where the connection is lost accordingly
  As shown to the right, increasing PRX increases the point at which the connection is dropped

## Slide 26: Test 2: 312.5 kHz Interference to Assess Sub-Carrier Susceptibility
Experiment
  MCS: IEEE 802.11a BPSK ½
  PRX: −50 dBm
  312.5 kHz interference signal placed at the center frequency, a random data tone (D24) and a random pilot tone (P7)
  The Wi-Fi station acting as an AP on the transmitter side dissociates on low acknowledgement
Observation
  In device 1, it is clear that interfering with a pilot sub-carrier is more harmful to the Wi-Fi traffic than a data sub-carrier, and interfering at the null tone has minimal impact as expected
  In device 2, these discrepancies are less noticeable, although the dissociation point for the three cases follow the same order as device 1
Device 1
Device 2

## Slide 27: Test 3: Higher-Order MCS
Experiment
  MCS: IEEE 802.11ac MCS 7
  PRX increased to −35 dBm
    To account for higher order MCS
  Assess 20 MHz and 2 MHz interference signals @ fc = 5180 MHz (100 % Duty Cycle)
  Evaluate if error detection and correction mechanisms offer better performance
  Can only perform test on Device 1 due to limited MCS control on OpenWRT
Observations
  We still see a greater throughput loss in the presence of narrowband interference
  We see less drastic of a difference between broadband and narrowband interference signals
IEEE 802.11ac MCS 7 Results
IEEE 802.11a BPSK 1/2 Results

## Slide 28: Test 3: Frequency Hopping Part 1
Experiment
  MCS: IEEE 802.11a BPSK ½
  PRX = −50 dBm
  Assess 2 MHz interference placed at fc = 5180 MHz + {0, 1, 2, 3, 4, 5, 6, 7, 8, 9} MHz
Observations
  Both devices are least sensitive to the test signal placed at the edge of the channel, with device 2 not dissociating up to an interference power of –50 dBm at this frequency placement
Device 1
Device 2

## Slide 29: Test 3: Frequency Hopping Part 2
Experiment:
  MCS: IEEE 802.11a BPSK ½
  PRX = −50 dBm
  Run a 2 MHz interference signal with different dwell times and duty cycles at 5180 MHz
    Run the interference using the described hopping algorithm
Observations
  Short dwell-times cause connection to dissociate due to every packet experiencing interference for a fraction of the packet duration
  Hopping with a 7.5 ms dwell-time and a 10 % duty cycle is equivalent to using an on-off signal with the same parameters at 5180 MHz, both of these result in the least throughput loss
Device 1
Device 2

## Slide 30: Side-By-Side Analysis of Transmitter and Receiver Results

## Slide 31
Device 1
Device 2
Compared to device 2, device 1 struggles to accurately detect narrowband traffic
Device 2 is more robust against narrowband traffic than device 1
Device 1
Device 2
Notes: Blue colour is different here, need to make it the same
Captions in larger font / bolded

## Slide 32
Device 1 performs CCA better at the center frequency where there is a notch than device 2
Device 2 has a sharper filter in that a signal at the channel edge, which is outside the occupied bandwidth, is not detected
Device 1 is more sensitive to narrowband traffic at the receiver side than device 2
Device 1
Device 2
Device 1
Device 2
Notes: Colours (yellow) on graphs need to be consistent
Caption font larger (match with middle text)

## Slide 33: Adaptive Energy Detection Threshold

## Slide 35: Background
While assessing the CCA mechanism of two additional commercial devices with the same chipset manufacturer, an adaptive energy threshold was observed
  Noise Floor visibly increases in the presence of Gaussian Test signal, proportional to the test signal power
  The EDT is calculated internally within the device as the: EDT Value = adapted noise floor + fixed offset
  In some cases, this causes the device to become “deaf” to the test signal after some time and not defer its transmissions
  Primarily in response to 20 MHz Gaussian Test Signal

## Slide 36: Time-Domain Visualization of Noise Floor Calibration
Device 3
Device 4

## Slide 37: Impact on Throughput
Experiment:
  Assess Energy Detection level of transmitting device using 20 MHz and 2 MHz test signals both before and after internal noise floor calibrations
    Country Code set to Canada
    Test signal transmitted at fc = 5180 MHz
    Device 4 uses IEEE 802.11n BPSK ½ due to configuration limitations
Observations
  In both cases, the noise floor calibration allows for higher transmission over the 20 MHz test signal
  Both devices measure narrowband signals very inaccurately and backoff even at low signal powers
Device 4
Device 3

## Slide 38: NB FH Impact
Experiment:
  Assess the impact of dynamic 2 MHz test signals on these devices at a power level above the experimental EDT
Observations
  In all cases better than expected throughput is achieved indicating that NB FH traffic does not have a disproportional impact on these devices' ability to perform CCA

## Slide 39: Conclusions
From our test results, narrowband traffic is not detected nor accounted for in the device design compared with broadband traffic by these commercial and enterprise-grade Wi-Fi devices
From our test results, rapid NB FH traffic does not disproportionately impact Wi-Fi's performance, and as demonstrated is less detrimental to an ongoing Wi-Fi connection
From our test results, there appear to be several inconsistencies amongst device implementations between different manufacturers and between the IEEE 802.11-2020 standards
Notes: No details available on
Work on this slide in Ottawa
Tone it down a bit: "In our tests, we observe...", "our tests show..."
Discussion in BRAN on definition of Narrowband
FH in American is permissible in 5 GHz
802.11 standard clearly states that you should do a power measurement

## Slide 40: References
[1] European Conference of Postal and Telecommunications Administrations, “ECC Decision (20)01 on the Harmonised Use of the Frequency Band 5945-6425 MHz for Wireless Access Systems Including Radio Local Area Networks (WAS/RLAN),” approved Nov. 20th, 2020.
[2] J.-L. Aufran, “Bluetooth LE To Support 6 GHz Frequency Band,” CNXSOFT, Nov. 21st, 2022. [Online]. Available: https://www.cnx-software.com/2022/11/21/bluetooth-le-6-ghz-frequency-band
[3] IEEE 802.11 Working Group, “IEEE Standard for Information technology—Telecommunications and information exchange between systems—Local and metropolitan area networks—Specific requirements—Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications,” IEEE Std. IEEE Std 802.11-2020, 2020.

## Slide 41: Appendix: Testbed Pictures