## Slide 1: Discussions on Non-Primary Channel Access
Date: 2024-06-18
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
The motion for Non-Primary Channel Access (NPCA) has passed during the May 2024 meeting as follows.
Move to add the following text to the TGbn SFD:
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.

## Slide 3: Introduction
The gain of NPCA comes from the following fact:
  When the occupied bandwidth of the OBSS transmission is smaller than the BSS operating bandwidth, the STAs in the BSS can utilize the idle channels within the BSS BW by performing NPCA
The basic operations of the AP and the non-AP STAs include:
  The AP and the non-AP STAs will switch to the NPCA primary channel (configured by the AP, e.g., in the Beacon frame) when detecting an OBSS packet on the primary channel, and switch back to the primary channel when the TXOP (obtained by the OBSS STA on the primary channel) ends
  Some conditions need to be met:
    The NPCA primary channel shall not be occupied by the OBSS transmission
    The occupied duration on the primary channel shall be long enough
In this contribution, we discuss several aspects of the NPCA operation, including:
  NPCA primary channel update
  Opportunistic power save for NPCA
  EDCA/MU EDCA for NPCA

## Slide 4: NPCA primary channel update
AP will announce NPCA related parameters in the Beacons and Probe response frames that it transmits, including the location of the NPCA primary channel
The AP may want to change the NPCA primary channel because of many reasons
  When the NPCA primary channel is near to the primary channel, it’s easily to be occupied by OBSS packet
  When the NPCA primary channel is far from the primary channel, narrow band STAs may not be served during NPCA operation
  AP may need to change the NPCA primary channel according to the current situation, OBSS traffic, STAs’ BW, etc.
Hence, we propose that the AP should be able to change the NPCA primary channel
  The change of the NPCA primary channel should be regarded as critical update of the BSS
  The AP needs to set the critical update related flags when it decides to change the NPCA primary channel

## Slide 5: Opportunistic power save for NPCA
NPCA provides more transmission opportunities, meanwhile, it also requires the STAs to detect the events that will trigger NPCA operation, and to perform the channel switching after detecting the NPCA events.
All of the above consumes power. Such power consumption may not be a problem when the STA has Low Latency or High Throughput traffic requirement, but can be a burden when the STA does not have such traffic requirement.
It is preferred that the STA can disable/enable the NPCA mode flexibly
Moreover, when a STA disables NPCA, it can perform opportunistic power save after detecting the NPCA events
  Since AP has switched to the NPCA primary channel, no data transmission is possible between the AP and the STA
  The power save duration is the length of the basic NAV that triggers the NPCA operation
  Note-the NPCA non-supportive STAs may also do so, but it requires such STAs to be able to detect the NPCA events

## Slide 6: Opportunistic power save for NPCA
If the AP already has a list of STAs that it intends to serve during NPCA, it can announce the list before hand, STAs that are not in the list can perform power save when detecting an NPCA event
The generation of the list depends on AP’s scheduling, based on non-AP STA’s traffic stream information
  Note-STAs not in the list can still do NPCA if it has urgent UL data to transmit.
Another option is, when AP switches to the NPCA primary channel after detecting an NPCA event, it can send an initial control frame (e.g., MU-RTS frame) to the STAs that it intends to serve on the NPCA primary channel, STAs that are not identified by the ICF can switch back to the primary channel, and do power save

## Slide 7: EDCA/MU EDCA for NPCA
In order to do data transmission, STAs need to perform EDCA after switching to the NPCA primary channel
Considering less STAs will contend under NPCA, smaller EDCA parameter values should be used
Considering the STAs are blind on the NPCA primary channel after switching, larger EDCA parameter values should be used
Hence, same or different EDCA parameter set can be used. If the AP wants to have different EDCA parameter set for the NPCA primary channel, it needs to announce it in the Beacon. Otherwise, it doesn’t include it in the Beacon.
  If the EDCA parameter set for the NPCA primary channel is not included, then the STAs will use the EDCA parameter set for the primary channel after switching to the NPCA primary channel
For MU EDCA, considering STAs may be triggered on the NPCA primary channel, will the STAs use MU EDCA parameter set after the successful UL data transmission?
  Disabling the MU EDCA operation on the NPCA primary channel is simpler

## Slide 8: Conclusion
We consider several aspects of NPCA in this contribution.
AP may change the NPCA primary channel, which is regarded as critical update event
STA can disable/enable the NPCA mode dynamically
When a STA disabled NPCA, it can do power save when detecting NPCA events
AP can proactively send a STA list for NPCA transmission to help STAs to save power
AP may or may not include the EDCA parameter set for the NPCA primary channel, if not included, the EDCA parameter set for the primary channel is used
MU EDCA can be disallowed on the NPCA primary channel

## Slide 9: References
[1] 11-23/34, “Non-primary channel utilization,” Sindhu Verma
[2] 11-23/1414, “Secondary channel usage follow up,” Liwen Chu
[3] 11-23/961, “UHR secondary channel access,” Minyoung Park
[4] 11-23/797, “Non-primary channel access,” Yongho Seok
[5] 11-23/1891, “Nonprimary channel access - follow up,” Gaurang Naik
[6] 11-23/2005, “Non-primary channel access (NPCA),” Minyoung Park
[7] 11-24/426, “EDCA for Non-Primary Channel Access,” Dongju Cha
[8] 11-24/427, “Enabling Non-Primary Channel Access,” Dongju Cha
[9] 11-24/486, “Some considerations on non-primary channel access,” Ming Gan
[10] 11-24/70, “Some details about non-primary channel access,” Yunbo Li