## Slide 1: Data forwarding for seamless roaming
Date: 2024-7-15
Authors:

## Slide 2: Introduction
TGbn agreed to define a mechanism that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after roaming to the other AP MLD[1].
There are some contributions on roaming procedure to enable this[2-4]. However, there may be UL suspension during roaming.
In this contribution, we see potential issues of seamless roaming procedure and what will be necessary for UL data continuity.

## Slide 3: Roaming with dual link
First, we see a roaming procedure when Source AP and Target AP are operating on same channel and there is no data forwarding from Source AP to Target AP[2].
Since Source AP and Target AP are operating on the same channel, STA can exchange frames simultaneously with Source AP and Target AP while links are enabled(dual link).

## Slide 4: Roaming procedure with dual link
STA may decide to roam and send roaming request to Source AP.
  Source AP may ack to the request.
After receiving the roaming request, Source AP transfers context and changes DS mapping to Target AP.
To keep DL data continuity, Source AP may transmit buffered DL packet to STA for TBD period.
STA suspends UL transmission while APs do context transfer and DS mapping change.
Source AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Source
AP
DL
Source
AP
+
Target
AP
Source
AP
UL
suspension
Target
AP
Delete link
Target
AP
Complete buffered DL transmission
Add link with Target AP

## Slide 5: Roaming with single link
However, Source AP and Target AP do not always operate on the same channel.
Source AP and Target AP may operate on different channel.
  For example, when distance between APs is narrow[5].
In such cases, STA cannot communicate with multiple AP simultaneously(single link).

## Slide 6: Roaming procedure with single link
In dual link case, STA can transmit UL to Target AP while receiving DL from Source AP.
However, in single link case, STA cannot transmit UL while receiving DL from Source AP.
After Source AP complete buffered DL transmission, STA can start transmitting UL to Target AP.
This causes longer UL suspension.
  Dropping buffered DL at Source AP could reduce this, but this causes DL discontinuity.
Source AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Source
AP
DL
Target
AP
Source
AP
UL
suspension
Target
AP
Complete buffered DL transmission
Delete link
Additional
UL suspension
Add link with Target AP

## Slide 7: Need for UL suspension minimization
Whether single or dual link, there is UL suspension during roaming.
However, in some cases, UL suspension should be minimized.
  AR/VR devices for the era of immersive experiences and the metaverse.
  mission-critical operations, such as manufacturing scenarios involving automatic guided vehicles, and smart agriculture applications for autonomous control of machines[6].
Therefore, it is necessary to reduce UL suspension duration, especially in single link case.

## Slide 8: How to minimize UL suspension
Minimization of UL suspension can be achieved by two possible solution.
To have Multi-radio capability at STA(MLMR).
  If STA is multi-radio, STA can exchange frames with Source AP and Target AP simultaneously and does not need to wait for buffered DL packet transmission.
To forward buffered DL data from Source AP to Target AP.
  By forwarding buffered DL data to Target AP and transmit them from Target AP could reduce UL suspension duration.

## Slide 9: Roaming procedure with MLMR STA
If STA has multi-radio capability, STA can transmit UL to Target AP while receiving DL from Source AP and Target AP. MLMR capability can mitigate UL suspension duration.
STA operating in EMLSR mode could have this capability[2].
Source AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Source
AP
DL
Source
AP
UL
suspension
Target
AP
Add link with Target AP
Delete link
Source
AP
+
Target
AP
Target
AP

## Slide 10: Roaming procedure with single link with DL data forwarding
With buffered DL data forwarding from Source AP to Target AP, STA does not need to wait for DL from Source AP and can start transmitting UL after link between Target AP becomes enabled.
  In some cases, Source AP cannot forward all buffered data due to amount of buffered data, backhaul condition, etc. In such cases, selective DL data forwarding may be needed.
Source AP can delete link with STA immediately after completing context transfer and DS mapping change.
Source AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Source
AP
DL
Target
AP
Source
AP
UL
suspension
Target
AP
Buffered data forwarding
Add link with Target AP
Delete link

## Slide 11: Other cases with DL data forwarding
Whether single or dual link, buffered DL data forwarding is useful in some cases.
For example, STA may disconnect from Source AP when
  Sudden RSSI drop happens[7].
  AP transitions to power save mode.
In such cases, buffered data forwarding from Source AP to Target AP and transmitting forwarded data from Target AP may help to keep data continuity.

## Slide 12: Summary
We show roaming procedure with single link and dual link and highlight the issue of UL suspension duration.
UL suspension duration can be minimized by enabling data forwarding between APs.

## Slide 13: SP1
Do you agree to define a mechanism in 11bn that minimizes UL suspension for a non-AP MLD that roams from one AP MLD to another AP MLD and can communicate with only one AP MLD at a time?

## Slide 14: SP2
Do you agree to define a mechanism in 11bn that enables an AP MLD to forward buffered data units that are addressed to a non-AP MLD which roams to another AP MLD?

## Slide 15: SP3
Do you agree to define a mechanism in 11bn that enables an AP MLD to forward selected buffered data units that are addressed to a non-AP MLD which roams to another AP MLD?
  How to select data is TBD.

## Slide 16: References
[1] 24/0209r3, “Specification Framework for TGbn”
[2] 24/0052r0, “Seamless Roaming details ,” Duncan Ho (Qualcomm Technologies, Inc.)
[3] 24/0396r0, “Seamless Roaming within a Mobility Domain – Follow Up,” Binita Gupta (Cisco Systems)
[4] 24/0412r0, “Seamless Roaming Procedure Follow-Up,” Yelin Yoon (LG Electronics)
[5] 24/0838r0, “Backhaul Design and Channel Setting for Multi-AP,” Kosuke Aio (Sony)
[6] 23/0079r10, ”UHR Draft Proposed CSD”
[7] 24/0398r0, “Coordinated Roaming through Target AP MLD,” Binita Gupta (Cisco Systems)