## Slide 1: Practical Multi-AP Coordination (MAPC) Scenarios
November 2024
Authors:
Name | Affiliation | Phone | email
Malcolm Smith | Cisco Systems |  | mmsmith@cisco.com
Binita Gupta | Cisco Systems |  | 
Brian Hart | Cisco Systems |  | 

## Slide 2: Problem Statement
Multi-service network that simultaneously supports:
  Low-latency channel access for multi-media, IIOT, XR, etc (~10ms)
  Ultra-reliable/ultra-low latency channel access for XR & IIOT/Wireless Time-Sensitive Networking (~1ms)
  Devices subject to irregular in-device coexistence (IDC) challenges
  Devices with P2P traffic
Managed contention/congestion from OBSS
  With optimizations within the same MANAGED administrative domain (e.g. TUA-O, R-TWT, MLO)
  With limited control over other UNAMNAGED administrative domains (e.g. QoS)
With:
  High system efficiency
  Implementation simplicity
  Acceptable fairness with legacy generations

## Slide 3: Key Traffic profiles
Wireless TSN (WTSN) e.g. IIOT, XR
  STA traffic synchronized to WLAN via 802.11 or 802.1 means e.g. 802.1Qbv/AS
  Rigid SCS QC parameters (SST, SI, etc)
  Target: 1ms 99.9% (at least)
Interactive real-time e.g. XR, UHD video conferencing
  STA traffic can be synchronized to WLAN via 802.11 means e.g. SCS QC, R-TWT
  Flexible SCS QC parameters (SST, SI, etc)
  Target: 1-10ms 99.9% (at least)
Collaboration/video-streaming
  STA traffic periodic but unsynchronized to WLAN
  Target 10-50ms 99.9% (at least)
Non-real-time (background) – aperiodic and unsynchronized

## Slide 4: QoS methods to manage delay congestion (My and OBSS)
QoS
  Apply VI/VO WMM/EDCA parameters to specific flows
  Available in Managed, SP and Enterprise WLANs
Triggered Uplink Access Optimization (TUA-O)
  Combined with SCS QoS Characteristics (QC) – period/SI, delay bound, etc.
  Expected availability in managed, SP and Enterprise WLANs
  STA requests via SCS QC and AP aligns traffic with MU trigger with e.g. TWT, R-TWT. SCS QC
MLO
  eMLSR expected to be commonly available in most WLANs
  Delay optimized mode assumed (i.e. first non-CS link )
Restricted TWT (R-TWT)
  Mapped to 802.1Qbv gate (time-slot reservation) for Wireless TSN (WTSN) applications
  Expected to be supported by a limited device set but not universally honored (e.g. legacy)
MAPC (C-R-TWT/C-SP/C-TDMA/etc)
  Under consideration by 802.11bn
  Details provided as needed

## Slide 5: BSS Coordination model
Managed WLAN
  QOS (WMM) [assumed default]
  Wi-Fi 7 (TUA-O/SCS-QC, R-TWT)
  SCS-QC driven scheduled MAPC service periods (SP)  e.g. C-R-TWT, C-SP
  Priority and/or SCS-driven on-demand (in – TXOP) MAPC coordination  e.g. C-TDMA
Managed to P2P/Unmanaged WLAN
  Uncoordinated (e.g. WMM QOS) [assumed default]
  Sharing of priority and SP needs (e.g., SCS-based)
  Negotiation of SPs

## Slide 6: Practical QoS analysis objectives
Baseline performance with pre-11bn methods on existing 5GHz/40MHz WLAN
  Most interference expected to be non-QoS or otherwise uncoordinated
Predict incremental gains with emerging 6GHz WLAN
  80MHz BW expected min. in dense environments (Enterprise, MDU, etc.)
Determine scenarios where MAPC provides key QoS benefits

## Slide 7: Analysis approach/parameters
Simulation-based with empirical validation (e,g. Wi-Fi7 TUA-O, Wireless TSN/R-TWT, etc)
My BSS and OBSS co-channel (CCI) modeled as best-effort (AC-BE) offered-load (Poisson) to achieve a target Channel Utilization (CU) with ‘heavy’ (60KB) payload
Real-time (RT) offered-load from either uplink
  Video (VI) [35ms period, 10KB/frame, 2.2Mb/s] with 35ms (default) MU-EDCA TO for TUA-O
  XR pose (VI/VO) [10ms period, 100B/frame, 80Kb/s] with 10ms MU-EDCA TO for TUA-O
Enterprise density assumed
  25 BE and 5 BE STA per AP
  Either one AP (non-MAPC) or (for MAPC) 4 identical co-channel APs (i.e. 25x4+5x4=120 STA)
  Average MCS 7 (81Mb/s @ 20MHz w/ 1 SS)
Only uplink channel ACCESS delay estimated (queueing delay ignored for now)

## Slide 8: Baseline: Wi-Fi 7 (Typical average peak load)
1 BSS Video
40MHz
Avg. 50% target CU
Only WTSN needs a specific QoS method (R-TWT)
*WTSN Qbv
Chart: Latency vs. mode
| No QOS | QOS (WMM) | MLO (+WMM) | TUA (+WMM) | R-TWT (+WMM)
90%-ile | 5.4 | 4 | 3.8 | 3.3 | 1
99%-ile | 5.8 | 4 | 3.5 | 2.4 | 0.1
99.9%-ile | 9.4 | 4.5 | 3.8 | 1 | 0.9

## Slide 9: Baseline: Wi-Fi 7 (High load)
1 BSS Video
40MHz
Avg. 90% CU
TUA-O needed to meet interactive-real-time/XR
R-TWT needed for WTSN
Chart: Latency vs. mode
| No QOS | QOS (WMM) | MLO (+WMM) | TUA (+WMM) | R-TWT (+WMM)*
90%-ile | 45 | 21 | 16 | 8.3 | 1
99%-ile | 150 | 19 | 13 | 8 | 0.1
99.9%-ile | 55 | 13.6 | 10 | 5.5 | 0.9
* WTSN Qbv

## Slide 10: Baseline: Wi-Fi 7 in 6GHz
1 BSS Video
TUA-O
Avg. 90% CU
40->80MHz close to meeting interactive-real-time /XR reqs.
WTSN reqs. not met
Chart: Delay vs. BW
| 40MHz | 80MHz | 160MHz
90%-ile | 10.3 | 4.3 | 2.6
99%-ile | 13.2 | 5.1 | 3.4
99.9%-ile | 4.4 | 2.2 | 1.8

## Slide 11: Practical MAPC formulation
Migration from 5GHz (40MHz) to 6Ghz (80/160MHz) will likely support low-latency (10ms) for a single BSS (no CCI) even at high CU (90%)
Ultra-low-latency (1ms) can be met via R-TWT if universally adopted
Multi-AP (CCI) will degrade latency further, so we expect TUA or R-TWT to be needed to meet ultra or low latency requirements.
For our 4 co-channel AP scenario, each AP uses QoS/WMM or TUA-O
WTSN worst-case whereby TUA-O operation is aligned across all APs (e.g. SCS QC have COMPETING Start-Time)
  NOTE TUA-O is a proxy for R-TWT under unmanaged BSS CCI

## Slide 12: MAPC: TUA-O vs. QOS (WMM)
4 BSS Video
Avg. 90% CU
TUA-O can perform worse than QOS/WMM
(continued on next slide)
Chart: 99.9% Delay vs. BW
| 40MHz | 80MHz | 160MHz
QOS (WMM) | 53600 | 34300 | 23200
TUA-O | 74800 | 76200 | 51900

## Slide 13: MAPC: TUA-O MU-EDCA TO side-effect
4 BSS Video
Avg. 90% CU @ 80MHz
TUA-O w/ MU-EDCA TO = 35ms
MU-EDCA TO needs to be lowered to avoid bi-modal PDF @ TO=35ms
TO=10ms would shift the EDCA escape point into the TUA-O long tail
⁄

## Slide 14: MAPC: TUA-O MU-EDCA TO optimized
4 BSS Video
Avg. 90% CU @ 80MHz
TUA-O w/ MU-EDCA TO = 10ms
Huge improvement over EDCA (76 vs. 38ms 99.9%)
Now can MAPC do better ?
⁄

## Slide 15: MAPC Modeling (C-TUA)
As before, TUA-O aligns traffic to trigger at each BSS i.e. 5 VI STA
SPs (TID, durations) and a target start time (TST) exchanged amongst APs
All APs contend at TST, and leader opens the TXOP via TUA to its own VI STA
Leader AP waits SIFS then then uses C-TDMA sequentially with each follower AP (i.e. allocate target duration, wait duration, expect TXOP return)
Each follower AP then uses TUA to its own VI STA (within the shared TXOP)
As per TUA, MU-EDCA TO allows follower AP to contend separately from leader
Since neither BSS-wide not ESS-wide R-TWT is assumed, notionally this is “Coordinated TUA” or C-TUA

## Slide 16: MAPC C-TUA
4 BSS Video
Avg. 90% CU @ 80MHz
C-TUA w/ MU-EDCA TO = 10ms
Huge Improvement over TUA-O (38 vs. 23ms 99.9%)
Loss is also dramatically improved (50%->~1% [not shown])

## Slide 17: Interim results and next steps
MAPC (C-TUA) evaluation with AC-VI (Video) indicated improvement but not necessarily preservation of a WTSN (1ms) SLA
Gains diminish when fewer APs server per TXOP (not shown for brevity)
For completeness, we evaluate with AC-VO (XR Pose – i.e., 10ms period, 100B/frame, 80Kb/s) and determine if a similar conclusion is warranted.
Applying lessons learned, we optimize the MU-EDCA TO to 5ms (1/2 the period) based on initial (unoptimized) PDF

## Slide 18: MAPC C-TUA: XR Pose
4 BSS XR Pose
TUA-O/C-TUA-O
Avg. 90% CU
XR/IRT requirements met but not WTSN (1ms) without further optimization (e.g. combined use of TUA*)
Chart: Delay vs. Mode
| QOS | TUA | C-TUA
90%-ile | 33 | 12.1 | 2.9
99%-ile | 8.3 | 1.4 | 3.4
99.9%-ile | 1.1 | 4 | 1.7

## Slide 19: Interim results
Choosing AC-VO (for XR Pose) reduces the baseline latency (over AC-VI) both TUA-O and C-TUA-O change the outcome significantly
Analysis reveals that the baseline case (4 APs x 30 STA per AP) is subject to:
  a high collision probability (~90%) generally irrespective of offered load (i.e. 50% and 90% achieved similar results) due to high # of CSMA contenders.
  initial traffic synchronization (i.e., all STA and/or AP collide by WTSN schedule) also creates additional collisions.
C-TUA form of coordination can be a low-cost universal method to achieve lower latency in a latency-sensitive (IRT or WTSN) high-density (HD) multi-AP environment with managed and unmanaged BSS

## Slide 20: Next-steps (C-SP)
To improve upon TUA-O/C-TUA-O for WTSN (hard-start-time) we examine the affect of defined service-periods (SP) without a start-time-protection-rule (STPR) for the BSS itself (i.e. no R-TWT)
In C-SP, each AP is assigned a non-overlapping slot within the shared TXOP (skewed slightly from it’s target start-time) but doesn’t require C-TDMA (TXS)
Unlike C-TUA-O, the AP is expected to take the time-slot and NOT contend outside it. Thus, there is a probability the AP will not be served IF the TXOP cannot be obtained at that time

## Slide 21: MAPC C-SP: XR Pose
4 BSS XR Pose
TUA-O/C-SP
Avg. 90% CU
C-SP has a marked reduction in latency (but suffers a non-zero loss of ~1% [not shown])
Chart: Delay vs. BW
| TUA | C-TUA | C-SP
90%-ile | 12.1 | 2.9 | 1.8
99%-ile | 1.4 | 3.4 | 2
99.9%-ile | 4 | 1.7 | 0.7

## Slide 22: Summary
High-Density (HD) Enterprise WLANs suffer from high client density contributing to high co-channel collision rates from both managed BSS and unmanaged BSS
Simple MAPC scheduling forms (C-TUA, C-SP) may be used to effectively bound latency in multi-AP environments even with unmanaged BSSs
Multi-follower C-TDMA forms offer acceptable latency bounds for interactive-real-time/XR traffic types (1-10ms)

## Slide 23: References
[1] XXXX

## Slide 24: Straw poll
XXXX
Y / N / A