## Slide 1: Practical Multi-AP Coordination (MAPC) Scenarios
April 2025
Authors:
Name | Affiliation | Phone | email
Malcolm Smith | Cisco Systems |  | mmsmith@cisco.com
Binita Gupta | Cisco Systems |  | 
Brian Hart | Cisco Systems |  | 

## Slide 2: Problem Statement
Multi-service network that simultaneously supports:
  Low-latency channel access for multi-media, IIOT/XR, etc (~10ms)
  Ultra-reliable/ultra-low latency channel access for XR/IIOT* in Wireless Time-Sensitive Networking (WTSN) (~1ms)**
  Devices subject to irregular in-device coexistence (IDC) challenges
  Devices with P2P traffic
Managed contention/congestion from OBSS
  With optimizations within the same MANAGED administrative domain (e.g. TUA-O, R-TWT, MLO***)
  With limited control over other UNAMNAGED administrative domains (e.g. QoS)
With:
  High system efficiency
  Implementation simplicity
  Acceptable fairness with legacy generations
*Industrial IOT (IIOT), AR/VR/MR/eXtended Reality (XR)
** Triggered Uplink Access Optimization (TUA-O), Restricted Target Wake Time (R-TWT), Multi-Link-Operation (MLO)

## Slide 3: Key Traffic profiles
Wireless TSN (WTSN) e.g. IIOT, XR
  STA traffic synchronized to WLAN via 802.11 or 802.1 means e.g. 802.1Qbv/AS**
  Rigid SCS QC parameters (SST, SI, etc)*
  Target: 1ms 99.9% (at least)
Interactive real-time e.g. XR, 4K video conferencing
  STA traffic can be synchronized to WLAN via 802.11 means e.g. SCS QC, R-TWT
  Flexible SCS QC parameters (SST, SI, etc)*
  Target: 1-10ms 99.9% (at least)
Collaboration/video-streaming
  STA traffic periodic but unsynchronized to WLAN
  Target 10-50ms 99.9% (at least)
Non-real-time (background) – aperiodic and unsynchronized
*SCS QoS Characteristics (SCS-QC), Service Start Time (SST), Service/Scheduling Interval (SI)
** 802.1AS and 802.1Qbv applied to Wireless TSN (WTSN) see: https://avnu.org/wireless/ for example usage

## Slide 4: QoS methods to manage delay congestion (My and OBSS)
QoS
  Apply VI/VO WMM/EDCA parameters to specific flows
  Available in Managed, SP and Enterprise WLANs
Triggered Uplink Access Optimization (TUA-O)
  Combined with SCS QoS Characteristics (QC) – SI, delay bound, etc.
  Expected availability in managed, SP and Enterprise WLANs
  STA requests via SCS QC and AP aligns traffic with MU trigger with e.g. R-TWT/SCS QC SST*
MLO
  enhanced Multi-Link-Single-Radio (eMLSR) expected to be commonly available in most WLANs
  Delay optimized mode assumed (i.e. first non-Busy link wins)
Restricted TWT (R-TWT)
  Mapped to 802.1Qbv gates (i.e. time-slot reservation) for Wireless TSN (WTSN) applications
  Expected to be supported by a limited device set but not universally honored (e.g. legacy)
Multi AP Coordination (MAPC) e.g. CoRTWT/CoTDMA/etc
  Under consideration by 802.11bn
  Details provided as needed here-in
*Service Start Time (SST) can be explicitly requested via SCS QC to align with an existing TWT/R-TWT session or via the latter during SP establishment

## Slide 5: BSS Coordination model
Managed WLAN
  QOS (WMM) [assumed default]
  Wi-Fi 7 (TUA-O/SCS-QC, R-TWT) with MUEDCATimer control
  Rigid SCS-QC or R-TWT derived MAPC service periods (SP)  e.g. CoRTWT
  Flexible SCS-QC on-demand (i.e., requested/allocated in–TXOP) MAPC coordination  e.g. CoTDMA
Managed to Peer2Peer (P2P) and/or Unmanaged WLAN
  Uncoordinated (e.g. WMM QOS) [assumed default]
  Sharing of priority and SP needs (e.g., rigid SCS-QC or R-TWT based)
  Negotiation of SPs

## Slide 6: Practical QoS analysis objectives
Baseline performance with pre-11bn methods on existing 5GHz/40MHz WLAN
  Most interference expected to be non-QoS or otherwise uncoordinated
Predict incremental gains with emerging 6GHz WLAN
  80MHz BW expected min. in dense environments (Enterprise, MDU*, etc.)
Determine scenarios where MAPC provides key QoS benefits
* Multi Dwelling Unit (MDU)

## Slide 7: Analysis approach/parameters
Simulation-based with empirical validation (e,g. Wi-Fi 7 TUA-O, Wireless TSN/R-TWT, etc)
My BSS and OBSS co-channel interference (CCI) modeled as best-effort (AC-BE) offered-load (Poisson) to achieve a target Channel Utilization (CU) with ‘heavy’ (60KB) payload
Real-time (RT) offered-load from uplink
  Video (VI) [35ms SI, 10KB/frame, 2.2Mb/s] with 35ms (default) MUEDCATimer
  XR pose (VI/VO) [10ms SI, 100B/frame, 80Kb/s] with 10ms (default) MUEDCATimer*
Enterprise density assumed
  25 BE and 5 real-time STA per AP
  Either one AP (non-MAPC) or (for MAPC) 4 identical co-channel APs (i.e. 25x4+5x4=120 STA)
  Average MCS 7 (81Mb/s @ 20MHz w/ 1 SS)
Only uplink channel ACCESS delay estimated (queueing delay ignored for now)
* XR can have either rigid SCS QC parameters for WTSN or flexible SCS QC parameters for interactive-real-time (IRT) applications

## Slide 8: Baseline: Wi-Fi 7 (Typical average peak load)
1 BSS Video
40MHz
Avg. 50% target CU
Only WTSN (1ms) needs a specific QoS method (R-TWT)
*WTSN Qbv
Chart: Latency vs. mode
| No QOS | QOS (WMM) | MLO (+WMM) | TUA (+WMM) | R-TWT (+WMM)
90%-ile | 5.4 | 4 | 3.8 | 3.3 | 1
99%-ile | 5.8 | 4 | 3.5 | 2.4 | 0.1
99.9%-ile | 9.4 | 4.5 | 3.8 | 1 | 0.9

## Slide 9: Baseline: Wi-Fi 7 (High load)
1 BSS Video
40MHz
Avg. 90% CU
TUA-O needed to meet interactive-real-time/XR
R-TWT needed for WTSN
Chart: Latency vs. mode
| No QOS | QOS (WMM) | MLO (+WMM) | TUA (+WMM) | R-TWT (+WMM)*
90%-ile | 45 | 21 | 16 | 8.3 | 1
99%-ile | 150 | 19 | 13 | 8 | 0.1
99.9%-ile | 55 | 13.6 | 10 | 5.5 | 0.9
* WTSN Qbv

## Slide 10: Baseline: Wi-Fi 7 in 6GHz
1 BSS Video
TUA-O
Avg. 90% CU
Increasing BW from 40 to 80MHz results in almost meeting interactive-real-time /XR target (10ms)
WTSN/XR (1ms) target not met
Chart: Delay vs. BW
| 40MHz | 80MHz | 160MHz
90%-ile | 10.3 | 4.3 | 2.6
99%-ile | 13.2 | 5.1 | 3.4
99.9%-ile | 4.4 | 2.2 | 1.8

## Slide 11: Interim summary and MAPC formulation
Migration from 5GHz (40MHz) to 6Ghz (80/160MHz) will likely support low-latency (10ms) for a single BSS even at high CU (90%)
WTSN/Ultra-low-latency (1ms) only met IF R-TWT is adopted ESS-wide
Multi-AP (CCI) will degrade latency further, so we expect TUA-O as a minimum requirement to meet ultra/low latency targets
For our 4 co-channel AP scenario, each AP uses QoS/WMM or TUA-O
Worst-case whereby TUA-O operation is aligned across all APs (i.e. Rigid SCS QC/WTSN flows have COMPETING SST across APs)

## Slide 12: MAPC: TUA-O vs. QOS (WMM)
4 BSS Video
Avg. 90% CU
TUA-O can perform worse than QOS/WMM
Wider BW fails to address QOS needs 
(continued on next slide)
Chart: 99.9% Delay vs. BW
| 40MHz | 80MHz | 160MHz
QOS (WMM) | 54 | 34 | 23
TUA-O | 75 | 76 | 52

## Slide 13: MAPC: TUA-O MUEDCATimer side-effect
4 BSS Video
Avg. 90% CU @ 80MHz
TUA-O w/ MUEDCATimer = 35ms
MUEDCATimer needs to be lowered to smooth bi-modal PDF @ 35ms
MUEDCATimer = 10ms would shift the MU-EDCA escape point into the TUA-O long tail
⁄

## Slide 14: MAPC: TUA-O MUEDCATimer optimized
4 BSS Video
Avg. 90% CU @ 80MHz
TUA-O w/ MUEDCATimer = 10ms
Huge gain (76 vs. 38ms 99.9%)
Wider BW still fails to address QOS needs!
Now can MAPC do better ?
⁄

## Slide 15: MAPC Modeling (CoTUA)
As before, TUA-O aligns traffic to trigger at each BSS i.e. 5 VI/VO RT STA
SPs (TID, durations) and target service start time (TSST) exchanged by APs*
All APs contend at TSST, winner opens the TXOP via TUA to its own RT STA
Sharing AP (TXOP holder) then polls (3) shared APs for criticality of SP (imminence**) then sequentially allocates a time-slot to each follower AP
Each follower AP uses TUA-O to its own RT STA then TXOP Returns
Similar to TUA, MUEDCATimer allows a follower AP to contend separately
Since neither BSS-wide not ESS-wide R-TWT is assumed, notionally this is “Coordinated TUA” or CoTUA (with SPs but without R-TWT per-se)
* A priori knowledge of the SP is used to help select the APs to poll in the CoTDMA process (e.g. similar AC/TID, similar SP TSST)
** Since SP starts times are flexible and/or RT flows within the group may have different expiry times – imminence is used to prioritize APs in the sequence

## Slide 16: MAPC CoTUA
4 BSS Video
Avg. 90% CU @ 80MHz
CoTUA w/ MUEDCATimer = 10ms
Huge Improvement over TUA-O (38 vs. 23ms 99.9%)

## Slide 17: Interim CoTUA results and next steps
CoTUA evaluation with AC-VI (Video) indicated improvement but not necessarily preservation of an Interactive Real Time/IRT (10ms) or WTSN (1ms) SLA
Gains diminish when fewer APs served per TXOP (not shown for brevity)
For completeness, we evaluate with AC-VO (XR Pose – i.e., 10ms period, 100B/frame, 80Kb/s) and determine if a similar conclusion is warranted.
Applying lessons learned, we optimize the MUEDCATimer TO to 5ms (1/2 the period) based on initial (unoptimized) PDF

## Slide 18: MAPC CoTUA: XR Pose
4 BSS XR Pose
AC-VO/TUA-O/CoTUA
Avg. 90% CU
XR/IRT requirements (10ms) met but not WTSN (1ms) without further optimization
Chart: Delay vs. Mode
| QOS/WMM | TUA-O | CoTUA
90%-ile | 33 | 12.1 | 2.9
99%-ile | 8.3 | 1.4 | 3.4
99.9%-ile | 1.1 | 4 | 1.7

## Slide 19: CoTUA Summary
Choosing AC-VO (for XR Pose) reduces the baseline latency (over AC-VI) while both TUA-O and CoTUA change the outcome significantly
Analysis reveals that the baseline case (4 APs x 30 STA per AP) is subject to:
  a high collision probability (~90%) generally irrespective of offered load (i.e. 50% and 90% achieved similar results) due to high # of CSMA contenders.
  initial traffic synchronization (i.e., all STA and/or AP collide by WTSN schedule) also creates additional collisions.
CoTUA form of coordination can be a universal* method to achieve lower latency in a latency-sensitive (IRT or WTSN) high-density (HD) multi-AP environment with managed and unmanaged BSS
* No reliance on legacy STA to honor R-TWT

## Slide 20: CoSP formulation
To improve upon TUA-O/CoTUA for WTSN (Rigid SCS QC w/ SST) we examine the effect of strict service-periods (SP) with a start-time-protection-rule (STPR) between the APs but not within the BSS (i.e. no R-TWT)
In CoSP, each AP is assigned a sequence and target SP duration within the shared TXOP which is contended/opened by only the first AP (TXOP leader)
Unlike CoTUA, the APs are expected to WAIT for their assigned time-slot (i.e. until the AP ahead finishes its SP) and NOT contend outside it. Thus, there is a probability the SP start-time will be delayed IF the TXOP cannot be obtained at the target time

## Slide 21: MAPC CoSP: XR Pose
4 BSS XR Pose
AC-VO/TUA-O/CoSP
Avg. 90% CU
CoSP has a marked reduction in latency
Waiting may beat contending!
Chart: Delay vs. BW
| TUA-O | CoTUA | CoSP
90%-ile | 12.1 | 2.9 | 1.8
99%-ile | 1.4 | 3.4 | 2
99.9%-ile | 4 | 1.7 | 0.7

## Slide 22: Summary
High-Density (HD) Enterprise WLANs suffer from high client density contributing to high co-channel collision rates from both managed BSS and unmanaged BSS
Simple MAPC scheduling forms (CoTUA, CoSP) may be used to bound latency in multi-AP environments with unmanaged BSSs and/or with BSSs w/o R-TWT
CoTDMA (w/ multiple shared APs per TXOP) might offer acceptable latency bounds for interactive-real-time/XR traffic types (1-10ms)
ESS-wide R-TWT support may still be needed to reach WTSN (1ms) targets