## Slide 1: Thoughts on IMMW For the Industry Use
Date: 2024-07-01
Authors:
Name | Affiliations | Address | Phone | Email
Yue Xu | Huawei | Huawei Nanjing R&D Institute, Nanjing, Jiangsu, China, 210012 |  | xuyue57@Huawei.com
Chenhe Ji |  |  |  | 
Mengshi Hu |  |  |  | 
Chun Pan |  |  |  | 
Xiaofei Bai |  |  |  | 
Xiaofei Bai |  |  |  | 

## Slide 2: Introduction
Based on the IMMW SG PAR document[1] and actual requirements in industrial scenarios, we propose the following concerns and corresponding suggestions.

## Slide 3: Recap: IMMW SG PAR[1]
Type | Brief info
AGV / AMR | Including guidance control, process data exchange, video/image, and emergency stop, between robots and a control system,
Robot/drone motion control | Remote operation with haptics communication, programmed robot operation with emergency stop.
IoT Sensors/ WIFI sensing | High-density deployment and Periodical/event-based report of information to the control system.
Use Case | Range | Throughput | Delay (ms) | Reliability
4k UHD Transmission | < 5 m | < 10 Gbps | 10~20 | jitter<5ms
VR | < 10 m | 10~20 Gbps | 5~10 | jitter <5 ms, PER<10E-2
PAR
Real [2]
AGV: Automated Ground Vehicle
AMR: Autonomous Mobile Robot
We believe that the content mentioned in the PAR document aligns with the development of application requirements for millimeter waves in industrial scenarios. However, these discussions are at a high level. Therefore, we aim to further share some of our detailed insights and perspectives on mmWave applications in industrial settings.

## Slide 4: Sharing - 1：The fast deployment
From the PAR, the core idea is the ‘fast deployment’. And we think:
Reuse/Minimum-adjust current baseband architecture
Reuse/Combine current-technique (e.g., Sounding, MLO, Power saving, TWT…)
Design Appropriate Bandwidth/KPIs
Bandwidth Concern#1
Throughout/Latency/Reliability Concern#1
The design should be
reasonable to facilitate quick deployment.
different from the existing standards to show the advanced nature.

## Slide 5: Sharing - 2：The Spatial Stream
Multiple streams can:
- ensure the throughput to help meet traditional and emerging requirements even in the densest environments
- enhance the stability (link optimization).
However, the increase in the number of flows inevitably increases the cost of hardware devices (hindering fast deployment). Meanwhile, the gain accelerate is ‘slowing down’.
The performance of a single flow may not meet the requirements.
Spatial Stream Concern#1
Throughout/Latency/Reliability Concern#2
In the MIMO, data is divided into multiple independent spatial flows. More spatial flows indicate more paths for independently processing data and a higher rate.
AP
STAs
#SS | throughput
1 | 350 Mbps
2 | 650 Mbps
4 | 1.2 Gbps
Setting: 11ax, 160MHz, 45G Band, 16QAM
The gain efficiency is decreasing.

## Slide 6: Sharing - 3：The Sensing/Ranging
Bandwidth | 80MHz | 160MHz | 320MHz | 640MHz | 1280MHz
Distance Resolution (m) | 1.875 | 0.9375 | 0.4688 | 0.2344 | 0.1172
Object Existence Detection
Object Counting
Motion recognition
Sensing and Ranging has been widely discussed (more than 20 uses case in [3]). And, commercial products have already application them without any standardization
802.11bf and 802.11az/bk are main IEEE standard for Sensing and Ranging. So, IMMW can be considered to provide support for these technical standards..
Larger bandwidth
[4]
Higher resolution
More information
More cost
Lower bandwidth
Less resolution
Less information
Lower cost
Bandwidth Concern#2
balance

## Slide 7: Summary
From the above 3 sharing opinions and corresponding concerns. We would like to provide our suggestions that:
Main Concern | Suggestion
Bandwidth | We recommend a minimum bandwidth of 160 MHz and a maximum bandwidth that is appropriate for fast deployment and standard differentiation. This approach will meet actual throughput requirements (e.g., 10 Gbps@client side) and expand the ecosystem.
Spatial Stream | We recommend limiting the number of spatial streams to avoid excessive complexity. Specifically, using no more than 2SS under SU-MIMO is preferable.

## Slide 8: SP1
Do you agree that Move to add the sentence “It is capable of supporting no more than 2 Spatial Streams.” to the end of the 2nd paragraph of clause 5.2.b of the PAR.?
  -Yes
  -No
  -Abstain

## Slide 9: References
[1] 11-24-0116-03-immw-immw-draft-proposed-par
[2] 11-23-1570-00-0uhr-latency-consideration-of-industrial-scenarios
[3] 11-24-0723-01-immw-sensing-and-ranging-in-immw
[4] 11-20-1712-02-00bf-wifi-sensing-use-cases