## Slide 1: DRU for Puncturing Case 1001
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
  According to Motion 20 shown in [1], in a non-punctured 80 MHz PPDU, the following distribution bandwidth (DBW) modes are allowed for DRU:
  80 (for the no puncturing case 1111)
  20 + 20 + 40 or 40 + 20 + 20 （for the no puncturing case 1111)
  Besides the above non-punctured case, the following 80 MHz DBW patterns are also discussed in the case of one 20 MHz or 40 MHz punctured [2]:
  x + 20 +40 (for the puncturing case 0111)
  20 + x + 40 (for the puncturing case 1011)
  40 + x + 20 (for the puncturing case 1101)
  40 + 20 + x (for the puncturing case 1110)
  40 (for the puncturing case 0011 or 1100)
  20 + 20 (for the puncturing case 0011 or 1100)
DBW 80 | DBW 80 |  |  | 
DBW 20 + 20 + 40 | DBW 20 | DBW 20 | DBW 40 | 
DBW 40 + 20 + 20 | DBW 40 |  | DBW 20 | DBW 20

## Slide 3: DBW for Puncturing Case 1001
According to the previous slide, the DBW patterns in the puncturing cases 1111, 0111, 1011, 1101, 1110, 0011, and 1100 have been discussed.
  However, the DBW patterns in the puncturing case 1001 is missing.
To enable DRUs in the puncturing case 1001, DBW patterns should also be discussed and supported. Similar to the 1100 and 0011 cases, it is natural to enble the following DBW pattern:
  20 + 20 (for the puncturing case 1001)
  In this contribution, we further suggest supporting the following aggregated 40 MHz DBW for the puncturing case 1001.
  Part 1 of 40 + Part 2 of 40 (for the puncturing case 1001)
DBW 20 + 20 | DBW 20 |  |  | DBW 20
DBW Aggregated 40 | Part 1 of DBW 40 |  |  | Part 2 of DBW 40

## Slide 4: Details of Aggregated 40 MHz DBW
Different from the conventional 40 MHz DBW, the aggregated 40 MHz DBW is divided into two parts, where each part corresponds to 20 MHz.
  However, this does not mean that the tone plan of the aggregated 40 MHz DBW is complex. Actually, a simple shift procedure could be utilized to generate the aggregated 40 MHz DBW.
  An example is shown below:
242 tones
242 tones
Tone plan of the conventional 40 MHz DBW
Tone plan of the aggregated 40 MHz DBW
242 tones
242 tones
Shift
Shift

## Slide 5: Benefits of Aggregated 40 MHz DBW
According to the analysis in [3], the difference of power gain between DBW 20 and DBW 40 is shown below:
  Note that although the tone indices of conventional and aggregated 40 MHz DBW are different, the power gains are the same.
  From the above table, it is worth defining the aggregated 40 MHz DBW for the puncturing case 1001 to further enhance the DRU performance.
NRU | DRU | 
 | DBW = 20 MHz | DBW = 40 MHz (Conventional/Aggregated)
26 | 8.06 | 11.07
52 | 6.3 | 8.06
106 | 3.29 | 6.3
242 | N/A | 2.62
Table Power Gain Compared to the RRU Case (dB)

## Slide 6: Summary
In this contribution, the following DBW patterns are discussed for the puncturing case 1001:
  Suggest defining the aggregated 40 MHz DBW for the puncturing case 1001 to further enhance the DRU performance.
DBW 20 + 20 | DBW 20 |  |  | DBW 20
DBW Aggregated 40 | Part 1 of DBW 40 |  |  | Part 2 of DBW 40

## Slide 7
[1] Alfred Asterjadhi, TGbn Motions List - Part 1, 802.11 DCN 2024/171r8
[2] Eunsung Park, et al. Distribution Bandwidth within 80 MHz for DRU, 802.11 DCN 2024/766r2
[3] Mengshi Hu, et al. Discussion on Distribution Bandwidth of DRU, 802.11 DCN 2024/801r1
References

## Slide 8
Do you agree to include the following into the 11bn SFD?
  DRU are allowed in the punctured case 1001 in an 80 MHz.
    1001 indicates that the two 20 MHz channels in the middle of an 80 MHz are punctured.
    Y
    N
    A
Straw Poll #1

## Slide 9
Do you agree to include the following into the 11bn SFD?
  In the puncturing case of 1001 in an 80 MHz, the following distribution bandwidth modes are allowed for DRU
    20 MHz + 20 MHz
    Aggregated 40 MHz
    Note 1: 1001 indicates that the two 20 MHz channels in the middle of an 80 MHz are punctured.
    Note 2: The aggregated 40 MHz is a distribution bandwidth consisting of the two non-punctured 20 MHz channels in the puncturing case 1001.
    Y
    N
    A
Straw Poll #2