## Slide 1: Multi-AP Coordination for Low Latency Traffic Transmission
Date: 2024-08-13
Authors:
Name | Affiliations | Address | Phone | email
Shirley Yin | Clourney Semiconductor |  |  | shy166@clourneysemi.com
Jerome Gu | Clourney Semiconductor |  |  | 
Jason Sheng | Clourney Semiconductor |  |  | 

## Slide 2: Introduction
“Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” is one of the objectives of 802.11bn[1].
A Motion on Multi-AP operation was approved [2]
  Move to add the following text to the TGbn SFD:
    Define a multi-AP Coordinated Spatial Reuse at TxOP-level with power control
    Define multi-AP Coordinated Beamforming
    Other multi-AP coordination modes are TBD
Currently, most of the contributions for low-latency traffic focus within a single BSS[3-7]. Multi-AP preemption for LL traffic has been proposed in [8].
The introduction of multi-AP coordination to LL can reduce inference and prioritize LL transmission, thus guarantee the timely and reliable transmission of low-latency traffic. In this contribution, we would like to discuss the support of low latency traffic transmission in Multi-AP coordination.

## Slide 3: How The Multi-AP Coordination Works with LL traffic?
LL latency traffic? Preemption?
  Supporting LL traffic does not necessarily mean supporting preemption only.
Support LL traffic in multi-AP coordination with low complexity
  The LL traffic can enjoy the gain from Multi-AP coordination.
Regarding four kinds of Multi-AP coordination
  C-SR: Allow spatial reuse decisions which are low latency traffic oriented. → reducing latency & enhancing reliability.
  C-Beamforming: Whether should the non-STA be nulled, or be covered by beamforming? → prioritizing LL traffic tranmissions.
  C-OFDMA: Sharing AP prioritizes TXOP allocation to shared AP with low latency traffic. → reducing latency.
  Joint transmission: Much protocol impact and quite complicate. It can be for further study.
Preemption
Complexity
?

## Slide 4: Support LL Traffic in C-SR
AP1
AP2 (LL)
STA1
STA2
AP1
AP2
(LL)
STA1
STA2
  There are many ways for C-SR desgin. For example, ICF/ICR frame could be adopted for C-SR.
  As one simple option, introduce one bit for LL traffic notification in ICF/ICR.
  Decide the C-SR policy according to LL traffic indication
  When there is no LL traffic indicated in each related AP, the common co-ordination is applied, e.g., one AP decreases its transmission power to an acceptable level.
  When there is LL traffic indicated in one of the related APs, the AP with LL traffic gets sufficient power(also a proper MCS) in order to transmit LL traffic in time and reliably.
  When both related APs are with LL traffic, decide the C-SR policy according to the priority of LL traffic.
AP2 performs power adjustment
AP1 performs power adjustment

## Slide 5: Support LL Traffic in C-BF
  C-BF: An AP performs beamnulling to protect a neighbor AP’ transmission, while completing its beamformed transmission.
  Nulling protects neighbor AP’s STA, also brings shrunk coverage.
  Decide which AP performs C-BF.
  When there are multiple STAs,
    Decide which STA(s) to be covered by beamforming.
    Decide which STA(s) to be nulled (for protection or interference reduction).

## Slide 6: Support LL Traffic in C-OFDMA
  MU-RTS/CTS frame exchange for LL traffic notification
    The MU-RTS/CTS frame exchange can be applied to multi-AP coordination [9]. Similarly, one bit can be introduced for LL traffic notification.
    Sharing AP transmitting an MU-RTS frame to poll LL notification from Shared AP.
    CTS frames could be simultaneously transmitted by Shared APs, to indicate whether there is LL traffic in queue and LL traffic related information could be transmitted either.
AP1
(Sharing AP)
AP2
(Shared AP)
AP3
(Shared AP)
MU-RTS
AP1’s TXOP
LL arrives
Trigger
AP3 uses TXOP for LL Transmission at first.
BA
......
......
CTS
CTS
AP2 uses the TXOP later
LL
poll
LL
Notification

## Slide 7: Discussions
  After LL notification:
    Detailed design
      TXOP sharing for the AP with LL traffic should be prioritized.
      The C-SR policy need to be decided. For example, biased to the AP with LL traffic.
      The C-BF policy should be decided, whether to cover a non-AP STA or null a non-AP STA.
    How to obtain more benefits from Multi-AP coordination?
      Interference reduction.
      Prioritize LL traffic transmission.
  Complexity
    Support LL in Multi-AP Coordination has a manageable complexity. Make sure to complete it in 11bn.
  More features enabling efficient LL traffic transmission
    Pre-emption in Multi-AP coordination.
    The joint transmission scenario.
Notes: Complexity?
1.不复杂，加一点东西，很容易就收敛了；
2.

## Slide 8: Summary
Multi-AP coordination benefits the timely delivery of low latency traffic.
Low latency traffic indication is with low complexity. It is necessary to indicate the presence of low latency traffic in multi-AP coordination.

## Slide 9: References
[1] 23/0480r3, UHR Proposed PAR
[2] 24/0171r12,TGbn Motions List
[3] 24/0390r0, A Uniform Procedure for Preemption
[4] 24/0389r0, Preemption for Low Latency
[5] 24/0168r0, TXOP preemption in 11bn
[6] 24/0625r0, Thoughts on Low Latency traffic transmission
[7] 24/0811r0, Overlapped indication for aperiodic low latency traffic
[8] 24/0636r0, Multi-AP Preemption for Low-Latency Traffic
[9] 24/0941r0 TXOP Sharing Group - Shared AP Selection