## Slide 1: NB hop density

## Slide 2: Introduction
These slides provide some examples on the relation between hop density and Wi-Fi channel access latency
Increased hop density causes more partially overlapping NB transmissions, which makes it harder for Wi-Fi to find 20/40/80/160/etc. MHz spectrum that is idle all at the same time
Possible methods are illustrated to (dynamically) control the NB duty cycle (DC)
  maximum DC per 20 MHz
  dynamic DC per 20 MHz
  these could be complemented with a dynamic EDT increase on repeated CCA busy at NB, so that neither Wi-Fi nor NB will be able to capture the medium entirely when both are confined in the same limited spectrum
  when sufficient spectrum is available, neither dynamic duty cycle adaptation nor dynamic EDT adaptation are expected to trigger much
This analysis mainly relates to ACL traffic, where the duty cycle can be very high

## Slide 3: Maximum DC per 20 MHz
NB uses a maximum DC per 20 MHz segment
  max 3.7% DC per 20 MHz, which adds up to 88% over 480 MHz
  the maximum DC could depend on the NB PSD, which would allow for a higher segment DC for lower PSD (or Tx power)

## Slide 4: Dynamic DC adaptation
With dynamic DC adaptation, the Bluetooth central reduces the Tx time in a given 20 MHz segment from 6377 us to 360 us (per 7.5 ms) after a CCA busy occurs in the segment, until 10 CCA idles have occurred in the segment
  effectively, the duty cycle in that segment is temporarily reduced from 3.6% to 0.3%
  transmissions in the segment can continue after the CCA busy, but with a shorter Tx time
  transmissions in other segments are not affected (except when a CCA busy occurs there too)
This causes that the overall Bluetooth duty cycle is reduced based on NB-NB collisions
  the NB-NB collision rate is typically low, so this mechanism only becomes active when there are many high duty cycle NB links in a relatively small portion of the spectrum
  the impact is distributed relatively fairly over all nodes
  this also causes that the NB duty cycle is reduced in the part of the spectrum where Wi-Fi is active, which improves frequency separation
There is no impact on ISO audio, because the Tx time is already 360 us
Other methods to achieve the same may be possible, e.g.
  the DC reduction could set in after a delay
  the DC reduction could depend on the PSD (i.e. longer TXOPs at lower PSD)
  etc.

## Slide 5: Topology

## Slide 6: Topology
nb_r8200c

## Slide 7: Sims

## Slide 8: Baseline
nb_r8200c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
The hop density in the upper part increases after Wi-Fi starts, due to the SCD
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz

## Slide 9: Max DC/20 MHz
nb_r8201c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz
The hop density in the upper part stays relatively the same

## Slide 10: Dynamic DC/20 MHz
nb_r8204c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
The hop density in the upper part stays relatively the same
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz

## Slide 11: Zoomed plots

## Slide 12: Baseline
nb_r8200c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
The hop density in the upper part increases after Wi-Fi starts, due to the SCD
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz

## Slide 13: Max DC/20 MHz
nb_r8201c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz
The hop density in the upper part stays relatively the same

## Slide 14: Dynamic DC/20 MHz
nb_r8204c
BT hops in 480 MHz
88% duty cycle per link
(ACL with 6377 us data packet length in a 7500 us period)
The hop density in the upper part stays relatively the same
Wi-Fi starts here
Wi-Fi uses static BW in 160 MHz

## Slide 15: CCA busy time distributions

## Slide 16: Baseline
nb_r8310a
The 160 MHz CCA busy probability is high both on the Wi-Fi channel and the segments where Wi-Fi is not currently active. The latency is caused by partially overlapping NB transmissions
160 MHz segments where Wi-Fi is not active
Wi-Fi channel

## Slide 17: Max DC/20 MHz
nb_r8311a
The 160 MHz CCA busy probability is improved but still high. The Wi-Fi channel is slightly worse somehow
160 MHz segments where Wi-Fi is not active
Wi-Fi channel

## Slide 18: Dynamic DC/20 MHz (10 CCA idles required)
nb_r8312a
The 160 MHz CCA busy probability is low on the Wi-Fi channel and reduced on the segments where Wi-Fi is not currently active
160 MHz segments where Wi-Fi is not active
Wi-Fi channel

## Slide 19: Dynamic DC/20 MHz (50 CCA idles required)
nb_r8313a
The 160 MHz CCA busy probability is low on the Wi-Fi channel and further reduced on the segments where Wi-Fi is not currently active
160 MHz segments where Wi-Fi is not active
Wi-Fi channel

## Slide 20: BRAN(24)124020 results for 160 MHz (Sebastian Max)
BRAN(24)124020