## Slide 1: Further discussions on NPCA
Date: 2024-07-12
Authors:

## Slide 2: Abstract
TGbn has agreed to define Non-Primary Channel Access [1]
Some details on the NPCA are under discussion:
  Switch timing (frame/PPDU formats)
  Channel access mechanism (EDCA parameters)
  Medium Synchronization
  Different view on P20 IDLE/BUSY between AP and STAs
  OBSS TXOP threshold to initiate NPCA operation, etc.
In this contribution, we discuss further details on NPCA:
  Different view problems on OBSS TXOP length
  NPCA primary channel selection
  NPCA Mode 1 / Mode 2

## Slide 3: Different view problems on OBSS TXOP length
Some contributions discussed different view problems on the primary channel state (idle/busy)
There is another different view problem regarding busy duration of the primary channel
  Each STA may have different view on the length of the OBSS TXOP occupying the primary channel
The problem occurs when the NPCA operation of each STA is initiated by different OBSSs
AP
STA1
STA2
STA3
OBSS1
OBSS2
OBSS3
P80
NAV set by OBSS1
(AP & STA1)
P80
NAV set by OBSS2
(STA2)
P80
NAV set by OBSS3
(STA3)
AP and STA1 transition to nP-channel operation due to OBSS1
STA2 transitions to nP-channel operation due to OBSS2
STA3 transitions to nP-channel operation due to OBSS3
(The STAs operating on the nP-channel have different views on the length of the nP-channel operation.)

## Slide 4: Different view problems on OBSS TXOP length (cont’d)
The different view between AP/STAs might lead to interoperability issues
  In nP-channel, TXOP responder may not respond to the received ICF due to its Duration/ID field value being larger than what it can respond
Basic approach to this problem is to let all the nP-channel STAs follow the AP’s view
  Option 1
    Limiting the TXOP holder role of the NPCA to AP only
  Option 2
    AP (if TXOP responder) indicates its NPCA operation duration (derived from AP’s recorded OBSS TXOP length) by using ICR, and the non-AP STA that transmitted ICF ends its TXOP based on the ICR’s duration
  In both options, nP-channel STA switches back to P-channel when the AP switches back to P-channel regardless of STA’s recorded OBSS TXOP length

## Slide 5: NPCA Primary Channel Selection
We may not need to define specific rules for AP to select the NPCA primary channel
  Baseline does not specify rules for AP to select the primary channel either
  Thus an AP may utilize measurements and internal algorithms to select the optimal NPCA primary channel
    e.g., It may measure channel load of each secondary subchannels to find the most idle subchannel
However, NPCA performance can vary greatly depending on the NPCA primary channel location, thus providing guidelines for selecting the NPCA primary channel would be beneficial
  The first guideline is to select a subchannel that has a low probability of being occupied by OBSS TXOPs occupying the primary channel
    The subchannels in S160 have lowest probability of being occupied since they can only be occupied by 320 MHz OBSS TXOP
      Preferred option for 320 MHz NPCA BSS
    The subchannels in S80 have lower probability of being occupied since they can be occupied by 320/160 MHz OBSS TXOP
      Preferred option for 160 MHz NPCA BSS
    The two subchannels in S40 will be occupied by 320/160/80 MHz OBSS TXOP

## Slide 6: NPCA Primary Channel and NPCA Operations
There are cases where the AP selects a NPCA primary channel which is outside of the operating bandwidth of some NPCA non-AP STAs
In this case, there will be two groups of NPCA STAs:
  Group 1: A group of NPCA non-AP STAs for which the NPCA primary channel is within their operating bandwidth
  Group 2: A group of NPCA non-AP STAs for which the NPCA primary channel is outside of their operating bandwidth
P20
NPCA P20
80 MHz STA
(Group 2)
160 MHz STA
(Group 1)
S80
P80

## Slide 7: NPCA Primary Channel and NPCA Operations (cont’d)
NPCA operational requirements
  Group 1 STA does not switch its operating channel for NPCA operations, but changes contending channel (primary channel  NPCA primary channel)
    Similar capabilities as TB PPDU responding procedure (switching to indicated RU)
  Group 2 STA needs to switch its operating channel to cover the NPCA primary channel
    Similar capabilities as the Dynamic Subchannel Operation
Therefore, there may be a non-AP STA that supports NPCA only when it belongs to Group 1 due to the operational complexity
P20
NPCA P20
Operating channel
P20
NPCA P20
OBSS TXOP
Group 2 STA (80 MHz) operation
Operating channel
Operating channel
Operating channel
Group 1 STA (160 MHz) operation
OBSS TXOP
S80
P80
S80
P80
Contending channel
Contending channel
Contending channel

## Slide 8: NPCA Mode 1 and Mode 2
Therefore, NPCA non-AP STAs may need to inform the AP of their NPCA-related capabilities and limitations so that the AP can take these limitations into account for each non-AP STA
An NPCA non-AP STA can inform its capabilities as
  Mode 1: Supports NPCA when the NPCA primary channel is within its operating bandwidth
  Mode 2: Supports NPCA regardless of the NPCA primary channel location
    A mode 2 supporting STA may inform the AP of its channel switching delay for when the NPCA primary channel is outside of its operating bandwidth
We may need to further discuss ways to ensure that Mode 1 STAs still receive benefits from NPCA operation when the NPCA primary channel is outside of their operating bandwidth

## Slide 9: Summary
Different view problems on OBSS TXOP length have been discussed
  Option 1: Limiting the TXOP holder role of the NPCA to AP only
  Option 2: AP (if TXOP responder) indicates its available NPCA duration to the TXOP holder
Guidelines on the NPCA primary channel selection by AP has been discussed
  Selecting one of the subchannels which is in the second half of the BSS operating bandwidth would be beneficial to avoid various bandwidth OBSS PPDUs in the primary channel
NPCA Mode 1 and Mode 2 for a non-AP STA have been discussed:
  Mode 1: Supports NPCA when the NPCA primary channel is within its operating bandwidth
  Mode 2: Supports NPCA regardless of the NPCA primary channel location

## Slide 10: Straw Poll 1
Which option do you prefer for resolving different view on the primary channel status for NPCA operation?
  Option 1: Limiting the TXOP holder role of the NPCA to AP only
  Option 2: AP (if TXOP responder) indicates its available NPCA duration to the TXOP holder
  Abstain

## Slide 11: Straw Poll 2
Do you agree that NPCA defines the following operation modes for non-AP STAs?
  Mode 1: A non-AP STA supports NPCA operation when the NPCA primary channel is within its operating bandwidth
  Mode 2: A non-AP STA supports NPCA operation regardless of the NPCA primary channel locations

## Slide 12: References
[1] 11-24/0209r3 Specification Framework for TGbn Ross Jian Yu
[2] 11-24/0495r0 Non-Primary Channel Access (NPCA) – Follow Up Minyoung Park
[3] 11-24/0868r0 Additional Considerations on Non-Primary Channel Access Leonardo Lanante
[4] 11-24/0426r0 EDCA for Non-Primary Channel Access Dongju Cha
[5] 11-23/0631r0 Secondary channel usage and secondary 20MHz channel backoff Liwen Chu
[6] 11-24/0070r2 Some details about non-primary channel access Yunbo Li
[7] 11-24/0486r1 Some considerations on non-primary channel access Ming Gan
[8] 11-24/0458r1 Considerations on Non-Primary Channel Access Salvatore Talarico
[9] 11-23/2023r1 Further discussion on Non-Primary Channel Access Sindhu Verma
[10] 11-23/1891r0 Nonprimary channel access – follow up Gaurang Naik