## Slide 1: TWT-Based Power Save with Enhanced Flexibility
Date: 2024-07-15
Authors:

## Slide 2: Background
Different power save (PS) mechanisms including scheduled PS, unscheduled PS, dynamic PS and link disablement have been discussed in previous contributions [1-9].
This contribution focuses on TWT based PS, which is one option for scheduled PS from both AP and non-AP STA side [1-4].
  Suitable to handle periodic traffic
MLO could be used to complement and enhance scheduled AP PS [2,3,10,11].
  At least one affiliated AP(s) goes to PS mode, while the other affiliated AP(s) maintains active mode on other (active) link(s).

## Slide 3: Problem
  Potential issue arises when there is no service outside the TWT SPs for a duration in the order of tens of milliseconds [1]. Thus, certain additional level of flexibility on top of the TWT on-off schedule is needed.
  Device with scheduled power save mechanism may hardly capture the dynamic needs from its peer STA(s) outside the TWT SPs.
  The scheduled AP power save impacts all STAs on a link [1,2]. Thus, a more efficient mechanism to jointly negotiate across devices based on TWT on-off schedule is needed on AP side.
  It could be costly for AP to negotiate with each TWT member STA when flexible schedule applies.

## Slide 4: Recap
According with the current spec, both AP and STAs could go to a doze state outside the negotiated TWT SPs.
  AP may go to doze state outside the TWT SPs by setting the Responder PM Mode bit of TWT element to 1.
  AP and TWT member STAs are awake within the negotiated TWT SPs.
Current spec provides flexibility for TWT schedule with following methods:
  Individual TWT supports both explicit and implicit TWT schedules, while broadcast TWT only support implicit TWT schedule.
  TWT Information field could be applied to both individual TWT and broadcast TWT to suspend and resume TWT agreements and related schedules.

## Slide 5: Explicit TWT for B-TWT
The explicit TWT could indicate explicitly the position of the Next TWT, but it could only be applied for individual TWT.
The current TWT Information frame cannot provide as much flexibility as explicit TWT.
  It cannot schedule TWT SP between two subsequent TWT SPs when All TWT is set to 1 or if any side of the TWT peer doesn’t support Flexible TWT schedule.
Enabling explicit TWT for broadcast TWT could provide more flexibility for broadcast TWT members.
B-TWT SP
B-TWT SP
B-TWT SP
I/B-TWT SP
I/B-TWT SP
I/B-TWT SP
I-TWT SP
I-TWT SP
I-TWT SP
AP
STA
Next TWT
Next TWT
Next TWT
Case 1: Flexible schedule in explicit TWT (I-TWT only)
AP
STA
Case 2: Suspension and Resumption in implicit TWT (I-TWT and B-TWT)
Next TWT
All TWT = 1
Skipped
Resumed
1st TWT after Next TWT
AP
STAs
Next TWT
Next TWT
Next TWT
Proposed Case 3: Flexible schedule in explicit TWT (enabled for B-TWT)

## Slide 6: Trade-off Between Flexibility and Power Saving
The AP may use QoS parameters as guidance for TWT setup, but random traffic (e.g., emergency traffic) may still arrive outside the TWT SPs.
Power saving is not properly optimized in current TWT design.
  Single link devices applying either explicit TWT or using TWT information frame cannot go to doze state until they have exchanged the non-zero Next TWT info.
These issues could be mitigated through the support of MLO
  The affiliated AP/STA could go to PS mode while cross-link signals could be exchanged by another affiliated AP/STA on an active link to capture the dynamic needs of the peer device(s).

## Slide 7: Cross-Link Power Saving Management
The active link should be able to support following functionalities:
  Discovery, active probing and association for all STAs (including pre-EHT STA).
  Signaling other affiliated AP/STAs that maybe in doze mode on other links to meet the requirement including increase throughput, provide certain service period and improve flexibility, etc.
Cross-link signal could be sent through the active link(s) to perform operations on at least one specific link(s) to:
  Wakeup the dozed AP and/or STAs.
  Put AP and/or STA(s) to doze mode.
  Suspend and resume TWT agreements/schedules for certain or all TWT member STAs.

## Slide 8: Efficiency Improvement for Scheduled AP Power Save
AP with very light traffic to serve (e.g., during night/holiday) may want to skip multiple I/B TWT SPs for all non-AP STAs
  The current TWT Information field can only suspend and resume one or more TWT agreements/schedules between AP and the same TWT member non-AP STA(s).
  It requests AP to suspend I/B TWT SPs with all TWT member non-AP STAs one by one (for I-TWT) or group by group (for B-TWT)
I-TWT 1
AP-STA1
I-TWT 1
AP-STA2
I-TWT 1
AP-STA1
AP
STA1, 2, 3
AP:
Awake
Doze
STA1:
skipped
Next TWT
STA2:
I-TWT 2
AP-STA1
skipped
I-TWT 1
AP-STA3
STA3:

## Slide 9: Cont.
It could be more efficient for AP to suspend and resume all I/B TWT agreements/schedules with all TWT member STAs at once.
  New signaling could be carried in TWT Information field for this purpose.
  The TWT Information field could be carried
    Option 1: by a cross-link signal on an active link on which all affiliated STAs can receive.
    Option 2: by Beacon frame to be delivered to all STAs.
I-TWT 1
AP-STA1
I-TWT 1
AP-STA2
I-TWT 1
AP-STA1
AP
STA1, 2, 3
AP:
Awake
Doze
STA1:
skipped
Next TWT
STA2:
I-TWT 2
AP-STA1
skipped
I-TWT 1
AP-STA3
STA3:
skipped
skipped

## Slide 10: Summary
We discussed the limitations of current design in TWT and proposed to enable explicit TWT for broadcast TWT.
We discussed the trade-off between flexibility and power saving and proposed the MLO based cross-link signaling in order to improve both.
We also discussed the current drawback for a scheduled AP power save and proposed to enable AP to suspend and resume all I/B TWT agreements/schedules for all TWT member STAs at once.

## Slide 11: SP 1
Do you agree that a more flexible design for TWT-based power save is needed by enabling explicit TWT for broadcast TWT?

## Slide 12: References
[1] 11-23-0010-00-0uhr-considerations-for-enabling-ap-power-save
[2] 11-23-0015-00-0uhr-ap-mld-power-management
[3] 11-23-2040-01-00bn-enabling-ap-power-save-follow-up
[4] 11-23-0225-00-0uhr-considering-unscheduled-ap-power-save
[5] 11-23-1965-02-00bn-dynamic-power-save-follow-up
[6] 11-24-0352-00-00bn-enabling-unscheduling-ap-ps-follow-up
[7] 11-24-0450-00-00bn-a-proposal-for-uhr-soft-ap-power-save
[8] 11-24-0485-00-00bn-low-power-listening-mode-for-clients
[9]11-23-1922-01-00bn-multi-link-sm-power-save-mode
[10] 11-24-0602-00-00bn-multi-link-power-management-for-mlo
[11] 11-24-0737-00-00bn-cross-link-wake-up-to-go-deeper-in-power-save