## Slide 1: Internetworking reference model of AMP only IOT devices
Date: 2024-07-11
Authors:

## Slide 2: Abstract
In this contribution, an internetworking reference model of an AMP only IOT devices is proposed and analyzed.

## Slide 3: AMP IoT device types
Different types of AMP devices have been identified and analyzed in previously presented and published contributions [1] and [2]. There are AMP-only IoT devices vs AMP-assisted IoT devices.
The AMP-only IoT device are characterized as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less (i.e., not using conventional battery).
An AMP-assisted IoT device may be similar to a legacy 802.11 (e.g., 802.11n/11ah) device, it can reuse the current PHY design but with enhanced MAC features to adapt to operation with a specific kind of ambient power. Since the ambient power is very limited and sometimes unstable and uncontrollable, the enhanced power saving and power management can be adapted for the unstable and uncontrollable ambient power.
Two types of the AMP-only IoT devices are identified: Type 1- RF powered AMP device; Type 2- non-RF powered AMP device, e.g., thermal, solar, etc.

## Slide 4: Preliminary conclusion
The requirements presented in [2] applies to all identified use cases of the AMP-only IoT devices. The use cases are characterized by very specific limitations of Maximum payload size (very short), and Peak device power consumption (very low)
In this contribution, we explore an internetworking reference model that meets these requirements

## Slide 5: Two approaches
Exchange of information between tag and interrogator via MAC SAP
  Delivering information through the data link layer to the MAC SAP
  Management by SME
Exchange of information between tag and interrogator via SME
  Delivery of information to SME
  Management by SME

## Slide 6: AMP-only IoT Reference model (Option 1)
802.11full stack compliant STA

## Slide 7: AMP-only IoT Tag Reference model (Option 2)
Block level 802.11 compliant STA

## Slide 8: Data delivery (Option 1)
Interrogator
Tag

## Slide 9: Data delivery (Option 2)
Tag
Interrogator

## Slide 10: Example of Tag inventory and command for Option 2 (based on [3])
None of the exchanges in the diagram use data type frames. Therefore, MAC SAP is not used.

## Slide 11: Optimization of Tag inventory and data delivery

## Slide 12: Tag requirements for Option 1 that are not required for Option 2
The recipient (AP STA) of the MPDU sent by the Tag shall be able to extract a spec-compliant MA-UNITDATA parameters from this MPDU.
The transmitter (AP STA) sending frames to a tag shall be able to uniquely identify the tag using the MA-UNITDATA parameters
It means that the Tag shall have unique MAC address
Note that the 802.11 data link layer is designed to allow a station to support various higher layer protocols. Such as TCP/IP, DHCP, ARP. This in turn increases the size of the MSDU, for example an IPV6 address is 128 bits long. Processing these protocols may require a significant amount of RAM.
Using a unique MAC address for Tags may compromise privacy because the tag inventory is visible to any observer.
Fulfilling these requirements may require a significant increase in the energy consumed by the AMP tag, which in turn will greatly reduce its range of action.
Option 1 cannot be implemented by AMP-only IoT devices

## Slide 13: References
11-23-0436-00-0amp-technical-report-on-support-of-amp-iot-devices-in-wlan
11-23-1005-00-0amp-discussion-on-requirements-for-amp-use-cases
ISO/IEC 18000-63:2021(E)
IEEE P802.11-REVme/D6.0, June 2024

## Slide 14: Straw Poll
SP#1
Do you agree that 802.11bp shall define Option 2 Internetworking reference model?
Yes
No
Abstain

## Slide 15: Backup

## Slide 16: AMP-only IoT device vs AMP-assisted IoT device
“In the first category of use cases, such as logistics/warehouse and smart home, object identification is one of the main functionalities provided by the AMP IoT devices. The essential information transmitted to the AP reader is the ID of the devices/tags that requires low peak data rate only (e.g., less than 100kbps). Since the devices/tags should be attached to all the objects within the service area, huge amount of such devices/tags is needed. In this regard, manual operation of the devices/tags is extremely difficult and simple maintenance or even maintenance-free feature is necessary. In some of the use cases requiring environmental monitoring and sensor data reporting, such as smart manufacturing, smart home, etc., only small packet (e.g., less than 200 bits) and infrequent sensor data reporting (e.g., one packet per minute) are needed, e.g., temperature sensing and reporting.
In these use cases, the devices/tags should have the features such as ultra-low complexity, ultra-low power consumption, very small form factor and battery-less (i.e., not using conventional battery). This device type is defined as AMP-only IoT device.” [1]

## Slide 17
Requirements [2]
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases |  |  |  |  |  |  | 

## Slide 18: AMP-only IoT device vs AMP-assisted IoT device (cont.)
“An AMP-assisted IoT device may be similar to a legacy 802.11 (e.g., 802.11n/11ah) device, it can reuse the current PHY design but with enhanced MAC features to adapt to operation with a specific kind of ambient power. Since the ambient power is very limited and sometimes unstable and uncontrollable, the enhanced power saving and power management can be adapted for the unstable and uncontrollable ambient power.” [1]

## Slide 19: RF powered AMP only IOT device
“Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc” [2]
“The main advantage of RF-based energy harvesting is its availability in indoor environments and the fact that RF power is controllable (e.g., power can be sent by a transmitter on demand or periodically). Potential applications include logistics/warehouse, manufacturing, smart homes, health monitoring, and environmental monitoring etc.” [1]

## Slide 20: Figure 7-1 Expectation of AMP-IoT [1]

## Slide 21: ISO/IEC ISO/IEC Standards