## Slide 1: Capability report and ID allocation for AMP STA
Date: 2024-07-08
Authors:

## Slide 2: Background
As stated in the 802.11bp PAR[1], 11bp amendment defines mechanisms for the coexistence of an AMP STA and deployed STAs in the same frequency.
There are couple of contributions [2] - [4] discussed the different PHY capabilities of AMP STAs.
In [5], different scenarios with or without associations are mentioned when discussing the MAC design of AMP.
Considering the implementation of relay, both AP(soft AP) and non-AP STA can serve as readers

## Slide 3: Abstract
In this contribution, we discuss the necessity of AMP capability reporting and the method of ID allocation for AMP STAs with storage capacity
- which allows the reader to learn about the AMP STA’s existence and capabilities
- which is beneficial for achieving grouping access and access restrictions in IoT scenarios with large-scale devices
Notes: 目前还没有统一的功能实体命名

## Slide 4: Recap-Fast Authentication and Association in 11ah
In Centralized Authentication Control (CAC), the AP dynamically changes the portion of stations that are allowed to send AuthReq messages.
- a CAC AP sets a threshold and broadcasts it to all stations, and a CAC STA shall generate a random value from the interval [0, 1022], and tries to send an AuthReq to the AP if the random value is smaller than the threshold obtained from the received beacon.
In Distributed Authentication Control (DAC), a beacon interval is divided into sub-intervals called Authentication Control Slots (ACSs).
- Stations randomly select a beacon interval and a ACS to send their AuthReq.
Notes: A station sends the AP an authentication request and association request which allows the AP to learn about the station’s existence and capabilities. By sending back an authentication response and association response to the station, the AP informs the station of the network parameters and assigns it an identifier, referred to as an AID.

## Slide 5: The necessity of capability reporting
During the study group stage, we discussed AMP-only devices and AMP- assisted devices based on different use cases[6]
AMP-assisted devices tend to achieve compatibility and coexistence with legacy STAs, and further reduce power consumption through environmental energy harvesting, while AMP-only devices may have active transmitters or just transmit through backscatter
There should be different channel access methods for different AMP STAs, and the reader should obtain the capability information of the AMP STA before initiating scheduling

## Slide 6: AMP STA capability report
The Reader broadcasts trigger frame to initiate the capability collection, indicating the protection window
AMP STAs send response frame with capability fields or element to report its device capability information
- The content of capability information needs further discussion
- Further discussion is needed on the channel access methods for the response frame, such as TDMA, FDMA, etc
For AMP STAs which are unable to initiate transmission through EDCA, the AMP STA capability collection should be initiated by the reader.
Based on capability reporting, the reader can further assign IDs to AMP STAs which can store the ID for grouping or allocation of transmission resources. AMP STAs which can obtain transmission opportunities on their own can follow the existing association way.

## Slide 7: AP as reader-ID allocation method a
AP broadcasts trigger frame to initiate capability collection, indicating the protection window
- AMP STA do not need to send request frame through EDCA
AMP STAs send response frame with its capabilities
AP assigns an ID to the AMP STA that successfully sent a response frame, like AID in 11ah
Within the protection window, the reader can repeatedly send trigger frames, and the AMP STA received the ID does not need to respond to subsequent trigger frames
Notes: 11ah AID：page、block、sub-block。。。。。

## Slide 8: AP as reader-ID allocation method b
AP broadcasts trigger frame to initiate capability collection, and AMP STA send response frame like method a.
Unlike method a, AP does not need to assign an ID immediately after receiving feedback from AMP STA, and shall send an ack to it
-the AMP STA received ack will not intend to respond again subsequent trigger frames
After multiple triggers, the AP can uniformly allocate IDs
For both method a and b, if no feedback is received after multiple triggers, AP could terminate the protection window in advance
Notes: AMP STA is likely unable to initiate association requests through EDCA, and the ID allocation process should be initiated by the reader to indicate the protection window for AMP STAs and legacy STAs

## Slide 9: non-AP STA as reader-ID allocation method c
Capability collection can be initiated by the reader or AP
The reader sends identification triggers to collect feedback from AMP STAs, similar to method b
The reader reports the information of AMP STA to the AP.
AP assigns IDs and forwards them to AMP STAs through a reader
Based on MLO, the link between AP and reader does not have to be in the 2.4G or S1G frequency band
Notes: Considering the implementation of relay, both AP and non-AP STA can serve as readers

## Slide 10: Summary
We discussed the necessity and methods of AMP STAs reporting capability to the reader
Based on the capability report, we proposed several methods for ID allocation of AMP STAs, which helps readers obtain the capability information of AMP STAs and perform group access or access restrictions, thereby reducing conflicts caused by large-scale device access.
We plan to further discuss the channel access schemes based on different AMP STAs’ capabilities and corresponding MAC frame formats in the future

## Slide 11: SP1
Do you agree that AMP STAs should report device capability information to readers
Note: The detailed capability information is TBD.
Y/N/A

## Slide 12: SP2
Do you agree to assign an ID to the AMP STA that can support storing parameters assigned by the reader
Note: The detailed ID allocation process and related frame formats are TBD.
Y/N/A

## Slide 13: References
[1] 11-24-0575-01-0amp-p802-11bp-par
[2] 11-24-0849-00-00bp-harmonization-of-waveform
[3] 11-24-0867-00-00bp-thoughts-and-questions-on-amp-phy
[4] 11-24-0853-00-00bp-design-target-and-device-capabilities-for-amp-iot
[5] 11-24-0872-00-00bp-mac-aspects-for-amp
[6] 11-23-2203-01-0amp-updated-technical-report-on-support-of-amp-iot-devices-in-wlan