## Slide 1: Follow Up on Transmission Modes
Date: 2024-07-18
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-24/1200r1
July 2024

## Slide 2: Abstract
In this contribution, we recap the harmonized waveform design and transmission modes discussed so far for different scenarios of AMP and discuss the feasibility and benefits of active UL transmission.
Doc.: IEEE 802.11-24/1200r1

## Slide 3
Recap: Multiple Solutions [1]
  Four solutions have been proposed and discussed so far
    Solution 1: active transmission;
    Solution 2: close range backscatter with full duplex;
    Solution 3: long range backscatter with bi-static;
    Solution 4: legacy 802.11 devices enhanced with AMP features, e.g., extremely low power consumption, energy harvesting capability, etc.
  Clearly, harmonization is needed
    Different solutions may diverge vastly in PHY and MAC design.
    Harmonization needs to start from basic design, e.g., waveform.
    Objective: optimal design for all solutions but may not be optimal design for each individual solution, thus compromise needed
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1200r1
July 2024

## Slide 4
Recap: Waveform Types [1]
  Different waveforms have been proposed and discussed so far as in the below table
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1200r1
July 2024
 | DL comm. | UL data | WPT | CW
S1: Active | MC-OOK (AP) | OOK/PSK/FSK/DSSS (AMP) | TBD (energizer) | 
S2: Backscatter (close range) | TBD (AP/M) | OOK (AMP) | Pulse/OFDM (AP/M) | Pulse/OFDM (AP/M)
S3: Backscatter (long range) | MC-OOK (AP) | OOK/PSK/FSK/DSSS (AMP) | TBD (energizer) | TBD (assistant node)
S4: Legacy enhanced | MC-OOK (AP) |  | TBD (energizer) | 

## Slide 5
Solution 1: Active UL Tx
  Feasibility of active UL Tx
    During TIG many contributions [2] have shown that low complexity, low cost and low power consumption can be achieved
    Multiple prototypes with already shown in the past meetings
  Benefits of active UL Tx
    Simple design with legacy protocols as a starting point
    No significant changes in PHY design, thus simple implementation within existing and new products and limited specification efforts are expected
  Technical requirements for active UL Tx
    Extremely low complexity and power consumption  no crystal, higher clock offset, e.g., ±1000ppm [3]
    Depending on harvested energy  less than 1 mW power consumption [2]
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1200r1
July 2024

## Slide 6
Summary
  In this submission, the harmonization of waveform issues is recapped and feasibility and benefits of active UL Tx are presented.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1200r1
July 2024

## Slide 7: Reference
[1] 11-24/0849, Harmonization of Waveform.
[2] 11-23/2203, Technical Report on support of AMP IoT devices in WLAN.
[3] 11-23/1140, Considerations for AMP Devices
Doc.: IEEE 802.11-24/1200r1
July 2024

## Slide 8: SP
Doc.: IEEE 802.11-24/1200r1
July 2024
Do you agree that 11bp defines at least one mode of MAC/PHY that allows an AMP device with active uplink communication in 2.4GHz with the following technical requirements?
  Maximum clock offset of ± 1000ppm