## Slide 1: NPCA – Next level discussions
Date: 2024-07-12
Authors:

## Slide 2: Recap
Non-Primary Channel Access (NPCA) will allow UHR STAs to access the nonprimary channel when the primary channel is Busy due to OBSS traffic
TGbn has agreed to the following:
  TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
    The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
    A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.

## Slide 3: Introduction
When an OBSS transmission is detected on the BSS primary, NPCA STAs will switch to the NPCA Primary channel and will contend to initiate a TXOP
To ensure coordinated operation on the NPCA Primary, the following details must be specified:
  When can an NPCA transmitter initiate a TXOP after switching?
  How does the transmitter contend on the NPCA Primary channel?
  Are there ways to improve coordination between two peer NPCA STAs?
In this contribution, we provide the details on the above aspects of NPCA

## Slide 4: Switching delay
A switch from the Primary channel to the NPCA Primary channel will incur a delay
  Refer to this as the NPCA Switching delay
Similarly, a switch from the NPCA Primary channel to the BSS Primary channel will also incur a delay
  Refer to this as the NPCA Switch back delay
The spec must allow the NPCA STAs to signal these delays to its peer
  As an example, AP announces in Management frames and non-AP STAs announces during NPCA mode enablement
Each NPCA STA must honor the switching delay of its peer when initiating a TXOP on the NPCA Primary channel
  Which implies that after switching, the NPCA transmitter shall not transmit a frame to the NPCA receiver until the receiver’s NPCA Switching delay has elapsed since a reference switch time (which must also be defined)

## Slide 5: Contention on NPCA Primary channel
Two successive TXOPs on the NPCA Primary channel may be separated by large gaps
During this time, NPCA STAs
  Will not contend on the NPCA Primary channel
  Will generally be unaware of OBSS activity (if any) on the NPCA Primary channel
Thus, maintaining contention parameters on the NPCA Primary channel in the same manner as BSS Primary channel is not required
For simplicity, we propose:
  NPCA STAs do not need to maintain a separate CW and backoff counter for the NPCA Primary
    Which would require the STA to remember these parameters across contentions on the NPCA Primary channel
  Instead, every time the NPCA STA switches to the NPCA Primary channel, it sets the CW to a certain value and picks a new backoff counter value

## Slide 6: Improving coordination in NPCA
There can be loss of coordination between the NPCA AP & NPCA non-AP STA if both AP and non-AP STA contend and transmit
  For example, due to hidden node or the asymmetric view problem among other issues
  Hidden node problem: When one peer observes OBSS but other does not
    If AP does not observe OBSS, client’s EDCA transmission would be wasted
    If client does not observe OBSS, TXOP is still successful as long as one NPCA STA responds to the AP
  Asymmetric view: When NPCA AP and non-AP STA observe different OBSS PPDU/TXOP
    The duration for which BSS Primary channel is Busy is different at the two NPCA peers (see adjoining figure)
    Client’s EDCA transmission might initiate TXOP for a duration longer than what is Busy at the AP
      Causing AP to become unavailable on the BSS Primary channel for a portion of time

## Slide 7: Improving coordination in NPCA
Proposal: Define a mode under NPCA where NPCA non-AP STAs do not use untriggered UL transmissions
In both problems discussed in the previous slide, it is the AP’s view that matters
  If AP is performing frame exchanges on NPCA Primary channel beyond how long its BSS Primary channel is Busy, legacy non-AP STA can have a performance impact
  Therefore, it is more efficient for the AP to initiate TXOP as per what it observes on the BSS Primary channel
Enabling a mode where NPCA non-AP STAs do not use untriggered UL transmissions may lower cases of coordination loss between NPCA peers

## Slide 8: Summary
NPCA can improve spectral utilization by utilizing unused secondary channels when the primary channel is Busy
However, switching and transmissions on the NPCA Primary channel must be coordinated to maximize these gains
In this contribution we presented details on the following aspects:
  When is the earliest that an NPCA transmitter can initiate a TXOP after switching
  How the transmitter contends on the NPCA Primary channel
  How a trigger-only mode under NPCA improves coordination between peer NPCA STAs

## Slide 9: Straw Polls
Do you agree that an NPCA STA shall indicate the following to its peer NPCA STA?
  NPCA switching delay
    time it needs to switch from the BSS Primary channel to the NPCA Primary channel
  NPCA switch back delay
    time it needs to switch from the NPCA Primary channel to the BSS Primary channel

## Slide 10: Straw Polls
Do you agree that an NPCA STA shall initiate a TXOP on the NPCA Primary channel following the rules defined in 10.23.2.2 (EDCA backoff procedure) and 10.23.2.4 (Obtaining an EDCA TXOP) with the following exception:
  Every time the STA switches to the NPCA Primary channel, it shall initialize CW_NPCA[AC] to TBD value and pick a new backoff counter (BO_NPCA) randomly between 0 and CW_NPCA[AC]. QSRC_NPCA[AC] shall be set to 0.
  NOTE – Baseline EDCA procedure is followed on the BSS Primary channel. The values of CW_NPCA and BO_NPCA are discarded by the NPCA STA when it switches back to the BSS Primary channel.

## Slide 11: Straw Polls
Do you agree to define a mode of operation in NPCA where the NPCA non-AP does not use untriggered UL transmissions on the NPCA primary channel
  This mode can be enabled/disabled by the AP
  Whether the mode is for all associated non-APs or per non-AP is TBD
  TBD whether MU EDCA parameters mechanism is used for this or not

## Slide 12: References
[1] M. Park, et al., “11-24/0495r0: Non-Primary Channel Access (NPCA) – Follow Up”