## Slide 1: Initial Control Frames in C-TDMA
Authors:
Date: 2024-xx-xx
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Duncan Ho |  |  |  | 
Giovanni Chisci |  |  |  | 
Sherief Helwa |  |  |  | 

## Slide 2: Introduction
C-TDMA allows an AP that owns a TXOP to share portion of the TXOP time with one or more APs
  The scheme is meant to improve latency and reduce contention/collisions
An initial Control frame (ICF) helps in efficient C-TDMA operation
  ICF at the start of the TXOP allows the sharing AP to:
    Announce intent to share the TXOP
    Poll candidate APs to assess if, and with whom, to share TXOP
    Provide critical C-TDMA information
Selection of ICF would mainly depend on:
  AP capabilities for responding (TB/non-TB PPDU)
  Number of APs to be polled (SU/MU transmissions)
  Signaling needs for C-TDMA information
This contribution focuses on the aspect of AP’s capability to respond to an ICF
  Discusses two options for the ICF as MU-RTS and BSRP Trigger frames

## Slide 3: C-TDMA Frame Exchange Sequence
The sharing AP polls candidate shared APs via ICF
  The ICF serves as a polling/announcement frame
The sharing AP triggers TXOP sharing via TXOP Allocation frame
The shared AP returns unused TXOP (if any) via TXOP Return frame
*Polling of in-BSS STAs of the sharing AP is optional
ICF

## Slide 4: Details of ICF in C-TDMA
The sharing AP sends an ICF at the start of the TXOP to:
  Announce its intent to share a part of its TXOP
  Poll candidate AP(s) to check their interest in participation
  Optionally, poll its in-BSS STA(s)
The ICF may specify traffic priority for the shared TXOP, such as:
  AC, SCSID, TID of the traffic
A response from a polled AP may indicate:
  Its intent to participate in C-TDMA
  Relevant information about its traffic
The ICF helps shared AP(s) make scheduling decisions:
  whether to participate in sharing during the current TXOP
    A shared AP will not participate if it has no traffic for the indicated traffic type
  If participating, the AP identifies suitable client(s) to serve during the shared TXOP

## Slide 5: Options for ICF in C-TDMA
There are two leading candidates for ICF in C-TDMA:
  MU-RTS Trigger frame
  BSRP Trigger frame
    Baseline requires a response in a Trigger based (TB) PPDU
In this contribution, we assess these two options of the ICF from the aspect of AP’s capability to respond to an ICF in a TB PPDU

## Slide 6: MU-RTS Trigger Frame
In baseline, the response to the MU-RTS Trigger frame is a CTS sent in a non-TB PPDU
Appropriate to use the MU-RTS Trigger frame as an ICF in C-TDMA if the candidate shared AP cannot respond in a TB PPDU
Additional considerations:
  Polling multiple candidate shared APs using an MU-RTS Trigger frame could be problematic:
    CTS responses from multiple shared APs would be identical
    It would be impossible for the sharing AP to determine which AP has responded and which has not
    The problem could be worse if the same MU-RTS frame is used to poll in-BSS STAs of the sharing AP, e.g., in eMLSR
  Only one candidate shared AP may be polled unambiguously
    In case of single AP polling, if there is no CTS response, the sharing AP may need to back off and lose the TXOP

## Slide 7: BSRP Trigger Frame
The response to the BSRP Trigger frame from a polled AP needs to be in a TB PPDU
  Needs a mechanism for an AP to indicate its capability to respond in a TB PPDU
Appropriate to use the BSRP Trigger frame as an ICF in C-TDMA if a candidate shared AP supports responding in a TB PPDU
Additional considerations:
  The BSRP Trigger frame can poll one or more candidate shared APs and optionally one or more its associated STAs unambiguously
  Each responder is assigned a distinct resource unit (RU), thus allowing the sharing AP to unambiguously identify who responded and who did not
  Can be used to receive a richer response, e.g., BSR

## Slide 8: Summary
Use BSRP Trigger frame as an ICF in C-TDMA if:
  A candidate shared AP supports responding in a TB PPDU
    Needs to provide a mechanism for an AP to indicate its capability to respond in a TB PPDU
Use MU-RTS Trigger frame as an ICF in C-TDMA if:
  A candidate shared AP does NOT support responding in a TB PPDU
Allowing both BSRP and MU-RTS Trigger frames as ICF in C-TDMA would not require defining new formats or adding exceptions to the spec
  eMLSR already allows both ICF options

## Slide 9: SP1
Do you agree that a UHR AP shall indicate to another AP its capability to respond in a TB PPDU or not?

## Slide 10: SP2
Do you agree that, as part of the C-TDMA procedure, a sharing AP may solicit a poll response in a TB PPDU from another AP only if the other AP has indicated support for responding via a TB PPDU?

## Slide 11: SP3
Do you agree that, as part of the CTDMA procedure, a candidate AP that is polled by the sharing AP shall provide, via a response,
  Its intention not to participate in TXOP sharing during the current TXOP.
  Its intention to participate in TXOP sharing during the current TXOP.
  Signaling details (including traffic indication) are TBD.

## Slide 12: References
[1] Abhishek Patil and et al. , “C-TDMA Frame Sequence,” 23/1895r1, Jan 2024.
[2] Yanjun Sun and et al., “Considerations on Coordinated TDMA (C-TDMA),” 23/0041r0, Jan 2023.
[3] Dibakar Das and et al. , “C-TDMA procedure in UHR,” 23/0261r0, Apr 2023.
[4] Yanjun Sun and et al., “Follow-up on Coordinated TDMA (C-TDMA),” 23/0739r1, Jul 2023.
[5] Si-Chan Noh and et al., “Considerations on Return TXOP between multiple APs,” 23/1327r0, Aug 2023.
[6] Liwen Chu and etc al., “Extended TXOP sharing,” 23/249r1, May 2023.
[7] George Cherian and et al., “Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be,” 19/1582r2, Nov 2019.
[8] Dibakar Das and et al., “C-TDMA Follow-up,” 23/93r2, Mar. 2024.
[9] Geonhwan Kim and et al., “TXOP Protection in C-TDMA,” 24/227r1, Apr. 2024.
[10] Geonhwan Kim and et al., “TXOP Return in C-TDMA,” 24/411r0, Apr. 2024.
[11] Geonhwan Kim and et al., “Coordinated TDMA (Follow up),” 23/1910r1, Nov. 2023.
[12] Si-Chan Noh and et al., “NAV protection for C-TDMA,” 24/375r0, Feb. 2024.
[13] Sanket Kalamkar and et al., “NAV Rule in C-TDMA,” 24/423r0, May 2024.