## Slide 1: Some usage of intermediate FCS
Date: 2024-07-12
Authors:

## Slide 2: Non-AP STA and non-AP MLD power save
In order to improve power saving during listen operation of non-AP STAs, we have agreed in 11bn to be able to include an intermediate FCS field before padding in initial control frames
For eMLSR, this allows to operate in listen mode only on 20MHz, terminate reception of the ICF after the intermediate FCS and use the padding and following SIFS to reconfigure the PHY to tune to the TxOP BW, perform CCA check, …
In order to make such power save be available to other STAs/MLDs, we have also agreed to define a generic Dynamic Power Save (DPS) mechanism that allows to transition from a low capability mode to a high capability mode thanks to the ICF-ICR exchange

## Slide 3: Reminder: eMLSR and DPS Listen mode power consumption reduction
STAs can stay for a long time in listen mode and should consume as little power as possible
With eMLSR, STAs can already only enable reception
  of some low MCSs
  of a single NSS with a single antenna
Current gap is to be able to only enable reception on 20MHz instead of the STA’s operating BW, which would provide significant power gains
  This is theoretically possible with eMLSR, but there’s currently no time after the ICF to reconfigure the radio to a larger bandwidth and to check CCA on the TxOP BW before responding with CTS
ICF (e.g. MU-RTS)
TxOP owner
AP
TxOP responder
STA
SIFS
ICF response (e.g. CTS)
20MHz operation: listen mode
80MHz operation: power mode
Data
Transition from 20 to 80MHz
Check CCA

## Slide 4: Proposal
We need to give more time for the STA to be able to change BW so that it can check CCA during SIFS between ICF and ICF response
One could thing we can use padding, but actually the padding is included before the FCS in non-HT dup (which has to be used in that case), which forces the STA to wait until the end of the ICF PPDU before being able to switch
New Intermediate FCS field, inserted before the padding allows the STA to use the padding time to change BW and use SIFS to check CCA on TxOP BW.
Frame control
Duration
RA
TA
Common info
User info
STA1
User info
STA2
Intermediate FCS
Padding User Info
…
Padding User Info
Transition from 20 to 80MHz
20MHz operation: listen mode
80MHz operation: power mode
FCS
FCS calculated on whole data portion up to FCS2 User Info field

## Slide 5: Next step
One easy and straightforward follow-up step is to:
  validate that the intermediate FCS field will be used and included in the ICF for eMLSR UHR STAs and for DPS
  Set the requirement that the field that carries the Intermediate FCS shall be designed to be ignored by legacy STAs if they are scheduled in the same eMLSR initial control frame
Note that the intermediate FCS can be used for other UHR mechanisms

## Slide 6: Padding for DPS
For eMLSR, we already have built-in the tools for an eMLSR non-AP MLD to indicate the amount of padding it needs in a received initial control frame
For DPS, we also need the same tool

## Slide 7: Straw poll #1
Do you agree to add the following to the 11bn SFD:
if a UHR non-AP MLD operates in the eMLSR mode, then its associated AP MLD, that supports transmitting intermediate FCS, shall include an intermediate FCS, if needed by the non-AP MLD, in every Initial Control Frames for eMLSR transmitted to the non-AP MLD through its affiliated APs on the eMLSR links?
  Mandatory/optional support for transmitting intermediate FCS is TBD
  The field that carries the Intermediate FCS shall be designed to be ignored by legacy STAs if they are scheduled in the same initial control frame
  Note: intermediate FCS may not be needed, for instance, if the STA requires no padding. It is TBD whether an intermediate FCS can be avoided if a MIC is present.

## Slide 8: Straw poll #2
Do you agree to add the following to the 11bn SFD:
if a UHR STA (UHR non-AP STA or UHR Mobile AP) operates with the power save mode where the STA transitions from a lower capability mode to a higher capability mode upon reception of an initial control frame (that we call here DPS), then its associated peer STA, that supports transmitting intermediate FCS, shall include an intermediate FCS, if needed by the STA, in the initial control frame that it transmits to the STA.
  Mandatory/optional support for transmitting intermediate FCS is TBD
  Note: intermediate FCS may not be needed, for instance, if the STA requires no padding. It is TBD whether an intermediate FCS can be avoided if a MIC is present.

## Slide 9: Straw poll #3
Do you agree to add the following to the 11bn SFD:
a UHR STA that uses the power save mode to transition from lower capability (LC) mode to higher capability (HC) mode, advertises the amount of padding it needs in a received initial control frame?
  Padding values range between 0 and 256 us with a TBD resolution