## Slide 1: AMP Tag Requirements for Close-range Mono-Static Backscattering
Date: 2024-09-09
Authors:

## Slide 2: Introduction
The clock characteristics of different AMP tags have been discussed and compared [3]
Close-range mono-static backscattering mode was agreed as an important use case for AMP [1]
In this presentation, more aspects of capability of mono-static backscattering AMP tags and the requirements to the standards definition are further discussed.

## Slide 3: Recap: Mono-static Backscattering Tag [1]
AMP + UHF: one tag for both B2B and B2C applications
  B2B: sub-1GHz backscattering with ~10m range
  B2C: 2.4GHz backscattering with ~10cm range
AMP mono-static backscattering tag should share common or similar RF/hardware requirements
900MHz + 2.4GHz
Antenna
Z_ant
Modulator
AMP
Logic
Memory
RFID
Logic

## Slide 4: UHF RFID Tag Requirements
EPC UHF Gen 2 standards [2] define the requirements for downlink/uplink communication with UHF RFID tags.
  Facilitates low-power and low cost deign
The requirements are specified in several aspects:
  Clock characteristics:
    The reference clock frequency tolerance: less than +/- 10%  100,000ppm
    The reference clock jitter max. 1%
  Data rate: max DL 160kbps and UL 640kbps
    Max operating clock is ~2MHz
  Hardware wakeup settling time: max 1.5ms
  No energy operation time is ~100us  small cap for energy storage
  Passive reflection with no mixer  no or limited frequency shift

## Slide 5: AMP Tag Requirement (1)
AMP Tag share similar hardware limitation
  Small energy cap
  Long wakeup settling time
  Clock characteristics
  No mixer and phase information
Design requirement: Waveform/PPDU
  Every read event (TXOP) starts with a wakeup waveform of ~1ms
  One read transaction needs to be finished within one PPDU or TXOP
    read transaction meaning either tag status query or data reading

## Slide 6: AMP Tag Requirement (2)
Design requirement: modulation
  OOK modulation only
  OOK bit encoding supports per-bit/symbol synchronization
    Both DL Data and UL backscattering
    e.g. PIE, FM0 or (differential) Manchester coding
  Clear indication of start of DL or UL segments
    Cannot rely on clock count for scheduled/polled events
  Not sensitive to excitation/energizer signal bandwidth
Design requirement: data rate
  DL Rx rate is 250kbps max
  UL backscattering data rate is 1Mbps max

## Slide 7: Summary
More detailed discussion of the requirement of UHF tag
  Clock characteristic, energy cap, wakeup settling, no mixer
Discuss about the implied design requirement of AMP tag
  Wakeup time for each read event
  Amplitude modulation only
  Bit-level synchronization
  Maximum data rate for both DL and UL
Other low-cost low-power AMP tags may share similar characteristics/requirements.

## Slide 8: References
[1] 11-23/2038, Close Range AMP Backscattering in 2.4GHz
[2] EPC UHF Gen2 Air Interface Protocol | GS1
[3] 11-24/1475, Discussion on ultra-low power timing clock

## Slide 9: SP
Do you agree that 11bp defines at least one data rate of at most 250kbps for DL transmission?