## Slide 1: 100 MHz PPDU
Date: 2024-07-08
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 
Wei Ruan |  |  |  | 

## Slide 2: Motivation for 100 MHz PPDU
6 GHz is popular world wide, whilst it is also worth to look into 5 GHz. A typical 5GHz spectrum is as follows.
In different regions, the available 5 GHz spectrum is different. Below is one example:

## Slide 3: Motivation for 100 MHz PPDU
With the existing 5GHz spectrum, the goal is to further increase the data rate compared with 802.11ax and 802.11be. One way would be to include 100 MHz transmission between 5735 MHz and 5835 MHz.
100 MHz increases the channel width by 25% compared with 80 MHz. Also, it is difficult or not efficient to use standalone 20 MHz by one BSS.

## Slide 4: 100 MHz OFDMA transmission
With OFDMA, 100 MHz transmission can be easily achieved without introducing new RU or MRU.
The existing RU(s) or MRU(s) within an 80 MHz channel can be combined with existing RU(s) or MRU(s) within an 20 MHz channel. Preamble puncturing can be further applied within the 80 MHz channel.
For PPDU Bandwidth, can reuse 160 MHz or introduce new 100 MHz.
DC can be in the center of 80 MHz channel or between the 484-tone RU and 242-tone RU.

## Slide 5: 100 MHz non-OFDMA transmission
For non-OFDMA, to support 100 MHz full bandwidth transmission, a new MRU type 996+242-tone MRU is needed.
Preamble puncturing may be further applied, but need furthers study.
PPDU bandwidth and DC positions can follow OFDMA case.

## Slide 6: Summary
In this contribution, 100 MHz transmission is introduced to maximize the data rate of 802.11bn in some region, compared with 802.11ax and 802.11be.

## Slide 7: Straw Poll #1
Do you agree to include the following into the 11bn SFD?
  11bn supports 100 MHz transmission from 5735 MHz to 5835 MHz.
    100 MHz transmission could be applied to certain TBD operating class
    Y
    N
    A

## Slide 8
IEEE Std 802.11axTM-2021
Draft P802.11be D6.0
References