## Slide 1: Further Considerations on NPCA
Date: 2024-09-01
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
IEEE 802.11bn task group has agreed to define NPCA operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions
There are several issues needed to be addressed for NPCA operation, such as ：
power consumption issue for STAs supporting NPCA,
blindness issue for STAs that switch to the NPCA primary channel, and
non-synchronized channel switches for different STAs.
This contribution analyzes the key issues for NPCA operation, and proposes candidate solutions for NPCA operation to be considered.

## Slide 3: Issue 1 - Power Consumption
Power consumption issue for STAs supporting NPCA
AP can only exchange frames with one or several STAs on NPCA primary channel at a TXOP level. For STAs that switch to NPCA primary channel but cannot become a TXOP holder or TXOP responder, their switches may be inefficient.
If unscheduled/uncontrolled and frequent switches between primary channel and NPCA primary channel happen to STAs, they may consume/waste a lot of power due to inefficient switches.
AP1
AP2
STA2-1
STA2-2
Figure. An example for the issues
STA1-1
Switch to NPCA primary channel
AP2, STA2-1, STA2-2，STA2-2 switch to NPCA primary channel due to OBSS traffic between AP1 and STA1-1
AP2 obtains a TXOP on NPCA primary channel and initiate frame exchange with STA2-2.
Although STA2-1 and STA2-3 switch to NPCA primary channel, their switches are inefficient as they cannot become a TXOP holder or TXOP responder.
STA2-3

## Slide 4: Issue 2 – Lost medium synchronization
Blindness issue for STAs that switch to the NPCA primary channel.
If AP/non-AP STA operating on their operating channel cannot perform CCA on its NPCA primary channel at the same time, when it switches to the NPCA primary channel it would loose medium synchronization on the NPCA primary channel.
Especially when both AP and non-AP STA loose medium synchronization, it is difficult to handle this issue, which may result in collision for channel access.
11be has specified medium access recovery procedure to address blindness issue in NSTR link pair case, which can be used a reference.
But the assumption of this mechanism is that AP doesn’t loose its medium synchronization.

## Slide 5: Issue 3 - non-synchronized channel switches
non-synchronized channel switches for different STAs.
For AP and non-AP STA, there is a case where the AP(or non-AP STA ) switches to the NPCA primary channel while the non-AP STA(or AP) does not switch to the NPCA primary channel, resulting in an non-synchronous channel switch for AP and non-AP STA
AP1
AP2
STA2-1
STA2-2
STA2-3
Figure. An example for the issues
STA1-1
Switch to NPCA primary channel
AP2, STA2-1, STA2-2 switches to NPCA primary channel due to OBSS traffic between AP1 and STA1-1
If AP2 obtains a TXOP on NPCA primary channel and intend to initiate frame exchange with STA2-3, STA2-3 cannot response as it has not switched to NPCA primary channel.

## Slide 6: Candidate Solution for Issue 1
Propose to provide a mechanism to manage STAs’ NPCA availability and unavailability
A STA can indicate its NPCA availability/unavailability to the associated AP
NPCA availability: the STA would switch to NPCA primary channel if the condition is met.
NPCA unavailability: the STA may not switch to NPCA primary channel even if the condition is met. The associated AP should not initiate frame exchange with it on NPCA primary channel.
The management of NPCA availability and unavailability is mainly applied for STAs in active mode.
AP can also schedule the NPCA availability and unavailability of its associated STAs supporting NPCA

## Slide 7: Candidate Solution for Issues 2 & 3
A assisting link is introduced to address blindness issue and non-synchronized channel switch issue:
Link1: supports NPCA operation
Link2 (assisting link): assist Link1 to listen on the NPCA primary channel and do CCA operation ,and receive ICF if required
Targets: 1. to ensure that AP1 doesn’t loose medium synchronization on NPCA primary channel; 2. AP1 can receive ICF even it has not switched to the NPCA primary channel
An example: non-AP MLD set up only one link(i.e. Link1) with AP MLD

## Slide 8: Summary
There are several issues needed to be addressed for NPCA operation, such as ：
power consumption/save issue for STAs supporting NPCA,
blindness issue for STAs that switch to the NPCA primary channel, and
non-synchronized channel switches for different STAs.
This contribution analyzes the key issues for NPCA operation, and proposes candidate solutions for NPCA to be considered
Propose to provide a mechanism to manage STAs’ NPCA availability and unavailability
A assisting link is introduced to address blindness issue and non-synchronized channel switch issue

## Slide 9: References
[1] UHR proposed PAR, https://mentor.ieee.org/802.11/dcn/23/11-23-0480-01-0uhr-uhr-proposed-par.pdf
[2] Draft P802.11be_D7.0
[3] non-primary channel access (NPCA) - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0495-00-00bn-non-primary-channel-access-npca-follow-up.pptx
[4] Non-primary channel access (NPCA), https://mentor.ieee.org/802.11/dcn/23/11-23-2005-01-00bn-non-primary-channel-access-npca.pptx
[5] Robust Secondary Channel Access, https://mentor.ieee.org/802.11/dcn/24/11-24-0318-00-00bn-robust-secondary-channel-access.pptx

## Slide 10: SP 1
SP : Do you support to specify a mechanism to manage the NPCA availability and unavailability of STAs supporting NPCA operation in 11bn?
The mechanism is TBD

## Slide 11: SP 2
SP : Do you support to specify a mechanism to address the blindness issue for STAs that switch to its NPCA primary channel and/or non-synchronized switches from primary channel to NPCA primary channel for STA and its peer STA(s) in 11bn?
The mechanism is TBD
Liuming Lu (OPPO)